## Slide 1: Proposed EVB TLV v2
March 4, 2010

## Slide 2: Contributing Authors
Company | Contacts
BNT | Daya Kamath
BNT | Jay Kidambi
BNT | Vijoy Pandey
Broadcom | Uri Elzur
Brocade | Anoop Ghanwani
Emulex | Chait Tumuluri
HP | Paul Bottroff
HP | Paul Congdon
HP | Chuck Hudson
HP | Michael Krause
IBM | Vivek Kashyap
IBM | Renato Recio
IBM | Rakesh Sharma
Juniper | Srikanth Kilaru
QLogic | Manoj Wadekar

## Slide 3: Summary of Proposed EVB TLV
Advertise a station or bridge’s EVB functional and resource capabilities
Activate common functional capabilities
Reduce resource capabilities to a maximum common value

## Slide 4: Proposed EVB TLV (1)
Transport: LLDP
EVB Capabilities -- Describes EVB capabilities that can be supported by the sender. Includes port forwarding modes and other capabilities.
EVB Current Configuration – Identifies the EVB capabilities that are currently enabled by the sender. (Only one port forwarding mode may be selected)
  Forwarding Mode
    Standard 802.1Q forwarding
    Reflective Relay
  Capabilities Bits
    VSI Discovery Protocol (VDP)
    802.1X Authentication Required
    T3PR Supported
    RTE (Retransmission Timer Exponent)
TLV header
TLV type = 127 (7 bits)
TLV information string length (9 bits)
OUI (3 octets)
Subtype (1 octet)
EVB Capabilities (2 octets)
EVB Current Config. (2 octets)
VSI (4 octets)
RTE
Octets:
Bits:
1
2
3
6
7
9
11
15
8
2
1
8
1
8
7
8
3
1
2
1
Forwarding Mode
Capabilities
Reserved
ETTP
RTE
RR
Reserved
4
STD
Auth
VDP
8
7
8
3
1
2
1
Forwarding Mode
Capabilities
Reserved
ETTP
RTE
RR
Reserved
4
STD
Auth
VDP
14
# VSI Supported
(2 octets)
# VSI
Configured
(2 octets)
TLV information string = 13 octets
R
5
1
8
6

## Slide 5: Proposed EVB TLV (2)
Transport: LLDP
Retransmission Exponent (RTE)
  RTG (Retransmission Granularity) = 10 us
  Retransmission Multiplier (RTM) = 2RTE
  The ULP retransmission timer = RTM * RTG
  Both sides agree to the largest common value
Number of VSI Supported – Identifies the number of VSI that are supported by the sender. It may indicate limits imposed by buffering, ACL rules, etc.
Number of VSI configured identifies the of VSI currently in use.
  From the station, it indicates the number of resources that should be reserved by the bridge.
  From the bridge, it indicates the number of active Virtual Station Interfaces (VSI) discovered / configured
TLV header
TLV type = 127 (7 bits)
TLV information string length (9 bits)
OUI (3 octets)
Subtype (1 octet)
EVB Capabilities (2 octets)
EVB Current Config. (2 octets)
VSI (4 octets)
RTE
Octets:
Bits:
1
2
3
6
7
9
11
15
8
2
1
8
1
8
7
8
3
1
2
1
Forwarding Mode
Capabilities
Reserved
ETTP
RTE
RR
Reserved
4
STD
Auth
VDP
8
7
8
3
1
2
1
Forwarding Mode
Capabilities
Reserved
ETTP
RTE
RR
Reserved
4
STD
Auth
VDP
14
# VSI Supported
(2 octets)
# VSI
Configured
(2 octets)
TLV information string = 13 octets
R
5
1
8
6

## Slide 6: EVB Discovery TLV Usage Example
Station (e.g., Hypervisor)
1
Bridge
EVB TLV – OFFER CAPABILTIES
Capabilities Forwarding: Std, RR Other: VSI, Auth, etc. Current Config.(Std, None) # VSIs Supported = J # VSIs Configured = 0
RTE = 15
EVB TLV - CONFIGURE
Capabilities & Current Config. Forwarding: RR Other: VSI, Auth, etc. # VSIs Supported = J # VSIs Configured = K
RTE = 10
EVB TLV – CONFIRMATION
Capabilities Forwarding: Std, RR Other: VSI, Auth, etc. Current Config. Forwarding: RR Other: VSI, Auth, etc. # VSIs Supported = J # VSIs Configured = K
RTE 10
Bridge advertises what modes it can support and the max number of VSIs it can handle.
Server configures itself from the available capabilities according to local policy.
But still advertises its full set of capabilities.
2
3
Bridge matches its configuration to the limited capabilities advertised by the station.
Station or Bridge may initiate EVB TLV Exchange