## Slide 1: Portal Models Maarten Vissers 2012-03-12 v1

## Slide 2: DRNI Applicability
DRNI model is applicable to many different portal types
  PB Portal (S-DRNI)
  BCB Portal (B-DRNI)
  IB-BEB Portal (S-DRNI)
  IB-BEB Portal (B-DRNI)
  PEB Portal (C-DRNI)
  PEB Portal (RCSI S-DRNI)
  PEB Portal (S-DRNI)
  PEB Portal (S-DRNI & C-DRNI)
  EOTN TB Portal (S-DRNI)
  EOTN TEB Portal (RCSI S-DRNI)
  EOTN TEB Portal (C-DRNI)
  MPLS(TP) S-PE Portal (S-DRNI)
  MPLS(TP) T-PE (RCSI S-DRNI)
  MPLS(TP) T-PE (C-DRNI)
  IP Router Portal (C-DRNI)
  IP Router Portal (S-DRNI)
  Etc.
Can be Ethernet, IP, MPLS(TP), OTN, ..

## Slide 3: DRNI Applicability
These portal types have a common element, the “DRNI”
The network side of these portal types however are portal specific and the
  “network links” may be Ethernet links or other (e.g. Ethernet over Ethernet, OTN, MPLS(TP), IP) links
  “intra portal link” may be an Ethernet link or other (Ethernet over XXX) link
The functionality of these portals is described by the portal’s model, which is implementation independent
A portal’s functionality may be implemented in different manners
  As per model, with e.g. multiple switch fabrics
  Different from the model, with e.g. a single switch fabric operating at the DRNI signal layer
  Different from the model, with e.g. a single switch fabric operating at a different layer then the DRNI signal layer
Should 802.1AX-REV address each of those Portal types and Portal implementation alternatives?

## Slide 4: DRNI Scope
My suggestion is that:
  the 802.1AX-REV DRNI specification is agnostic to the different portal types and different portal type implementations
  there is a reference point between the DRNI Portal functionality and the network side portal functionality over which traffic and some limited amount of control information is exchanged
  the portal type specific specifications for the distributed network side functionality, are specified in the appropriate standards, e.g.:
    802.1Q for Ethernet PB, BCB, IB-BEB, PEB
    SG15 recommendations for Ethernet over OTN
    SG15 recommendations for EC protection
    IETF RFCs for Ethernet over MPLS(TP)
    IETF RFCs for IP over Ethernet
    …
  the portal type implementation specific aspects are outside the scope of the standards, but an example could be documented in an annex
Can be Ethernet, IP, MPLS(TP), OTN, ..

## Slide 5: Basic DRNI model
  The basic DRNI model on the left is derived from “Choices for Modeling IB-BEB DRNI”
  This model is used as starting point for developing the models of the different portal types
  This model can be used directly as model for the PB and BCB portals, as illustrated hereafter
  This model requires extensions for the other portal types, some of which are also illustrated in this slide set
  The model for the IB-BEB (S-DRNI) portal differs from the model in “Choices for Modeling IB-BEB DRNI”
Relay
Relay
System A
System B
Port
Port
MAC
Port
Port
MAC
MAC
IPP
IPP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed Relay
Distributed Relay
Intra-Portal Link
possible network link
Gateway Link
possible other network links
possible other network links
Gateway Link
Emulated System C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
Relay
Relay
System A
System B
Port
Port
Port
Port
IPP
IPP
Link Agg*
Link Agg*
MAC
MAC
Distributed Relay
Distributed Relay
Intra-Portal Link
possible network link
possible other network links
possible other network links
Link Aggregation Group (to Portal or Aggregation System)

## Slide 6: Basic DRNI model with DRNI related MEP/MIP location
  The MEP and MIP functions on the Link Agg Group ports are located in alignment with the location of those functions in clause 22/802.1Q as discussed in the Jan. 2012 meeting
  For the case the DRNI is supporting an E-NNI, the
    E-NNI (or Internet-Network) ME just spans a single physical link
    Network Operator ME monitors the Ethernet Connection up to the point where it will cross the E-NNI physical link (including the IPL, if in the path)
  The Ethernet Connection MEP/MIPs on the two portals will be Active in one portal and Standby in the other
Relay
Relay
System A
System B
Port
Port
MAC
Port
Port
MAC
MAC
IPP
IPP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed Relay
Distributed Relay
Intra-Portal Link
possible network link
Gateway Link
possible other network links
possible other network links
Gateway Link
Emulated System C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
Relay
Relay
System A
System B
Port
Port
Port
Port
IPP
IPP
Link Agg*
Link Agg*
MAC
MAC
Distributed Relay
Distributed Relay
Intra-Portal Link
possible network link
possible other network links
possible other network links
Link Aggregation Group (to Portal or Aggregation System)

## Slide 7: Basic DRNI model with multiple DRNIs
  A portal will typically connect the domain with more than one other domain
  Multiple DRNI instances will be present in such case on a portal
  Each DRNI instance is represented by an instance of the Emulated System C (C_1, C_2, ..)
  The multipoint nature of MP Ethernet Connections is assumed to be supported by the Relay functions in System A and B; each Emulated System C_i has one Active Gateway Link (other one is Stanbdy)
Relay
Relay
System A
System B
Port
Port
Port
Port
possible network link
possible other network links
possible other network links
MAC
MAC
MAC
IPP
IPP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed Relay
Distributed Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated System C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
MAC
MAC
MAC
IPP
IPP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed Relay
Distributed Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated System C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
MAC
MAC
MAC
IPP
IPP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed Relay
Distributed Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated System C_1
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)

## Slide 8: PB and BCB Portals

## Slide 9: PB/BCB Portal
  Basic DRNI model applies to PB and BCB portals
  This model specifies the DRNI aspects
  This model does not specify the network side aspects
  Network side includes an additional “Emulated PB/BCB D”
  Functionality of such Emulated PB/BCB D depends on deployed survivability method in network
    S-VLAN EC restoration via MSTP/MVRP
    S-VLAN EC protection via G.8031 EC SNCP
  See next two slides
S Relay
S Relay
PB/BCB A
PB/BCB B
PNP
PNP
MAC
PNP
PNP
MAC
MAC
PNP
PNP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
possible network link
Gateway Link
possible other network links
possible other network links
Gateway Link
Emulated PB/BCB C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
S Relay
S Relay
PB/BCB A
PB/BCB B
PNP
PNP
PNP
PNP
PNP
PNP
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
possible network link
possible other network links
possible other network links
Link Aggregation Group (to Portal or Aggregation System)

## Slide 10: PB/BCB Portal with G.8031 EC SNC protection
  EC SNC protection adds an Emulated PB/BCB D to the model
  It consists of Distributed S Relay functions, PNP port functions, an Intra-Portal Link and SNCP functions which connect via a Gateway Link to an S Relay function
  The distributed S Relay functions either relay the incoming EC signal, or present the W and P EC segment signals to the SNCP function
  EC SNCP MEP functions are located between SNCP function and Distributed S Relay function; the two sets operate in Active/Standby mode
S Relay
S Relay
PB/BCB B
PNP
PNP
MAC
PNP
PNP
MAC
MAC
PNP
PNP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
possible network link
Gateway Link
possible other network links
possible other network links
Gateway Link
Emulated PB/BCB C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
MAC
MAC
MAC
PNP
PNP
MAC
PNP
PNP
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated PB/BCB D
* The two “SNCP” state machines require coordination
EC Protection Group (to Portal or SNCP endpoint)
SNCP*
SNCP*
PB/BCB A

## Slide 11: PB/BCB Portal with MSTP/MVRP EC restoration
  EC restoration with MSTP/MVRP restores “EC segments”, like EC SNC protection
  Does this imply that EC restoration adds an Emulated PB/BCB D to the model as illustrated on the right?
  Is the model on the right a correct model?
S Relay
S Relay
PB/BCB A
PB/BCB B
PNP
PNP
MAC
PNP
PNP
MAC
MAC
PNP
PNP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
possible network link
Gateway Link
possible other network links
possible other network links
Gateway Link
Emulated PB/BCB C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
MAC
MAC
MAC
PNP
PNP
MAC
PNP
PNP
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated PB/BCB D
* The two “SNCP” state machines require coordination
S/B-VLAN EC Restoration Group
?

## Slide 12: EOTN TB Portal

## Slide 13: EOTN TB Portal
  EOTN TB Portal is very similar to PB/BCB Portal for the DRNI functionality
  Main difference is the type of ports used: ONP versus PNP
S Relay
S Relay
TB A
TB B
ONP
ONP
MAC
ONP
ONP
MAC
MAC
ONP
ONP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
possible network link
Gateway Link
possible other network links
possible other network links
Gateway Link
Emulated TB C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
S Relay
S Relay
TB A
TB B
ONP
ONP
ONP
ONP
ONP
ONP
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
possible network link
possible other network links
possible other network links
Link Aggregation Group (to Portal or Aggregation System)

## Slide 14: EOTN TB Portal with G.8031 EC SNC protection
  EC protection adds an Emulated TB D to the model, similar to the PB/BCB case
S Relay
S Relay
TB A
TB B
ONP
ONP
MAC
ONP
ONP
MAC
MAC
ONP
ONP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
possible network link
Gateway Link
possible other network links
possible other network links
Gateway Link
Emulated TB C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
MAC
MAC
MAC
ONP
ONP
MAC
ONP
ONP
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated TB D
* The two “SNCP” state machines require coordination
EC Protection Group (to Portal or SNCP endpoint)
SNCP*
SNCP*
S-VLAN MEP function pairs are Active on one port and Standby on the other

## Slide 15: EOTN TB Portal with ODU SNC protection
EOTN supports also other network side survivability methods, e.g.:
  ODU SNC protection (which is an ODU segment protection)
  ODU restoration
For the ODU SNC protection case, a similar Emulated System D is present, now operating at the ODU level (instead of the S-VLAN EC level) [see next slide].
Emulated System D connects to two ODU Relay functions (providing the OTN System A and B functionality). The ODU Relay functions connect via ONP functions with the S Relay and Distributed S Relay functions.
This Emulated system (SWXC) D consists of
  Distributed ODU Relay functions,
  OTN port functions,
  an Intra-Portal Link,
  ODU SNCP related MEP functions
  SNCP functions which connect via a Gateway Link to an ODU Relay function

## Slide 16: EOTN TB Portal with ODU SNC protection
ODU Relay
ODU Relay
SWXC A
SWXC B
Port
Port
Port
ONP
possible network link
possible other network links
possible other network links
S Relay
S Relay
TB A
TB B
ONP
ONP
ONP
ONP
Intra-Portal Link
possible network link
Port
Port
Port
Port
Distributed ODU Relay
Distributed ODU Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated SWXC D
* The two “SNCP” state machines require coordination
ODU Protection Group (to Portal or SNCP endpoint)
SNCP*
SNCP*
MAC
MAC
MAC
ONP
ONP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated TB C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
ODU MEP functions are Active on one port and Standby on the other
ODU MEP function pairs are Active on one port and Standby on the other

## Slide 17: IB-BEB (S-DRNI) Portal

## Slide 18: IB-BEB (S-DRNI) Portal with ESP/TESI segment protection
ESP Segment protection is the functional equivalent of ODU SNC protection
A similar model – in which ODU is replaced by ESP – is applicable [see next slide]
Note: The model on the next slide describes the required behaviour of the portal. Implementations will typically provide only a single switch fabric, which implies that the behaviour of the second Relay function has to be emulated in the implementation. This emulation is assumed to be outside the scope of the standard.
Question: is there a need for a possible network link between the S Relay functions in systems A and B?

## Slide 19: IB-BEB (S-DRNI) Portal with ESP/TESI Segment protection
possible network link?
B (ESP) Relay
B (ESP) Relay
B-component A
B-Component B
PNP
PNP
PNP
PNP
possible network link
possible other network links
possible other network links
S Relay
S Relay
I-Component A
I-Component B
PIP
?
?
PIP
Intra-Portal Link
MAC
MAC
MAC
PNP
PNP
MAC
PNP
PNP
Distributed B (ESP) Relay
Distributed B (ESP) Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated B-Component D
* The two “SegP” state machines require coordination
SegP*
SegP*
MAC
MAC
MAC
PIP
PIP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated I-Component C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
CBP
CBP
CBP
CBP
ESP Segment Protection Group (to Portal or endpoint)
ESP MEP functions are Active on one port and Standby on the other
ESP MEP function pairs are Active on one port and Standby on the other
Implementation “shortcut”

## Slide 20: IB-BEB (S-DRNI) Portal with B-VLAN restoration (MSTP/MVRP)
B-VLAN restoration by means of MSTP/MVRP provides also a segment like survivability method
A similar model – in which ESP is replaced by B-VLAN – is assumed to be applicable [see next slide]
Note: The model on the next slide describes the required behaviour of the portal. Implementations will typically provide only a single switch fabric, which implies that the behaviour of the second Relay function has to be emulated in the implementation.

## Slide 21: IB-BEB (S-DRNI) Portal with B-VLAN restoration (MSTP/MVRP)
possible network link?
?
?
B Relay
B Relay
B-component A
B-Component B
Port
Port
Port
PNP
possible network link
possible other network links
possible other network links
S Relay
S Relay
I-Component A
I-Component B
PIP
PIP
Intra-Portal Link
MAC
MAC
MAC
PNP
PNP
MAC
PNP
PNP
Distributed B Relay
Distributed B Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated B-Component D
* The two “SegP” state machines require coordination
B-VLAN Restoration Group (to Portal or endpoint)
MAC
MAC
MAC
PIP
PIP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated I-Component C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
CBP
CBP
CBP
CBP
?
B-VLAN MEP functions are Active on one port and Standby on the other

## Slide 22: IB-BEB (S-DRNI) Portal with ESP/TESI protection
ESP/TESI protection switching is performed at the other side of the B Relay compared to ESP/TESI Segment protection
Also in this case an Emulated System D is present, but now located between B Relay functions and I-component functions [see next slide]
Note: The model on the next slide describes the required behaviour of the portal. Implementations will typically provide only a single switch fabric, which implies that the behaviour of the second Relay function has to be emulated in the implementation.

## Slide 23: IB-BEB (S-DRNI) Portal with ESP/TESI protection
possible network link?
?
?
B (ESP) Relay
B (ESP) Relay
B-component A
Port
Port
Port
PNP
possible network link
possible other network links
possible other network links
S Relay
S Relay
I-Component A
I-Component B
PIP
PIP
Intra-Portal Link
B-Component B
MAC
MAC
CBP*
MAC
MAC
CBP*
MAC
MAC
Distributed B (ESP) Relay
Distributed B (ESP) Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated B-Component D
* The two “CBP” state machines require coordination
ESP Protection Group (to Portal or endpoint)
MAC
MAC
MAC
PIP
PIP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated I-Component C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
CBP
CBP
MAC
MAC
ESP MEP function pairs are Active on one port and Standby on the other

## Slide 24: PEB (C-DRNI) Portal

## Slide 25: PEB (C-DRNI) Portal with EC SNC protection
A similar model as described for the IB-BEB case – in which S-VLAN is replaced by C-VLAN and ESP by S-VLAN – is assumed to be applicable [see next slide]
Note: The model on the next slide describes the required behaviour of the portal. Implementations will typically provide only a single switch fabric, which implies that the behaviour of the second Relay function has to be emulated in the implementation.

## Slide 26: PEB (C-DRNI) Portal with EC SNC protection
S Relay
S Relay
S-Component A
S-Component B
PNP
PNP
PNP
PNP
possible network link
possible other network links
possible other network links
C Relay
C Relay
C-Component A
C-Component B
CNP
PEP
PEP
CNP
Intra-Portal Link
PNP
PNP
PNP
PNP
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated S-Component D
* The two “SNCP” state machines require coordination
EC Protection Group (to Portal or SNCP endpoint)
SNCP*
SNCP*
MAC
MAC
MAC
PEP
PEP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed C Relay
Distributed C Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated C-Comp. C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
CNP
CNP
MAC
MAC
MAC
MAC
S-VLAN MEP function pairs are Active on one port and Standby on the other
S-VLAN MEP functions are Active on one port and Standby on the other
Implementation “shortcut”

## Slide 27: PEB (S-DRNI & C-DRNI) Portal
A PEB Portal might have DRNI active on both the UNI and the (E)NNI sides
On a C-Tagged UNI this will be a C-DRNI
On the (E)NNI this will be a S-DRNI

## Slide 28: PEB (S-DRNI & C-DRNI) Portal
S Relay
S Relay
S-Component A
S-Component B
PNP
PNP
PNP
PNP
possible network link
possible other network links
possible other network links
C Relay
C Relay
C-Component A
C-Component B
CNP
PEP
PEP
CNP
Intra-Portal Link
MAC
MAC
MAC
PEP
PEP
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed C Relay
Distributed C Relay
Intra-Portal Link
Gateway Link
Gateway Link
Emulated C-Comp. C
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
CNP
CNP
MAC
MAC
S-VLAN MEP functions are Active on one port and Standby on the other
Implementation “shortcut”
Intra-Portal Link
MAC
MAC
Link Agg*
Link Agg*
MAC
MAC
Distributed S Relay
Distributed S Relay
Intra-Portal Link
Gateway Link
Gateway Link
* The two “Link Agg” state machines require coordination
Link Aggregation Group (to Portal or Aggregation System)
Emulated S-Comp. D
MAC
MAC
MAC
MAC
PNP
PNP

## Slide 29: PEB (RCSI S-DRNI) Portal
To be added

## Slide 30: Conclusion and Questions

## Slide 31: Conclusion and Questions
The portal examples in the previous slides illustrate that the same basic DRNI model with “emulated system C” can be used in the different portal types to describe the DRNI behaviour
The examples also illustrate that at the network side an additional “emulated system D” is present to represent the distributed network protection/restoration functionality
These emulated systems C and D are interconnected via either one pair of system A/system B Relay functions, or via two (or more) pairs of system A/system B Relay functions and interconnecting ports
Proposal: Include some or all of those portal examples in Annex D or Z/802.1AX-REV
Question 1: Should 802.1AX-REV specify both the emulated system C (DRNI) and the emulated systems D (network side protection/restoration) functionality, or should 802.1AX-REV be restricted to the DRNI functionality? If the latter, where can we specify the emulated system D functionality? In 802.1Q for the Ethernet specific cases?
Question 2: Should the emulated system C and emulated system D interconnecting architectures be in the scope of 802.1AX-REV? If not, should this be in the scope of 802.1Q, which is specifying the architectures of the different nodes (PB, PEB, IB-BEB, BCB)?

## Slide 32: Thank you