## Slide 1: Port ID issue raised in DRNI
Corona Wei
Wei.yuehua@zte.com.cn

## Slide 2: What does 802.1AX-2008 say?
6.3.4 Port identification
Link Aggregation Control uses a Port Identifier (Port ID), comprising the concatenation of a Port Priority and a Port Number, to identify the Aggregation Port. Port Numbers (and hence, Port Identifiers) shall be
uniquely assigned within a System. Port Number 0 shall not be assigned to any Aggregation Port.
When it is necessary to perform numerical comparisons between Port Identifiers, each Port Identifier is considered to be a four octet unsigned binary number constructed as follows:
a) The most significant and second most significant octets are the first and second most significant octets of the Port Priority, respectively.
b) The third and fourth most significant octets are the first and second most significant octets of the Port Number, respectively.

## Slide 3: Two options
Port Identifier (Port ID) (4 Octets) |  |  | 
Port Priority |  | Port Number | 
Octet4 | Octet3 | Octet2 | Octet1
Portal System Number
Or
How to construct the Port ID in order to include “Portal System Number” to keep the new “Port Number” to be unique among a Portal?
What’s the difference?
Option 1 : There’s possibility that people configure different Port Priority but get EQUAL Port ID. Maybe we need modify the definition of “Port Priority” to 14 bits to avoid the risk.
Option 2: People can use/configure Port Priority(which is read-write) to adjust/affect the aggregation port‘s position in all Aggregation Port’s ordered lists. It is consistent with the existing implementation of legacy LAG. Maybe we need to restrict the local Port Number to less than 14 bits so that value we got in the third and fourth most significant octets of the Port ID is UNIQUE between all of the Portal Systems.
Option1: concatenate “Portal System Number” to the least significant two bits to the place of Port Priority.
Option 2: concatenate “Portal System Number” to the most significant two bits to the place of Port Number.

## Slide 4: Two concerns
For option 1: if we modify Port Priority to 14 bits, will it lead to compatibility issues? Port Priority is a read-write variable, the industry has already implemented it as 16 bits.
For option 2: if we restrict the local Port Number to less than 14 bits(<16383) , the question is: is 14 bits for local Port Number (from 1 to 16383) enough? Has the industry (chips) assigned BIG number to local ports?

## Slide 5: Thank you!