## Slide 1: RAC concerns for longevity of the OUI / MAC Address registry
Robert M. Grow
Chair, IEEE Registration Authority Committee

## Slide 2: OUI registry
OUI registry provides a 24 bit company identifier
All assigned OUIs have two appropriate bits as zero to allow use in creation of universally (aka, globally) unique MAC addresses
The RAC has “products” based on OUIs, that provide MAC addresses

## Slide 3: OUI registry longevity
Target was for 100 year longevity
We are now 40 years into assignment of OUI identifiers (including Xerox assignments)
Current rate of use if maintained is not a problem for exhaustion of values
Rate of consumption though is not linear, it is accellerating, hence concern
How many still want to be able to use 48-bit addresses 60+ years from now?

## Slide 4: Company ID (CID)
OUIs are being consumed for identifiers where no MAC addresses are needed.
Multiple 48-bit MAC addresses are now common on devices
  Products consuming 128 addresses per network interface were an alarm
CID can be used to reduce consumption of OUIs for non-address purposes as well as for reduction of consumption of MAC addresses

## Slide 5: RAC considerations
From earliest consideration of introducing a CID product, use of CID as a base for local addresses was always part of the debate
This is evident from RAC tutorials