## Slide 1
802.1AS Asymmetrical delay problem and potential update
Tom McBeath
Forthgem Consultants LLC

## Slide 2
Why does this matter
In the case of audio or video total addition of asymmetry is unlikely to be significant enough to matter and so doesn't matter and would not have been noticed.
In the case of 802.1Qbv if the accumulation of the asymmetric delay is sufficient to mean that the packet is sent too late to be meet the open window this would mean that Qbv would guarantee slow forwarding due to closed gates.
In the case of an industrial application difference might cause mechanical problem

## Slide 3
Asymmetric delay examples
Master time (mt) | Calculated slave time (cst) | Calculated receive timestamp | Actual Receive Timestamp | Correct receive time
1 | -1 | 1+8=9 mt+c | 10-1=9 cst+t | 1+10=11 mt+1t
5 | 2 | 5+8=13 | 3+10=13 | 5+10=15
Asymmetry in delay is 4 units (d) transmit delay is 10 (t) calculated delay is 8 (c)
Master time | Calculated slave time | Calculated receive timestamp | Actual Receive Timestamp | Correct receive time
1 | -2 | 1+7=8 | 10-2=8 | 1+10=11
5 | 2 | 5+7=12 | 2+10=12 | 5+10=15
12 | 9 | 12+7=19 | 9+10=19 | 12+10=22
Asymmetry in delay is 6 units transmit delay is 10 calculated delay is 7

## Slide 4
Asymmetric delay examples
Master time | Calculated slave time | Calculated receive timestamp | Actual Receive Timestamp | Correct receive timestamp
3 | 7 | 3+10=13 | 7+6=13 | 3+6=9
7 | 11 | 7+10=17 | 11+6=17 | 5+10=15
Asymmetry in delay is 8 units transmit delay is 6 calculated delay is 10

## Slide 5
Problem Diagram
Grand
Master
Qbv
Source
802.1As
Switch
Qbv
Next hop
Clock sync path
Qbv
Source
Data path
802.1Qbv channel gate window
802.1AS Asymmetric Time offset per switch
802.1AS Accumulated offset
Packet occasionally has to wait for
next gate window slightly more
than perfect timing

## Slide 6
Problem Diagram
Grand
Master
Qbv
Source
802.1As
Switch
Qbv
Next hop
Clock sync path
Qbv
Source
Data path
802.1Qbv channel gate window
802.1AS Asymmetric Time offset per switch
802.1AS Accumulated offset
802.1As
Switch
Packet more
occasionally
has to wait for
next gate window

## Slide 7
Problem Diagram
Grand
Master
Qbv
Source
802.1As
Switch
Qbv
Next hop
Clock sync path
Qbv
Source
Data path
802.1Qbv channel gate window
802.1AS Asymmetric Time offset per switch
802.1AS Accumulated offset
802.1As
Switch
802.1As
Switch
Packet frequently
has to wait for
next gate window

## Slide 8
Problem Diagram
Grand
Master
Qbv
Source
802.1As
Switch
Qbv
Next hop
Clock sync path
Qbv
Source
Data path
802.1Qbv channel gate window
802.1AS Asymmetric Time offset per switch
802.1AS Accumulated offset
802.1As
Switch
802.1As
Switch
802.1As
Switch
Packet nearly always
has to wait for
next gate window

## Slide 9
Problem Diagram
Grand
Master
Qbv
Source
802.1As
Switch
Qbv
Next hop
Clock sync path
Qbv
Source
Data path
802.1Qbv channel gate window
802.1AS Asymmetric Time offset per switch
802.1AS Accumulated offset
802.1As
Switch
802.1As
Switch
802.1As
Switch
802.1As
Switch
Packet always
has to wait for
next gate window

## Slide 10
Problem Diagram
Grand
Master
Qbv
Source
802.1As
Switch
Qbv
Next hop
Clock sync path
Qbv
Source
Data path
802.1Qbv channel gate window
802.1AS Asymmetric Time offset per switch
802.1AS Accumulated offset
802.1As
Switch
802.1As
Switch
802.1As
Switch
802.1As
Switch
802.1As
Switch
Packet always
has to wait for
next gate window

## Slide 11
No issue if BV and AS have same path
802.1Qbv
802.1As
Switch
802.1Qbv
gate window
802.1AS
Asymmetric
Time offset per
switch
802.1AS
Accumulated offset
Since if the data and Time Sync are on same path the sync time error equals the calculated
delay error and then there is no window alignment issue
Correct time is there was no Asymmetric error
Time line for gate opening and closing window
802.1Qbv
802.1As
Switch
802.1Qbv
802.1As
Switch
802.1Qbv
802.1As
Switch
802.1Qbv
802.1As
Switch
802.1Qbv
802.1As
Switch

## Slide 12
Problem definition
Neither 802.1AS nor 1588 have standard mechanism to compensate for Asymmetrical delays between two points in a network.
An extreme example of this problem is if one end of link is a hardware based Switch and other end is software based end point. Without use of something like DPDK the delay on receive could be on average milliseconds greater than on transmit due to potential scheduling issue. So this is a case where Asymmetry might matter for AVB if only on one listener.
A less extreme example would be a PCIe controller chip that might take longer to receive a message and forward to processing engine than to send a message from the processing unit to to the I/O

## Slide 13
Source of Asymmetric delay
Clock master end
Clock Slave end
Calculated delay equals
Which is accumulated delay Divided by 4
Asymmetric error red block
Delay from processing doing send to processing getting receive
Not just time on link

## Slide 14
Effect of Asymmetrical delay on time
Time on Device 2 is calculated as the timestamp on the message sent from Device 1 plus a delay which is calculated as half the sum of the round trip delay.
So if delay from D1 to D2 is 3 and delay from D2 to D1 is 9 then delay between units is calculated as 6 so time set at D2 will be 3 time units ahead of correct time.
In worst case if delay offset is same direction on 6 units in chain then offset of final unit in chain from correct time would be sum of all 6 units' asymmetric time delays divided by 2.

## Slide 15
Potential solutions
Specify in 802.1Qbv standard that timing for switches should be set on same path as data
Have exactly the same switches in whole network in which case delay is guaranteed to be Symmetrical so no delta to accumulate or have two types of switches interspersed in the form A-B-A-B-A-B-A-B-A-B in which case Asymmetry cancels out
Add the manufacturer measured TX and RX delays to the specifications of an AS Switch.

## Slide 16
Alternative solution
Specify in standard that delay on TX side should be proven to be same as delay on RX side in which case even if devices have different delays round trip delay will still be symmetric.
Mechanism to do this would be to have a layer 1 device which set bit when it sees packet and bit on Switch device to indicate it received packet and is ready to compare time and another bit to say its sending a packet. The time delay between silicon and test bits give RX and TX latency.