## Slide 1: Proposal for the MAC address assignment protocol
Ting Ao
ao.ting@zte.com.cn

## Slide 2: Prior Arts
Local Address Study Group:
  P802C:define Local MAC address, almost done.
  P802.1CQ: A Local Address assignment protocol, on going
Problems MAC address assignment protocol faces
  How to get MAC address without any source address
  How to locate the MAC address requester when response
  How to avoid MAC address conflict
  How to avoid broadcast flooding
  ……
Notes: How

## Slide 3: Our proposal for Local MAC address protocol
Define a structured Local MAC address with position information
  Like: Bridge ID+Host ID
  Or:Bridge ID+Port ID+Host ID
Take a “class-by-class” assignment strategy
  Every network device get a Bridge ID assignment from its upper class network device and inherit Bridge ID of the upper class network device.
  Every host get a Host ID from network device it connected and inherit Bridge ID from the network device connected.
  So Bridge ID+ Host ID make up the MAC address of a host.

## Slide 4: Take SAI as an example
Logical DB
Bridge 1
Bridge 2
B11
B12
B13
B23
B22
B21
H1
H3
H4
H5
H6
H7
H8
H9
H
10
H
11
H2
H
12
Request
Response
1E0000000000
2E0000000000
1E1000000000
2E1000000000
1E1000000001
2E1000000002
Note：the lenth of the Bridge ID depend on the scale of this class of network device.
Class 1
Class 2

## Slide 5: Merits
Every MAC address is related to its bridge connected  No MAC addresss conflict exists
Every network device communicate with other device it connected directly  No broadcast frames flooded
Every network device can keep the mapping between the bridge id/host id assignment and the port. It’s easy locate the requester, the port connected is the requester.
Every structured Local MAC address is position related.
   Improve the forwarding performance
   Easy to locate fault and fault diagnosis

## Slide 6
Thanks!