## Slide 1: Plans for next Editor’s draft Version 1
Stephen Haddock
January 19, 2017

## Slide 2: Selected plans for AX-Rev-d0.1
(Re-)Incorporate Wait-to-Restore timer
Mick’s MUX state machine
ISS Status parameters
actorAdminX and actorOperX variables
Merge Verification and Receive Long LACPDU state machines into the LACP Receive state machine
  Which would fix the setting of default values for Conversation Sensitive Collection and Distribution
Start work on clause 9 (DRNI)

## Slide 3: Mux state machine
Propose to accept Mick’s Mux state diagram
    Fig 4 of http://www.ieee802.org/1/files/public/docs2017/ax-rev-seaman-wait-to-restore-0117-v01.pdf
  Incorporates WTR Timer (adding ATTACHED_WTR state)
  Subsumes WAITING state into DETACHED state
    Makes wait-to-attach timer responsibility of Selection Logic
  Adds ATTACH state and “mux_attach” variable
    Would prefer to name the variable ”port_attached” or simply “attached”
  Provides direct transitions for cases where current Mux machine “ripples” through several states with no change in input variables
  Consolidate independent-control and coupled-control diagrams

## Slide 4: ISS Status Parameters
History
  802.3ad-2000 (clause 43) placed the Link Aggregation Sublayer between MAC Control and MAC Client sublayers, and included status parameters consistent with 802.3 layer architecture and naming.
  802.1AX-2008 made Link Aggregation a stand alone 802.1 standard, with minor changes to make sublayers MAC type independent.
  802.1AX-2014 placed the Link Aggregation Sublayer between instances of the Internal Sublayer Service (ISS) to make it consistent with 802.1 architecture (and allow things like CFM shims around the Link Aggregation sublayer).
    Made description of the parser/mux elements consistent with ISS
    Provided text to connect the 802.3 style status parameters to the ISS Status
      Still a few gaps and sources of confusion …

## Slide 5: Aggregation Port Status parameters
ISS has MAC_Enabled and MAC_Operational
Link Aggregation Sublayer
  does not use the MAC_Enabled parameter
  does use the MAC_Operational parameter …
    but calls it “port_enabled” (Arghh !)
    The name dates back to the dark ages when 802.3 MACs had no idea if they were connected to anything or not and did not distinguish between being enabled and being operational.
  Propose renaming this to “port_operational”
    Does not affect any managed objects or the MIB.

## Slide 6: Aggregator Port Status parameters
The ISS MAC_Enabled and MAC_Operational are variables associated with the service providing the SAP
  But if look in “6.4.6 Variables associated with each Aggregator” you won’t find anything looking like enabled and operational status parameters for the Aggregator Port.
  The Aggregator managed objects (6.3.1.1.13 and 6.3.1.1.14) include aAggAdminState (Read/Write with values up/down) and aAggOperState (Read-only with values up/down) that have (almost exactly) equivalent semantics to MAC_Enabled and MAC_Operational.
  802.1AX-2014 added section “6.3.12 MAC_Operational Status” that describes how the managed objects relate to the Aggregator Port MAC_Operational value, but no mention of MAC_Enabled
    … with a few inconsistencies in the MAC_Operational description.

## Slide 7: Aggregator Port Status proposal
Add Aggregator_Enabled and Aggregator_Operational parameters to 6.4.6.
  Modify section 6.3.12 to use these terms
Rename the managed objects to use 802.1AC ISS style names and values instead of 802.3 sub-layer interface style
  Would require deprecating old MIB objects and adding new, but we’ll certainly have other MIB updates anyway
  Don’t have to do this, but I think it would reduce confusion.
Delete the Aggregator Receive_State and Transmit_State
  These are not used anywhere, or available to management.
  Only reference to them is in 6.3.12 and is wrong.

## Slide 8: actorAdminX/actorOperX variables
There are several cases where actorAdmin and actorOper variants of a variable are present
  without a description of when/how the Admin value affects the Oper value,
  and without a clear specification of the side effects when writing a new Admin value

## Slide 9: Merge CSCD Rx state machines into the LACP Receive state machine
802.1AX-2014 went to extraordinary lengths
  not to modify the description of LACP v1 functionality, and
  to keep any new LACP v2 functionality completely separate.
This was generally a noble objective, but in some cases led to unreasonable results
  Having a single received LACPDU be parsed and processed by three separate state machines is a prime example.
    Not incorporating the Verification machine into the basic receive machine prevents correct handling of “recordDefault…” functions.

## Slide 10: Backup Slides