## Slide 1: VDP extension for SR-IOV
Lu Huang, China Mobile (huanglu@chinamobile.com)

## Slide 2: SR-IOV Scenario in telecom cloud Network
In telecom cloud, NFV is used to replace traditional core network, such as EPC, IMS, etc. Traditional specific device is transformed into virtual network function software (VNF) running on virtual machine (VM) of generic hardware (e.g. x86).
And SDN controller is used to build traffic path for VNFs. Usually SDN controller can control vSwitches to build paths through OPENFLOW. But in some case, SR-IOV is introduced in for acceleration, where traffic don’t go through vSwitch. So in SR-IOV scenario SDN controller have to control physical switch to build paths for VMs/VNFs.
OpenStack
NFV-O
VNFM
SDN
controller
Server
V
M
V
M
vSwitch
Server
V
M
V
M
pSwitch
SR-IOV
Non SR-IOV
VLAN x
VLAN y

## Slide 3: VDP extension requirement in SR-IOV scenario
When building forwarding paths, SDN controller should get the association between network and VMs.
  In non-SR-IOV scenario, vSwitch can report “port status” to SDN controller who can read port UUID from vSwitch through OVSDB. Based on port UUID, SDN controller can associate ports on vSwitch and networks
  In SR-IOV scenario, there’s no standard entity and protocol for information exchange between SDN controller, pSwitch and Server. VDP extension probably is the appropriate solution for us.
OpenStack
NFV-O
VNFM
SDN
controller
Server
V
M
V
M
vSwitch
Server
V
M
V
M
pSwitch
SR-IOV
Non SR-IOV
Create network
Create port (with UUID)
OpenFlow
& OVSDB
?
?
VLAN x
VLAN y

## Slide 4: Further consideration
There’s another scenario where we have the similar requirement. In some cases, pSwitches work as the SDN forwarding devices no matter vSwitches exist or not. Then we need to use extended VDP as same as the SR-IOV scenario.
OpenStack
NFV-O
VNFM
SDN
controller
Server
V
M
V
M
vSwitch
Server
V
M
V
M
pSwitch
(VTEP)
SR-IOV
Non SR-IOV
Create network
Create port (with UUID)
?
?
VLAN x
VLAN y
pSwitch
(VTEP)
?
?

## Slide 5: Proposal
Support SR-IOV scenario in VDP extension, which is not an EVB case.
Support information exchange between server and pSwitch, pSwitch and SDN contoller
Support UUID+VID exchange
OpenStack
NFV-O
VNFM
SDN
controller
Server
V
M
V
M
vSwitch
Server
V
M
V
M
pSwitch
SR-IOV
Non SR-IOV
Create network
Create port (with UUID)
OpenFlow
& OVSDB
VDP(UUID + VID)
VLAN x
VLAN y
VDP(UUID + VID)

## Slide 6: Thank you Q&A