## Slide 1: Coexistence & Convergence in TSN-based industrial automation networks
Marius Stanica, IEEE/IEC JP 60802, July 2018, Frankfurt

## Slide 2: Topics
Coexistence of the TSN configuration models
Coexistence of two traffic shaping mechanisms
  For the same traffic type
Convergence of network segments supporting various port/media redundancy mechanisms
  Seamless: IEEE 802.1 CB, IEC 62439 PRP, HSR
  Non-seamless: IEC 62439 MRP, DLR

## Slide 3: Coexistence. Configuration. Problem statement
System
  Operations & Engineering
  Network Infrastructure
  Process & Field
Mixed methods of TSN features configuration
  Operations & Engineering: fully-centralized
  Network Infrastructure: fully-centralized
  Process & Field: mixed
    Functional Unit 1: fully-distributed
    Functional Unit 2: fully-centralized
    Functional Unit 3: fully-distributed
  Head-CNC: a CNC which has an understanding of the whole system
    Local-CNC: a CNC for a functional unit (if needed/relevant) – a physical subnetwork
  Examples of TSN domains: Functional Unit 1, Functional Unit 2, Functional Unit 3, Network Infrastructure, Operations & Engineering, Communication2HMI
System has to work!

## Slide 4: Coexistence. Configuration. Needed functions
Synchronised and joint (dynamic and/or static) reservations management
  Actors involved
    Head-CNC, Local-CNC(s), bridges
  Understanding of the system
    Head-CNC has knows/discovers the capabilities of the whole network, including of bridges which are not centralized-configurable
  Synch (between fully-distributed and centralized bridge resource-related reservations)
    Head-CNC polls boundary bridges of the fully-distributed subnetwork(s) for currently allocated reservations
    Head-CNC informs the boundary bridges (of the fully-distributed subnetwork(s)) about reservations made over the centralized model
  CNC-hierachy control
    Head-CNC polls Local-CNC(s) for their centralized-allocated resource reservations
  Race conditions avoidance
    Locks must be in place while a poll is ongoing for a bridge, both for bridges and CNC reservations
    Locks must be also in place in bridges and Local-CNC(s) when Head-CNC poll happens
  Reservations conflict management
    Head-CNC must be capable of handling conflicts: identification, analysis, solution, information of all parties
  Security
    Authentication
  Diagnostics
    Early identification of misconfigurations
    Support for troubleshooting in case of misconfigurations
  Nice to have: Dynamic resource-usage optimization
    Head-CNC may perform regular analysis of the traffic and of application communication requirements and may propose optimizations, following current situation

## Slide 5: Coexistence. Traffic shaping. Problem statement
TSN domain for Functional Unit 1
  Only cyclic communication traffic type/pattern (for now, let us consider just this example) within this Functional Unit
  Three Drives and a PLC supporting the same traffic shaping mechanism for cyclic communication (i.e. Qav)
  One Drive (Drive 4), supports only another traffic shaping mechanism for cyclic communication (i.e. only fixed priority) and it is brought in, i.e. as a fast replacement (until a new device arrives following order)
  Daisy-chain ring topology
  Bridges support both traffic shaping methods
  TSN configuration model: as presented in Slide 3, thus Drive 4 supports only fully-distributed TSN configuration
Drive 4 should be integrate-able to this functional unit (then is this functional unit „a safe neighbourhood/TSN domain“ anymore? It should be.)

## Slide 6: Coexistence. Traffic shaping. Needed functions
Synchronization between traffic shaping mechanisms
  It depends on which exact traffic shapers do we refer to
    The example with Qav and Fixed Priority is rather easy and can be handled by the fully-distributed TSN configuration model
    If the preponderent traffic shaper would have been Qbv and the added device would only support Qav, then the fully-distributed TSN configuration model would not be enough (as of todays Qcc) to support such an use case, without the support of a CNC
    Configuration coexistence concepts from the previous chapter would be a good fit
Head-CNC must be capable of
  Understanding which traffic shapers are supported in the system
  Calculate the correctly needed reservations
  Send the reservations towards the bridges of Functional Unit 1

## Slide 7: Convergence. Redundancy. Problem statement
Same system as in Slide 3
  Seamless media redundancy model is IEEE 802.1 CB in the Operations & Engineering and Network Infrastructure
  Seamless media redundancy model in Functional Unit 1 is a different one: i.e. HSR
  Could be also viceversa than in the pictured example: there is a functional system working on a given seamless media redundancy (i.e. HSR, PRP,…) and an new functional unit based on IEEE 802.1 CB is added
Functional Unit 1 should be integreatable without the need of additional hardware

## Slide 8: Convergence. Redundancy. Needed functions
Compatibility between mechanisms of doubling/elimination of double frames must be achieved, for seamless mechanisms
Non-seamless media redundancy protocols (i.e IEEE RSTP, IEC 62439 MRP) are already coexistent with 802.1 CB
PRP, HSR are interoperable with 802.1CB (at least partly?)