IEEE 802.11

Wireless Access Method and Physical Specification

Proposed Text for Section 7 (Layer Management)

July 11, 1995

Greg Ennis

Symbol Technologies, Inc.

Bob O’Hara

Advanced Micro Devices

Mike Trompower

Aironet Wireless Communications

Dean Kawaguchi

Symbol Technologies, Inc.

Michael Fischer

Digital Ocean Inc.

Background

Layer Management section:

was Section 6 (Draft 1.1), now Section 7 (Draft 1.2)

Section currently has no content

Small group volunteered at Salt Lake City meeting to work on this

Goal: develop basic framework consistent with other sections

Layer Management Entities and Service Access Points

GET and SET Operations

GET/SET.REQUEST and CONFIRM

XX = PM or MM:

XX_GET.request (MIB_parameter)

XX_GET.confirm (status, MIB_parameter, 							  MIB_parameter_value)

XX_SET.request (MIB_parameter, MIB_parameter_value)

XX_SET.confirm (status, MIB_parameter)

Other Primitives

Everything could be represented as MIB operations

May be more natural to represent certain operations with dedicated primitives

Example: complex operations involving multiple parameters

Different PHYs currently take different approaches

Current PHY Management Primitives (Non-MIB)

FH:

Reset, Power, SetChannel

DS:

Reset

IR:

(None)

Reset

Applicable to both MAC and PHY

MM_RESET.request:

MM_RESET.confirm

PM_RESET.request:

PM_RESET.confirm

MAC Management Non-MIB Primitives

MM_SCAN.request (scan_parameters)

MM_SCAN.confirm

MM_POWER_MGT.request (power_mgt_parameters)

MM_POWER_MGT.confirm

Summary: PHY Management SAP Primitives

PM_GET.request

PM_GET.confirm

PM_SET.request

PM_SET.confirm

PM_RESET.request

PM_RESET.confirm

Summary: MAC Management SAP Primitives

MM_GET.request			MM_SCAN.request

MM_GET.confirm			MM_SCAN.confirm

MM_SET.request			MM_POWER_MGT.request

MM_SET.confirm			MM_POWER_MGT.confirm

MM_RESET.request

MM_RESET.confirm

Motion: accept Document 11-95/118 for inclusion in the 802.11 draft.