IEEE 802.9
 Wireless IS LAN MAC and PHY

IEEE 802 Tutorial
Tuesday evening -- July 8, 1997

Chandos A. Rypinski, LF
LACE, Inc. and Ubiquity Communication, Inc.

Introduction -- Part I

Goal:  New Wireless IS LAN MAC and PHY for 802.9 IS LAN
(IS = Integrated Services)

Use of new NII Band frequency space--200 MHz at 5.25 GHz

Consider for differentiation:

World-wide developments of Wireless ATM

Completion of IEEE 802.11 Standard

Action Request--write/message to Dhadesugoor Vaman, the Chairman of 802.9:
 I / we support the formation of a Study Group to address the possibility of a PAR for a Wireless MAC and PHY for 802.9.  Depending upon the direction taken, it is probable that (my organization) would participate in an effort to develop such a standard.

Service Definition at User Station

Packet LAN services

802 LLC higher layer interface, and at this point:

Successful transfers of errorless packets at wireline probability

Low access delay (<1.5 msec) and high transfer rate after access (16 Mbps)

Connection-type services

ISDN/Telecom-based higher layers with on-demand up to 24/30 B channels one or two-way

Future capacity reservation

Low through-system transfer delay (<6 msec including quantization delay)

System Suitability Definition

Near 100% area coverage within a building and nearly that within a campus

Intensive reuse of the channels for high Mbps per hectare/acre

Interference-limited radio system design

Robust rather than high bps/Hz radio modulations

One radio infrastructure for all supported services

External WAN Interconnectability Supported

Telecom ISDN (PRI) and customary transports (T-1, T-3, SONET)

Router Ports for 100BaseT and possibly FDDI

ATM UNI at selected transport interfaces (future)

Markets and Applications

In and out-of-building access to both external LAN, internet and telecom networks where ever that function is useful

School, university, commercial and manufacturing campii or individual premises

Wireless gateways to any existing private or public network

Fast setup facilities for convention centers, disasters or construction sites

Value of Extending 802.9

802.9 is the primary Integrated Services group in 802 at workstation interface level

There is no difference in the services provided by 802.9 now relative to those of a new PAR

802.9 has defined an interface between a user station and a physical medium where a central manager serves multiple physical medium ports

802.9 has already dealt with localizing the standard to a station interface when there is a multiport central machine external to the scope of the standard

802.9 is more likely to recognize need for an ATM upward interface than pure LAN groups

Why Not Extend 802.11?

802.11 has decided that their use of the NII band will use their existing MAC including distributed logic and LBT, but with modifications for increased medium transfer rate.

802.11 has no provision for telecom connection-type services

802.11 has no provision for central coordination of many channel sharing access points

In this radio band, a variant of HIPERLAN /1 is an existing standard; and it might be a better MAC for an LBT access method with distributed logic

Do WAND and HIPERLAN /2 make this project redundant?

WAND (Wireless ATM Network Demonstrator) is the European wireless ATM development.  ETSI RES 10 HIPERLAN /2 is the development of the physical layer.

The headline statement will be true when and if PC’s commonly execute ATM setup logic.  Winsock 2 is a step in this direction.  When the general purpose PBX’s use an ATM rather than an ISDN interface, it is here.

The proposal is that stations use legacy protocol stacks, and that the formal transition to ATM, when required, comes at a central hub equipment

Request for Action:

Address the Chairman of IEEE 802.9:
	Professor Dhadesugoor Vaman               <vaman@ati.stevens-tech.edu>

In writing use words like the following:

I / we support the formation of a Study Group to address the possibility of a PAR for a Wireless MAC and PHY for 802.9.  Depending upon the direction taken, it is probable that (my organization) would participate in an effort to develop such a standard.

Signature and organizational identification

Technology--Part II

Segmentation is Inevitable and Beneficial

The 802.9 Protocol Stack Now (Figure)

The MAC function should be common to both Packet and Connection bearing cells

The 802.9 Protocol Stack After Adding a Wireless PHY/MAC (Figure)

The Local Connection Concept

Protocol Requirement for 90% Capacity Utilization

Radio Propagation Problems Influencing MAC

Important Details

Anticipation of Changes in NII Band FCC Rules

Segmentation is Inevitable and Beneficial

Segmentation to a 48 octet payload corresponds to a 12 millisecond accumulation delay at a 32 Kbps channel rate.

The access delay experienced for packets and connections is a multiple of the average holding time per channel use

802.11 “fragments” packets to 256 octets for transmission

The shorter the segment the higher the probability of error-free reception and the less channel time invested in unusable transmission--and the higher the overhead

For peer-to-peer communication where peers may or may not be served by the same access point, no reassembly of segments is necessary for local relay

The 802.9 Protocol Stack Now

There are separate LLC and MAC’s for packet and connection type services

The two stacks are use separate multiplexed space in the PHY frame

The modem and line functions are common to both

A Common MAC Function for Both Packet and Connection Bearing Cells

All of the present IS Protocols (802.6, 802.9 and Telecom SDH) are an isochronous medium where time slots are dedicated to either packets or connections using a physical medium multiplexer

Priority and queue management are more efficient using a common space rather than a fixed partition into one space for each service

The total amount of logic equipment is reduced by shared rather than independent MAC’s

The 802.9 Protocol Stack After Adding a Wireless PHY/MAC

There are still two LLC and higher level interfaces for packets and connections

The two services are separately segmented, multiplexed and sent as a common stream to the MAC

There is now one common MAC and PHY

The Local Connection Concept

Stations talk to the central Hub to request service and use of the radio medium

After setup, station-originated connections and packets are repeated either to a second connection/path to an external network or to another station within the system

Segmented packets are treated as a connection with a duration of one packet length between station and Hub

Connection type services include bounded size reservation of future capacity managed by the Hub where the reservation is not that of a particular time slot

Protocol Requirement for 90% Capacity Utilization

To achieve near 100% of capacity utilization, it is necessary that access for service requests be near out-of-band and near non-blocking

The function must be that of Erlang C blocking to aid in calculation of probable wait delay as a function of traffic loading

The delay experienced for both packets and cells is a multiple of the average holding time for each individual use of the channel--short bursts are essential to low access delay

The channel(s) must be as large as possible for a given pool of users

Radio Propagation Problems Influencing MAC

High inherent non-random error rate from multipath and interference

Variability of user station location and resulting propagation path

Need for access point diversity requires suspension of principle:
 “only one path at a time to any user station”

Variable path to user station must be shielded from outside networks

Important Details

Forward error correction

MAC level repeat send

Positive ACK for all packet segments

NACK and one retry for connection segments

Modulation method optimized for resistance to like-signal interference

Transmitters are ON only when in use

Anticipation of Changes in NII Band FCC Rules

The WINForum SRDS Committee is working on sharing rules

Results will be incorporated in a future filing with FCC

It is improbable that LBT will be either required or prohibited

Probably, there will be defined channeling 20-25 MHz

There might be duty cycle or transmitter ON time limitations

There will almost surely be additional restrictions on out-of-band radiation