IEEE P802.11
Wireless LANs

Lucent/Harris TGb proposal comparison matrix input

Date:	           June, 25, 1998

Author: 	Jan Boer / Carl Andren

Input for the comparison matrix provided by Lucent and Harris for their compromise proposal.

General description:

| Lucent/Harris |
| --- |
|  | Modulation Technique |

16-CCK

complementary code keying

| 16 chip spreading |
| --- |
|  | Data Rate(s) |
| 1,2,5 and 10 Mbit/s |
|  | Sensitivity |

-91 dBm @ 5Mbit/s

| -88 dBm @ 10Mbit/s |
| --- |
|  | Reference submissions |

Harris MBOK doc

70254,
70867,
71447,
80467B,
80477B, 97/124
Lucent PPM doc

98/10r1
98/11
98/99
98/100

Combined doc

98/246 new doc

98/xxxx draft text

Receiver structure:

| Lucent/Harris |
| --- |
|  | Receiver structure description |

Matched filter

Decoding simple with Hadamar transforms

simple DFE possible to increase performance

|  | RF/IF complexity relative to current low rate PHYs. |
| --- | --- |
| Same as low rate PHYs |
|  | Baseband processing complexity. relative to current low rate PHYs. (Gate Count, MIPS) |

twice low rate PHYs for moderate complexity receiver, with MF (not required)

| complexity trade off for performance |
| --- |
|  | Equaliser Complexity and performance impact (if applicable). |
| 40K gates. Will improve delay spread from 100 ns to 300 ns. This is roughly double the gate count |
|  | Antenna Diversity and performance impact. |
| Same possibilities as low rate PHY with long PLCP header. |

Multipath and Noise performance:

| Lucent/Harris |
| --- |
|  | PER vs. multipath RMS delay spread (no noise). Delay spread @ 10% PER for 64 and 1000 byte packets. |

10 Mbit/s

RAKE

64 byte:  90 ns

1K byte:  65 ns

RAKE-ISI Equaliser

64 byte:  144 ns

1K byte:  87 ns

RAKE-ICI/ISI Equaliser

64 byte:  333 ns

1 kbyte:  226 ns

5 Mbit/s

RAKE

64 byte:  235 ns

1 kbyte:  180 ns

RAKE-ISI Equaliser

64 byte:  450 ns

1 kbyte:  380 ns

RAKE-ICI/ISI Equaliser

| This configuration is not needed |
| --- |
|  | PER vs. thermal noise w/ multipath @ 10% PER. Eb/No @ 20% PER for 64 and 1000 byte packets. |

10 Mbit/s

RAKE

64 byte:  15.2 dB

1 kbyte:  17.5 dB

RAKE-ISI Equaliser

64 byte:  15 dB

1 kbyte:  17.5 dB

RAKE-ICI/ISI Equaliser

64 byte:  15.5 dB

1 kbyte:  17.7 dB

5 Mbit/s

RAKE

64 byte:  15 dB

1 kbyte:  17 dB

RAKE-ISI Equaliser

64 byte:  16 dB

1 kbyte:  18 dB

RAKE-ICI/ISI Equaliser

| Not needed |
| --- |
|  | PER vs. thermal noise (no multipath). Eb/No @ 10% PER for 64 and 1000 byte packets. |

10 Mbit/s

RAKE

64 byte:  5.5 dB

1 kbyte:  7 dB

RAKE-ISI Equaliser

64 byte:  5.5 dB

1 kbyte:  7 dB

RAKE-ICI/ISI Equaliser

64 byte:  5.5 dB

1 kbyte:  7 dB

5 Mbit/s

RAKE

64 byte:  5.5 dB

1 kbyte:  7 dB

RAKE-ISI Equaliser

64 byte:  5.5 dB

1 kbyte:  7 dB

RAKE-ICI/ISI Equaliser

64 byte:  5.5 dB

1 kbyte: 7 dB

Carrier and Data frequency accuracy:

| Lucent/Harris |
| --- |
|  | Required Carrier frequency accuracy. |

25 PPM

| = low rate PHYs |
| --- |
|  | Degradation at worst case carrier frequency offset. |

Negligible  with carrier tracking

Similar to low rate PHYs

| Easy carrier tracking, but non coherent processing OK |
| --- |
|  | Data clock frequency accuracy. |
| 25 PPM |
|  | Degradation at worst case data clock frequency offset. |

CMF gives optimal timing

Tracking circuits should compensate

Overhead related parameters:

| Lucent/Harris |
| --- |
|  | Preamble length |

Long preamble + header = 192 microseconds

| Short preamble + header = 75 microseconds |
| --- |
|  | Does the preamble length include receive antenna diversity? Yes or no. |
| Long preamble, same as low rate PHY: yes Short preamble: yes 30 Microseconds (1.5 slottime) reserved for diversity |
|  | Does the preamble length include equaliser training? Yes or no. |

Long preamble: yes

Short preamble: yes (24 microseconds reserved)

|  | Slot time. |
| --- | --- |

= low rate PHY

| 20 microseconds |
| --- |
|  | CCA mechanism description. |
| = low rate PHY |
|  | Co-Channel signal detection time. |

Energy detect time = current PHY

| 15 microseconds |
| --- |
|  | RX/TX turnaround time. |

= low rate PHY

| 5 microseconds. |
| --- |
|  | SIFS. |

= low rate PHY

10 microseconds

Spectral efficiency, Cell density related parameters:

| Lucent/Harris |
| --- |
|  | Channelization scheme |
| = low rate PHY |
|  | Cell planing scheme |

= low rate PHY

| 3 independent channels |
| --- |
|  | Adjacent channel interference rejection. |
| 32-35 dB |
|  | Co-channel interference rejection. |
| 6dB |
|  | S/J where CW interference gives 10% PER. |
| 8 dB at 10 Mbit/s, 5 dB with 5 Mbit/s |
|  | Other interference immunity tests. |
| GFSK immunity is the same as CW |
|  | Co-Channel signal detection time. |
| = low rate PHY |
|  | Total number of channels in 2.4GHz band. |

=  low rate PHY, 3 colocated channels for FCC or ETSI

Total tuneable channels:

| FCC: 11 ETSI: 13 MTP: 1 |
| --- |
|  | Aggregate throughput. |

Dependent on cell topology.

e.g. three channels in one cell gives 3 * throughput or 30 Mbit/s

Misc. critical performance factors:

| Lucent/Harris |
| --- |
|  | Phase noise sensitivity |
| comparable to low rate PHY (QPSK) |
|  | RF PA backoff |
| 4-5dB |
|  | DC power consumption |

Comparable to low rate PHY

PCMCIA form factor and spec.

TX < 300mA @ 3V

RX < 250A @ 3V

Interoperability:

| Lucent/Harris |
| --- |
|  | Interoperability / Co-existence strategy with current low rate PHYs |

Long Preamble: interoperable and coexistent

Optional short preamble: low rate PHY is coexistent with transmitter using short preamble

and high rate receiver recognises both long and short preamble : interoperable

| Interoperable with FH using FH header |
| --- |
|  | Is the proposal Interoperable at the data level? |
| Yes |
|  | Is the proposal Interoperable at the antenna level? |
| yes |
|  | Performance penalty due to Interoperability / Coexistence. |

Long preamble: 192 micro PHY overhead

Short preamble: overhead reduces with factor 3

General Information:

| Lucent/Harris |
| --- |
|  | Has the submission of the required IEEE letter covering IP been made? Yes or No |
| yes |
|  | Applicable patent numbers |
| none |
|  | Point of contact |

Lucent:

Bruce Tuch

Lucent Technologies

PO Box 755

3430 AT Nieuwegein, The Netherlands

tel: +31 30 6097527

fax: +31 30 6097556

Al Petrick

Harris Semiconductor

PO Box 883

Melbourne, FL 32905

tel: 407-729-4944

fax: 407-724-7886