IEEE P802.11
Wireless LANs

QPSK modulation for 5GHz-band Wireless LANs (Draft Text)

Date:	January 19, 1998

Author:	Kazuhiro OKANOUE, Yoshikazu KAKURA, Tomoki OHSAWA
	NEC Corporation
	4-1-1, Miyzaki, Miyamae-ku, Kawasaki, Kanagawa, 216 JAPNA
	Phone: +81 44 856 2255
	Fax: +81 44 856 2230
	e-Mail: {okanoue,kakura,ohsawa}@ccm.CL.nec.co.jp

Abstract

This document describes draft specifications for a QPSK modulation system for 5GHz band high speed wireless LANs PHY. Simulation results and discussions for the specifications are also described.

1.

Modulation

1.1.	Modulator

The proposed system provides 20Mbit/s based on single carrier with QPSK modulation (SC system). The modulation method uses the phase constellation shown in Figure  1. The binary data stream entering the modulator, bm, is converted by serial-to-parallel converter into two separate binary streams (Xk) and (Yk). Starting from bit 1 in time of stream bm, all odd numbered bits form stream Xk and all even numbered bits form stream Yk. The digital data sequences (Xk) and (Yk) are encoded onto (Ik) and (Qk) according to;

.

The signals Ik and Qk can take one of two values +/-2-1/2, resulting in the constellation show in Figure  1.

Figure  1 Phase contellation

Impulses Ik, Qk are applied to the inputs of the I & Q baseband filters. The baseband filters shall have linear phase and square root raised cosine frequency response of the form:

,

where T is the symbol period, 80nsec. The roll-off factor, a, determines the width of the transmission band and is 0.5. Figure  2 is for explanatory purposes and does not prescribe a specific implementation.

Figure  2 implementation example

The resultant transmitted signal s(t) is given by:

where g(t) is the pulse shaping function, wc is the radian carrier frequency, T is the symbol period. Any methods which generate the specified s(t) may be used.

1.2.	Transmit Spectrum Mask

The transmitted spectral products shall be less than (TBD)  dBc for fc – (TBD) MHz < f < fc + (TBD) MHz and fc +(TBD) MHz < f < fc + (TBD) MHz and –(TBD) dBc for f < fc – (TBD) MHz and f > fc +(TBD)  MHz where fc is the channel center frequency.  The transmit spectral mask is shown in Figure  3.

Figure  3 Transmit spectral mask

1.3.	Transmit Center Frequency Tolerance

The transmission center frequency tolerance shall be +/- 20 ppm maximum.

(Simulation results and discussion)

Figure  4 and Figure  5 demonstrates packet error rates in static channel and multipath environment for 64-byte packets with AFC. It is shown that thermal noise degrades AFC capability seriously. We consider that a PLL for a whole packet duration will improve the degradation.

Figure  4 PER v.s. frequency offset in static channel

Figure  5 PER v.s. frequency offset in multipath environment

1.4.	Transmit Power On and Power Down Ramp

Figure  6 shows a mask of The transmit power on ramp and power down ramp during transmission.

Figure  6 Power mask during transmission

1.5.	Transmit Modulation Accuracy

The transmit modulation accuracy for the SC PHY shall be based on the difference between the actual transmitted waveform and the ideal signal waveform. The ideal transmitter and receive filters in cascade from a raised cosine Nyquist filter having an impulse response going through zero at symbol period intervals, so there is no intersymbol interference at the ideal sampling points. The ideal signal samples S(k) can be represented as follows;

Let Z(k) be the complex vectors produced by observing the real transmitter through an ideal measuring receiver filter at instants k, one symbol period apart. Then Z(k) can be represented with S(k) as:

,

where

W=e dr+jra : accounts for  both frequency offset giving “da” radians per symbol phase rotation and an amplitude changes of “dr” nepers per symbol;

C0 is a constant origin offset representing quadrature modulator imbalance;

C1 is a complex constant representing the arbitrary phase and output power of the transmitter, and

E(k) is the residual error on sample S(k).

The sum square vector error is then:

C0, C1 and W shall be chosen to minimize this expression and are then used to compute the individual vector errors E(k) on each symbol. The symbol timing phase of the receiver output samples used to compute the vector error shall also be chosen to give the lowest value.

The value of MAX and MIN are:

MIN : 1 (The first symbol of preamble) and

MAX: the number of the last symbol of a transmitted.

The RMS vector error is then computed as the square root of the sum-square vector divided by the number of symbols in the packet. The RMS error in any packets shall be less than TBD.

2.	Receiver specfication

2.1.	Sensitivity

The Frame Error Rate (FER) shall be less than 10% at an PSDU length of 1000 bytes for an input level of –74 dBm measured at the antenna connector.

(Simulation Results and assumptions): Figure  7 demonstrates PER v.s. Eb/N0 for a static channel. It is shown that PER less than 10% can be achieved at Eb/N0 more than 11dB with out FEC. The sensitivity requirements are based on noise floor of –174 dBm/Hz, +74dB for transmission bandwidth, noise figure +10dB,  Eb/N0=+11dB and an implementation margin of +5dB. The cording gain (about 2dB) is not counted for.

Figure  7 P.E.R. vs Gaussian Noise

2.2.	Multipath rejection

The Frame Error Rate (FER) shall be less than 10% in a multipath fading environment of which delay spread is less than 140nsec without any additive Gaussian noise.  The FER shall be less than 20% in the multipath fading environment at Eb/No larger than 22 dB.

(Simulation results):

Figure  8 FER v.s. Delay spread

Figure  9 PER v.s. Eb/N0 in multipath environment

2.3.	Adjacent Channel Rejection

Adjacent channel rejection performance is defined as the minimum desired channel to a undeidired adjacent channel signal power ratio (DUR) that causes the PER equal to or less than 10%. The minimum DUR shall be equal to or greater than  (TBD) dB.

(Simulation result and discussion)

Figure  10 shows PER performance in the conditions where an adjacent channel is exiting. When ideal root nyquist filters for a transmitter and a receiver and an ideal linear amplifier filters are adopted, degradations of PER are negiligible at DURs larger than –30dB against an adjacent channel of 18.75MHz separation. We need to study PERs for more realistic filters and amplifiers.

Figure  10 PER v.s. adjacent channel

2.4.	Co-channel rejection

Co-channel rejection performance is defined as the minimum desired channel to a undeidired adjacent channel signal power ratio (DUR) that causes the PER equal to or less than 10%. The minimum DUR shall be equal to or greater than  (TBD) dB.

(Simulation result and discussion)

Figure  11 shows PER performance in the conditions where an co-channel interference is exiting. Receiver can achieve PER less than 10% at desired-to-undesired ratio (DUR) of 20dB.

Figure  11 PER v.s. Co-channel interference

2.5.	Jamming rejection

Under simulation!

3.	Overhead related parameters

3.1.	Preamble and structure

Figure  12 shows a proposed frame format. The PLCP Preamble consists of 124 symbols in a SYNC field and 8 symbols in a SFD (Start Frame Delimiter) field. The PLCP header includes both a 8-symbol header error check filed and a 6-symbol PSDU length word.  The rest 2 symbols in the PLCP header are used for PLCP control information.

Figure  12 Frame Format

The SYNC filed is basically formed as a repetition of the 64-bit sequence, SEQ64. The SEQ64 can be represented based on the Xk and Yk in section 0, as follows;

SEQ64=(X0Y0X1Y1  X2Y2X3Y3  …  X30Y30X31Y32)

=(1111 1111 1111 0000 1111 0011 0011 0000 1100 0000 0000 1111 0000 1100 1100 0000).

Figure  13 shows an auto correlation functions of a sequence obtained by converting SEQ64 based on XkYk -> IkQk conversion rule described in section Figure  13.

Figure  13 autocorrelation function

Figure  14 shows a structure of SYNC field. A receiver executes antenna selection, AGC (Automatic Gain Control) setup, AFC (Automatic Frequency Control) setup and channel impulse response estimation through the SYNC filed. A typical usage of the SYNC filed is also described in Figure  14.

Figure  14 structure of SYNC field

3.2.	Slot size

Slot size is defined as a summation of CCATime, RxTxTurnaroundTime, AirPropagationTime and MACProcessingTime.  The RxTxTurnarroundTime is obtained as a summation of TxPLCPDelay, RxTxSwitchTime, TxRampOnTime and TxRFDelay. The CCATime includes CCADetectTime and RxRFDelay. The proposed Slot size is TBD. Details are shown in Table  1.

3.3.	SIFS time

SIFS time is obtained as a summation of RxRFDelay, RxPLCPDelay, MACProcessingDelay and RxTxTurnaroundTime. The proposed SIFS time is TBD. Detail is also shown in Table  1.

| CCATime | CCADetectTime | <1usec | <5usec |
| --- | --- | --- | --- |
|  | RxRFDelay | 4usec |
|  | RxPLCPDelay | about 2.5usec |
| RxTxTurnaroundTime | TxPLCPDelay | 1usec | TBD |
|  | RxTxSwitchTime | TBD |
| TxRampOnTime | TBD |
| TxRFDelay | 1usec |
|  | AirPropagationTime | TBD |
| MACProcessingTime | 2usec |

Table  1 detail of Slot size calculation

3.4.	CCA detection mechanism

As a CCA detection mechanism, we propose to adopt envelope detection mechanism as shown in Figure  15. When an averaged envelope level of received signals gets over the threshold level (TBD), the CCA detector detects that the medium is busy.

Figure  15 CCA detection mechanism

(Simulation Results and Discussions): A CCA detection error rate with 4-symbol averaging is described in Figure  16. In the figure, the real and the dotted lines show the detection errors, which means that

a receiver detects that the medium is not busy though a packet has been transmitted (miss detection) and

a receiver detects that the medium is busy though a packet has not been transmitted (false detection)

respectively. Threshold level is defined as a relative value of Gaussian noise lebel. From the figure,  the proposed method achieve both of the detection errors less than 10% when signal-to-noise ratio (SNR) is 5 dB and threshold is 16dB.

Figure  16 CCA detection error rate

4.	Channel Coding

The channel error control for all bits in PSDU employs the BCH code of which block and information lengths are 31 and 26 ((31,26) BCH code), respectively. The (31,26) BCH code has a error correction capability against bit errors less than or equal to 2 bits in each block. The (31,26) BCH encoder outputs coded PSDU. Figure  17 shows a procedure of the channel encoding. The PSDU is divided into blocks of 208 bits from the first bit of the PSDU. When the length of PSDU is not multiple of integer and 26, 0s shall be added to the top of the last block for padding. Each block, PSDU[i],  is encoded by a (31,26) BCH encoder and added 47 bits as redundant information, R[i], and stuff bit, S[i], for even parity. The coded PSDU is constructed by concatenating all of PSDU[i] and R[i] as shown in Figure  17. For the padded block, al of the additional 0’s shall be removed from the encoder output to construct the coded PSDU.

Figure  17 Encode procedure

Figure  18 shows a procedure of the channel decoder. The coded PSDU is divided into blocks of 32 bits from the first bit of the coded PSDU. When the length of encoded PSDU is not multiple of integer and 32, 0s shall be added to the top of the last block for padding. Each block, coded PSDU[i],  is decoded by a (31,26) BCH decoder after removing its stuff bit. The PSDU is constructed by concatenating all of decoded PSDU[i] as shown in Figure  18. For the padded block, al of the additional 0’s shall be removed from the output of the decoder.

Figure  18 Decode procedure

5.	Channellization plan

5.1.	U-NII band

Table  2 shows a channelization plan for U-NII band. 14 channels are proposed.

| Channel # | Center frequency [MHz] | Power Limits |
| --- | --- | --- |
| 1 | 5162.5 | Low power (< 50mW) |
| 2 | 5181.25 | Low power (< 50mW) |
| 3 | 5200.0 | Low power (< 50mW) |
| 4 | 5218.75 | Low power (< 50mW) |
| 5 | 5237.5 | Low power (< 50mW) |
| 6 | 5262.5 | Medium power (< 250mW) |
| 7 | 5281.25 | Medium power (< 250mW) |
| 8 | 5300.0 | Medium power (< 250mW) |
| 9 | 5318.75 | Medium power (< 250mW) |
| 10 | 5337.5 | Medium power (< 250mW) |
| 11 | 5746.875 | High power (<1W) |
| 12 | 5765.625 | High power (<1W) |
| 13 | 5784.375 | High power (<1W) |
| 14 | 5803.125 | High power (<1W) |

Table  2 Carrier frequency in U-NII band

Figure  19, Figure  20 and Figure  21 show channel allocation scheme for each band based on the Table  2.

Figure  19 Channel allocation in 5150-5250 MHz band

Figure  20 Channel allocation in 5250-5350 MHz band

Figure  21 Channel allocation in 5725-5825 MHz band

In these figures, it is assumed to use a non-linear amplifier shown in Figure  22 with 3dB backoff.

Figure  22 non-linear amplifier characteristic