## Slide 1: FEC Frame Formats for 802.11a
John M. Kowalski
Sharp Laboratories USA
Camas, Washington
(360) 817-7520
kowalskj@sharplabs.com

## Slide 2: Outline
Motivation
General Requirements
Tradeoff of Where Coding is done
Timing Issues with 802.11a PHY
Conclusions
Proposed Coding

## Slide 3: Motivation
Adding an outer code option with the 802.11e/802.11a PHY would:
Greatly expand the market for 802.11 devices
Allow existing infrastructure networks to perform more reliably
Address competition from other wireless home network solutions
Facilitate delay/jitter management for QoS

## Slide 4: General Requirements
Provide less than 1 frame (PSDU) error in 10 hours ( or P[error] < 1.15X10-9 for 1000 octet packets.)
Minimal overhead
Be compatible with OFDM symbol sizes
Be consistent with 802.11/802.11a SIFS timing rules
Be friendly to known AV formats
Be friendly to any aggregation proposals.

## Slide 5: Tradeoff of Where Coding is Done (1)

## Slide 6: Tradeoff of Where Coding is Done (2)
1
1. P[PLCP Header Failure]  3.15 X10-4 at specified MDSL
at 6 Mbps. At higher rates, (due to higher MDSL)
this falls of drastically.

## Slide 7: Tradeoff of Where Coding is Done (3)

## Slide 8: Timing Issues in 802.11A (1)
In 11a, aMACProcessingDelay < 2s to do:
  FCS
  Check control field and address field to decide whether to ACK.
Cannot be done before PHY-RXEnd.indicate
Must be done in time to issue PHY-TXStart.request for ACK so that beginning of ACK preamble reaches transmit antenna within ±10% of SIFS time.

## Slide 9: Timing Issues in 802.11A (2)
Issue: it may not be feasible to use a decoder that decodes within aMACProcessingDelay
However we can use delayed ACK/Unacknowledged frames
  Can this be used in enhanced DCF?

## Slide 10: A Proposed Coding Format
IV=initialization vector
ICV= integrity check vector
RS coding assumed

## Slide 11: Proposed Coding Format
Other codes, e.g., RS(204, 188) work well, but are do not have small least common multiples of 48.
Codes that are multiples of 48 work well with MPEG-2, DVD (k can be any fixed number on which the group agrees, e.g., RS(64,48)).
This format has benefits for aggregated MPDU’s with TS packets: higher layers can selectively retry.
Smaller code sizes for smaller PDU sizes can improve channel efficiency.

## Slide 12: Conclusions
For AV applications, delayed ACK/unacknowledged service OK.
Requirements can be met at high data rates, (higher MDSL), where they would be used anyway.
We would prefer this ASAP (i.e., in the MAC), but we want to make sure any potential issues are addressed.