| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Paging and Ranging Mechanisms for M2M Network Re-Entry |
| Date Submitted | 2011-03-11 |
| Source(s) | Ping-Heng Kuo, Wei-Chieh Huang, Yu-Tao Hsieh, Pang-An Ting ITRI | E-mail: pinghengkuo@itri.org.tw |
| Re: | Call for contributions from Rapporteur Group ‘Power’ |
| Abstract | This contribution provides a method to distribute ranging opportunities among different M2M devices and groups, in order to alleviate the anticipated congestions of network re-entry. |
| Purpose | To be discussed and adopted by 802.16p WG |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Paging and Ranging Mechanisms for M2M Network Re-Entry

Ping-Heng Kuo, Wei-Chieh Huang, Yu-Tao Hsieh, Pang-An Ting

ITRI

# Introduction

Severe congestions can be envisaged in M2M network re-entry, since potentially a large number of devices would attempt to perform ranging simultaneously. Actuated by this anticipation, a number of contributions submitted to 802.16p PWR RG suggested that the access opportunities should be distributed among M2M devices and groups. Specifically, the network could assign different ranging parameters to devices using paging or some other MAC messages.

This contribution proposes a ranging parameter assignment mechanism, based on a look-up table that shall be pre-configured at both ABS and M2M device. The look-up table is consisted of multiple sets of ranging parameters, and each of the sets is associated with an index dubbed as ranging instruction index (RII). By including the index value in the paging message, the ABS could provide M2M devices the ranging information that is to be used. With this mechanism based on a look-up table, the overhead required by ranging parameters assignments could be reduced.

On the other hand, in some emergency events, the M2M server may need to immediately communicate with a specific device, or a group of devices, that are currently idle. For examples:

1. The server has an urgent need to read the environmental measurement data collected by a group of sensors.

2. The server is required to send an urgent instruction to switch on/off a group of M2M devices in certain emergencies.

In order to handle such scenarios, we also introduce “urgent paging mode” in this contribution. When this mode is triggered, M2M devices are notified via the paging message. Then, if the device is not within the paging list, it should wait for a certain interval of time before attempting to initiate ranging for its voluntary network re-entry (if any) operation. Therefore, the network is able to page specific devices to perform ranging for network re-entry without interruptions.

# Text proposal for inclusion in the 802.16p AWD

# Blue underlined text: New text to be added.

# Green underlined text: Text with consensus in C802.16p-11/0002 (PWR RG output).

# [Bracketed Green highlighted text: Text without consensus in C802.16p-11/0002 (PWR RG output).]

# Stroke-out Red text: Text to be removed.

--------------------------------- Start of Proposed Text Part 1 ---------------------------------

16.2.3.X AAI-PAG-ADV

| Field | Size (bits) | Value/Description | Condition |
| --- | --- | --- | --- |
| Num_PAG_GRP | TBD | The number of M2M groups to be paged. |  |
| URG_PAG_triggering | 1 | 0b0: Normal paging mode 0b1: Urgent paging mode. Any of devices or groups should delay the ranging operation of its voluntary re-entry for a time interval [interval length is TBD], unless it is included in the paging list. |  |
| For (j=0; j<Num_PAG_GRP; j++) { |  |  |  |
| Group ID | TBD | M2M Group ID |  |
| Action Code | 1 | 0b0: Perform network re-entry 0b1: Perform location update |  |
| Ranging Instruction Index (RII) | TBD | The devices should use the ranging parameters correspond to the assigned RII in accordance to Table xxx. | Present if network re-entry is required (Action Code = 0b00). |
| } |  |  |  |

--------------------------------- End of Proposed Text Part 1 ---------------------------------

--------------------------------- Start of Proposed Text Part 2 ---------------------------------

16.2.18.7.X Network re-entry from idle mode for M2M devices

[An M2M device [which is individual or belongs to one M2M group] may perform network reentry from idle mode voluntarily for UL transmission. Network also may request the M2M device [or M2M group] to perform network reentry from idle mode by transmitting a paging message.] For network reentry from Idle Mode, ranging parameters may be different for [distinct] among M2M devices, or among M2M groups [to avoid the network access congestion].

Based on the information indicated in the received paging message, M2M devices should map the given ranging instruction index (RII) value with Table xxx, in order to determine the ranging parameters to be used for network re-entry.

| Ranging Instruction Index (RII) | Ranging Parameters |
| --- | --- |
| 0 | TBD |
| 1 | TBD |
| 2 | TBD |
| …. | TBD |
| TBD | TBD |

Table xxx: Ranging instructions for network re-entry

When the urgent paging mode is triggered, any device that is not in the paging list while intending to initiate ranging for voluntary network re-entry, should delay the ranging operation for a time interval. The devices can switch back to normal mode and commence the ranging operation for voluntary network re-entry once the waiting time is expired.

--------------------------------- End of Proposed Text Part 2 ---------------------------------