| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Multicast transmission in IEEE P802.16p |
| Date Submitted | 2011-11-06 |
| Source(s) | Jeongki Kim, Youngsoo Yuk, Giwon Park, Inuk Jung, Jinsam Kwak LG Electronics | Email: jeongki.kim@lge.com |
| Re: | IEEE 802.16-11/0027, IEEE 802.16 Working Group Letter Ballot #33 |
| Abstract | This contribution proposes the text for resource allocation of multicast data transmission in IEEE P802.16p |
| Purpose | For discussion in 802.16p TG and adoption in to the IEEE P802.16p AWD |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Multicast transmission in IEEE P802.16p

Jeongki Kim, Youngsoo Yuk, Giwon Park, Inuk Jung, Jinsam Kwak

LG Electronics

# Introduction

In IEEE 802.16REV3/D1 a CID (e.g., basic CID, transport CID for unicast service, multicast CID for multicast service (MBS), etc.) is used in DL/UL MAP IEs to assign the DL/UL allocation to MSs. However, in 16p multicast service the multicast CID cannot be reused to allocate the M2M multicast burst because of the insufficiency of CID space (Total number is 95: 0xFEA0 – 0xFEFE in Table 658). According to the definition of MGID in P802.16p/D1, an MGID only is assigned to a multicast service flow. In this case MGID can be used in multicast MAP IE and MAC header to transmit the multicast data.

So, we propose the new DL extended IE (i.e., M2M Multicast Assignment IE) which is used to allocate the resource of M2M multicast burst based on the MGID and an MGID related to the multicast burst is included in the new extended IE. Instead of CID the MGID will be included in the MAC header of multicast MPDU.

# Text proposal

---- Start of proposed text ----

[Remedy #1: Add the following subclause 8.4.5.3.2:]

8.4.5.3.2 DL-MAP Extended IE format

8.4.5.3.2.3 DL-MAP Extended-3 IE encoding format

Modify Table 409 as Indicated

Table 409—Extended-3 DIUC code assignment for Extended-2 DIUC = 15

| Extended-3 DIUC (hexadecimal) | Usage |
| --- | --- |
| 0x0 | Power Boosting IE |
| 0x1 | MR DL-MAP Monitor IE |
| 0x2 | DL_Burst_Transmit_IE |
| 0x3 | OFDMA Periodic_Channel_Measurement_IE |
| 0x4 | M2M multicast assignment IE |
| 0x45-0xF | Reserved |

[Remedy #2: Add the subclause 8.4.5.3.xx:]

Add new subclause 8.4.5.3.xx as indicated

8.4.5.3.xx M2M Multicast Assignment IE format

In the DL-MAP, a BS shall transmit the M2M Multicast Assignment MAP IE to indicate the DL allocation in which M2M Multicast data is sent.

Table xxx—M2M Multicast Assignment IE format

| Syntax | Size (bit) | Notes |
| --- | --- | --- |
| M2M Multicast Assignment IE(){ | - | - |
| Extended-2 DIUC | 4 | M2M Multicast Assignment IE () = 0xF (Extended-3 DIUC) |
| Length | 8 | Length in bytes |
| Extended-3 DIUC | 4 | 0x04 |
| MGID | 15 |  |
| DIUC | 4 |  |
| OFDMA Symbol Offset | 8 | The offset of the OFDMA symbol measured in OFDMA symbols from beginning of the DL frame in which the DL-MAP is transmitted. Counting from the frame preamble and starting from 0 |
| Subchannel offset | 7 | The offset of the first OFDMA symbol of the MBS region measured in OFDMA symbols from beginning of this DL frame |
| No. Subchannels | 7 |  |
| NO. OFDMA symbols | 7 |  |
| Boosting | 3 | Refer to Table 321 |
| Repetition Coding Indication | 2 | 0b00—No repetition coding 0b01—Repetition coding of 2 used 0b10—Repetition coding of 4 used 0b11—Repetition coding of 6 used |
| if !(byte boundary) { |  |  |
| Padding Nibble | variable | Padding to reach byte boundary |
| } |  |  |
| } | - | - |

[Remedy #3: Add the following texts at the end of the 6.3.34 as following:]

6.3.34 Support of multicast operation for machine to machine application

A BS shall send an M2M Multicast Assignment IE to allocate the resource of the multicast burst. The multicast burst carries a multicast MPDU including an MGID. In this case, the MGID is added at of the M2M multicast MAC header in the multicast MPDU.

6.3.34.1 M2M multicast operation in idle mode

…

[Remedy #3: Add the subclause 6.3.2.1.1.2 as following:]

6.3.2.1.1.2 M2M multicast MAC header format

M2M multicast MAC header is illustrated in Figure xx.

Figure xx – M2M multicast MAC header format

---- End of proposed text ----