| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | MS Network Entry for RS Groups |
| Date Submitted | 2007-09-17 |
| Source(s) | Israfil Bahceci, Senarath Gamini, Peiying Zhu, Wen Tong, Mo Han Fong, Derek Yu, David Steer, Mark Naden Nortel Networks 3500 Carling Avenue Ottawa, Ontario K2H 8E9 | Voice: +613-763-1315 E-mail: wentong@nortel.com E-mail: pyzhu@nortel.com |
| Re: | IEEE P802.16j/D1: IEEE 802.16j working group letter ballot #28 |
| Abstract | MS Network entry procedures through RS group are proposed |
| Purpose | To incorporate the proposed text into the P802.16j/D1 Baseline Document |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

MS Network Entry for RS Groups

Israfil Bahceci, Senarath Gamini, Peiying Zhu, Wen Tong, Hang Zhang, Mo Han Fong, Derek Yu, David Steer, Mark Naden

Nortel Networks

# Introduction

Network entry procedures for an MS through a virtual RS group are described.in this Section after the recent modifications to network entry procedures through the contribution IEEE.802.16j/459r4.

# Proposed Text Changes

++++Begin Text Changes++++++++

[Delete the text in Subclause 6.3.9.16.3.1.1 ]

Remedy 1:

{Enter the following Sentence in Section 6.3.7 RS Grouping}

For both transparent and non-transaprent RS Groups, the MS network entry procedure and the associated initial ranging procedure  shall be the procedure for the transparent RSs specified in Subclause 6.3.10.3.1.1 for the systems with transparent RSs.  The  periodic ranging procedure for the RS groups shall follow the procedure adopted in Subclause 6.3.9.16.3.4

Remedy 2:

{Enter the following Sentence in Section 6.3.10.3.1.1  at the end of the section on Transparent RSs}

For both transparent and non-transparent RS Groups, the MS network entry procedure and the associated initial ranging procedure shall be the procedure for the transparent RSs specified in above for the systems with transparent RSs.

++++End Text Changes++++++++