| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Comments on SS ranging and network entry in transparent and non-transparent mode |
| Date Submitted | 2007-09-20 |
| Source(s) | Erik Colban NextWave Broadband Inc [add other co-authors here] | Voice: +1 858 480 3240 ecolban@nextwave.com |
| Re: | IEEE 802.16j-07/043: “IEEE 802.16 Working Group Working Group Letter Ballot #28” |
| Abstract | This contribution proposes clarifications to the reference model. |
| Purpose | Text proposal for 802.16j Draft Document. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Clarifications to the reference model for Multihop Relay

Erik Colban, NextWave Broadband Inc.

Introduction

The reference model section 1.4.3 needs to clarify that wherever the standard specifies communication between an SS and a BS, the entity on the BS side in direct communication with the SS could be an MR-BS, one or more RSs, or an MR-BS and one or more RSs, and messages and other signals exchanged between the BS and the SS may be fully processed by the entity or entities in direct communication with the SS or be relayed to one or more other entities.

Proposed Changes

In section 1.4.3, make the following changes:

1.4.3 Multihop relay

Multihop Relay (MR) is an optional deployment by which a BS may be replaced by a Multihop Relay BS (MR-BS) and one or more Relay Stations (RS). Wherever this standard specifies communication between an SS and a BS, the entity on the BS side in direct communication with the SS may be an MR-BS, one or more RSs, or an MR-BS and one or more RSs, and messages and other signals exchanged between the BS and the SS may be fully processed by the entity or entities in direct communication with the SS or be relayed to one or more other entities for processing.