| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Virtual MIMO communication |
| Date Submitted | 2007-11-07 |
| Source(s) | Anubala Varikat Sasken Communication Technologies Ltd. Vishwanatha Rao Thumparthy Sasken Communication Technologies Ltd. Krishnamurthy Giridhar IIT Madras, India | Voice: +91 80 6694 3057 E-mail: anubala.varikat@sasken.com viswam@sasken.com giri@tenet.res.in |
| Re: | IEEE 802.16m-07/040 Call for Contributions on Project 802.16m SDD |
| Abstract | Description of virtual MIMO communication with co-operation between subscriber stations for both the uplink and the downlink |
| Purpose | Proposal for consideration in the 802.16m SDD |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Virtual MIMO communication

Anubala Varikat, Vishwanatha Rao Thumparthy, Krishnamuthy Giridhar

Sasken Communication Technologies Ltd.

Functionalities that support Virtual MIMO (VMIMO) communication with co-operation between subscriber stations are suggested for 802.16m and for inclusion in the SDD.

# Description of the concept

According to the proposed Virtual MIMO technique, Subscriber Stations (SSs) in the vicinity of each other form clusters and act as antennas for each other for MIMO communication with a multiple antenna base station. This will require a means for communication between two SSs. Using the scheme, an unlimited number of antennas can theoretically be used by an SS, and dramatic improvement in spectral efficiency is expected.

# Support required in the standard

Support for at least 8 antennas on the BS and for 8 x 8 MIMO communication is suggested.

Suitable resources will need to be provided for the inter-SS communication. A separate time zone is allocated for the communication, called the IL (Inter-SS Link) zone, so as to easily ensure backward compatibility with 802.16e. Higher order modulation schemes, higher rate coding schemes and shorter cyclic prefixes are required on the IL zone.

Location information of the SSs will enable efficient spatial re-use of the resources used for the inter-SS link for both centralized and localized resource allocation schemes. To help in certain localized resource allocation schemes, location information of SSs is made available on the DL-MAP when the operation is in VMIMO mode.

The number of SSs available in the vicinity for formation of a virtual MIMO cluster would change continuously, and the BS needs to be informed continuously of the number of antennas available even when in open loop MIMO mode. Uplink messaging is introduced to notify the BS of the number of antennas with which an SS will communicate at a point in time when in VMIMO mode.