| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Enhanced Multicast Broadcast Service with Multicarrier Support |
| Date Submitted | 2008-05-05 |
| Source(s) | Kelvin Chou, Yih-Shen Chen, I-Kang Fu and Paul Cheng MediaTek Inc. No.1, Dusing Rd. 1, HsinChu Science-Based Industrial Park, HsinChu, Taiwan 300, R.O.C. | Kelvin.Chou@mediatek.com Yihshen.Chen@mediatek.com IK.Fu@mediatek.com |
| Re: | IEEE 802.16m-08/016, “Call for Contributions on Project 802.16m System Description Document (SDD)”. In response to the following topics: • Comments on the entire content of IEEE 802.16m-08/003r1 |
| Abstract | This contribution presents the scenarios of enhanced multicast broadcast service with multicarrier support. |
| Purpose | To be discussed and adopted by TGm for the 802.16m SDD. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Enhanced Multicast Broadcast Service with Multicarrier Support

Kelvin Chou, Yih-Shen Chen, I-Kang Fu and Paul Cheng

MediaTek Inc.

# Introduction

With the support of multiple RF carriers, the BS can provide MBS on dedicated RF bands other than its primary/unicast bands. The advantage is to provide more stable bandwidth resources for MBS without interleaving with the normal unicast transmission. A BS which has multiple MBS zone IDs for different MBS services can either multiplex multiple MBS IDs on a single RF band or dedicate one band for each MBS zone. The MS with multiple RF carriers may maintain its normal operations with the serving BS while join the MBS zone using another RF carrier.

For example, as seen in Figure 1, BS1 has three frequency bands. RF1 and RF2 are dedicated to MBS zone 1 and zone 2 respectively, while RF3 serves as the unicast band (the primary band). BS2 provides only two frequency bands. Therefore it multiplexes the traffic of MBS zone 1 and zone 2 on RF1 and provides unicast services on RF2. MS1 has only one RF module and hence its MBS traffic interleaves with its unicast traffic. MS2 and MS3 both have two RF modules. Therefore, each of them dedicates one RF carrier for MBS and the other RF carrier for the unicast services.

Figure 1. Dedicated RF carriers for MBS

During inter-MBS zone transition, the MS with multiple RF carriers can keep its existing MBS flows uninterrupted and perform MBS zone switch operations, such as MCID/LCID update, via another RF carrier. After the MS has successfully joined the target MBS, its old serving BS may be informed, either by the MS or by the target BS via backbone networks, to prune the MS.

Figure 2. Seamless inter-MBS zone transition

# Proposed Text for SDD

[In 80216m-08_003, Section 15, add the following text]

-------------------------------  Text Start  ------------------------------------------------------------------------------------

# 15.x Enhanced MBS with Multicarrier Support

With the support of multiple RF carriers, the BS can provide MBS on dedicated RF bands other than its primary/unicast bands. The advantage is to provide more stable bandwidth resources for MBS without interleaving with the normal unicast transmission. A BS which has multiple MBS zone IDs for different MBS services can either multiplex multiple MBS IDs on a single RF band or dedicate one band for each MBS zone. The MS with multiple RF carriers may maintain its normal operations with the serving BS while join the MBS zone using another RF carrier.

During inter-MBS zone transition, the MS with multiple RF carriers can keep its existing MBS flows uninterrupted and perform MBS zone switch operations, such as MCID/LCID update, via another RF carrier. After the MS has successfully joined the target MBS, its old serving BS may be informed, either by the MS or by the target BS via backbone networks, to prune the MS.

-------------------------------  Text End  ------------------------------------------------------------------------------------