| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Enhanced HARQ Technique for Multiple Antennas Transceiver |
| Date Submitted | 2008-07-07 |
| Source(s) | Tao Wu, Yinwei Zhao, Qi Li, Hongjie Si, Chongli Liu Huawei | Voice: 86-755-28970182 E-mail: liuchongli@huawei.com |
| Re: | IEEE 802.16m-08/024 - Call for Contributions on Project 802.16m System Description Document (SDD), for “Hybrid ARQ” topic. |
| Abstract | This document proposes an enhanced HARQ technique for multiple antennas transceiver. |
| Purpose | For discussion and approval by TGm. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Enhanced HARQ Technique for Multiple Antennas Transceiver

Tao Wu, Yinwei Zhao, Qi Li, Hongjie Si, Chongli Liu

Huawei

# Introduction

This proposal provides an enhanced method for HARQ transmission for multiple antennas transceiver. The method inherits the design of STC sub packet combing in 802.16e [1] and makes an enhancement by introducing interference cancellation to spatial diversity scenarios. Simulation result shows that the proposed scheme outperforms the current design.

# Background

A HARQ-CC (Chase Combing) scheme with multi-antenna transmission has been accepted in the existing 802.16 standard [1] .The current STC-HARQ scheme is based on the assumption that the channel is quasi static in the successive transmission. Because the successive two transmission symbols form an Alamouti spatial time code, the HARQ CC sub packet combing performance has been enhanced obviously.

In our proposal, we follow the same assumption and introduce a self-interference cancellation processing to STC HARQ for space diversity scenario to enhance the performance.

# Proposed Method

Take D-STTD re-transmission as an example to demonstrate our method. Table 4 shows the design for D-STTD re-transmission:

Table 1-STC subpacket combining (4-Tx antenna D-STTD case)

|  | Initial transmission | Odd retransmission | Even retransmission |
| --- | --- | --- | --- |
| Spatial time code incremental redundancy for D-STTD |  |  |  |

The received signal of the first transmission with 2 receiving antennas can be expressed as the following formula:

The received signal of the second transmission can be expressed as the following formula:

Respectively, where  represents the channel response from ith transmitting antenna to jth receiving antenna in kth transmission,

represents the transmission signals,

represents the noise in the jth receiving antennas and kth transmission.

Consider the evaluation ofby ZF (zero forcing) in the first and second transmission:

According to the assumption in 802.16e standard, the channel in the successive transmission could be considered as a slowly variable channel. To simplify the analysis, we assume that . If we combine the evaluation of and , the interference from, to  will be cancelled and the performance will be improved significantly. Although the actual channel is not static, our scheme will still have significant gain in slowly variable channel.

The method can be extended to 3-Tx Matrix B with antenna grouping in 802.16e standard. The detailed design is shown in table 5.

Table 2-STC subpacket combining (3-Tx Matrix B with antenna grouping case)

|  | Initial transmission | Odd retransmission | Even retransmission |
| --- | --- | --- | --- |
| Spatial time code incremental redundancy |  |  |  |

# Simulation results

Link-level simulation assumptions are listed in Table 3

Table 3 Simulation Assumptions

| Number of Rx/Tx Antennas | Rx=4，Tx=4 |
| --- | --- |
| FFT Size | 512 |
| CP Ratio | 1/8 |
| Code Type | Turbo 1/3 |
| Channel estimation | LS Linear interpolation |
| Channel model | Pedestrian B 3 km/h |
| Scheme comparison | 16e D-STTD HARQ | First: Second: |
|  | Proposed D-STTD HARQ | First: Second: |

# Conclusion

In this proposal, an extended STC HARQ design has been proposed and the performance would be improved significantly.

# Reference

[1] Standard for Local and metropolitan area networks Part 16: Air Interface for Broadband Wireless Access Systems, P802.16Rev2/D4 (April 2008)

# Text Proposal to SDD

------------------------------------Start text proposal------------------------------------

[Adopt the following text in the P802.16m System Description Document (SDD)]

*.*.*.* STC subpacket combining

Table *-STC subpacket combining (3-Tx Matrix B with antenna grouping case)

|  | Initial transmission | Odd retransmission | Even retransmission |
| --- | --- | --- | --- |
| Spatial time code incremental redundancy |  |  |  |

Table *-STC subpacket combining (4-Tx antenna D-STTD case)

|  | Initial transmission | Odd retransmission | Even retransmission |
| --- | --- | --- | --- |
| Spatial time code incremental redundancy for D-STTD |  |  |  |

------------------------------------End text proposal------------------------------------