| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Power Control Scheme supporting Non-Orthogonal Superposition |
| Date Submitted | 2008-07-7 |
| Source(s) | Juergen Otterbach, Joerg Schaepperle Alcatel-Lucent | E-mail: Juergen.Otterbach@alcatel-lucent.de, Joerg.Schaepperle@alcatel-lucent.de, *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | Call for Contributions (80216m-08_024.pdf)on Project 802.16m System Description Document (SDD) Specific Topic Power Control |
| Abstract | Proposal for Power Control to support Superposition in Multi User Applications |
| Purpose | To be considered and discussed by TGm and adopted as text for the SDD to Session #56 |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Power Control Scheme supporting Non-Orthogonal Superposition

Juergen Otterbach,, Joerg Schaepperle 
Alcatel-Lucent

# References

[1] 802.16m System Requirements Document IEEE 802.16m-08/002r4

[2] Call for Contribution:  http://ieee802.org/16/tgm/docs/80216m-08_024.pdf

[3] IEEE 802.16m-08/003,  http://ieee802.org/16/tgm/docs/80216m-08_003r3.pdf 
     “The Draft IEEE 802.16m System Description Document”

Introduction

Multi-User MIMO mode will be supported according to §5.7 [1]. Different users share the same radio resource in DL and/or in UL. One scenario to realize Multi-User MIMO is to use non-orthogonal superposition of different user bursts on the same radio resource (frequency/time allocation).

Proposal

In 16e standard there are today means for power control in different modes of operation

CDMA codes:

RNG-RSP with power level adjust for initial ranging during Network Entry

Periodic Ranging and BR transmission (to do Bandwidth Request)

Data Burst:

Table 512—Normalized C/N per modulation for adaptation to C/N per MCS

Closed Loop and Open Loop Power Control

In the 16m system, mechanism should to be implemented supporting individual power levels for non-orthogonal superposition of different user signals:

DL power:

Power control mechanism for individual non-orthogonal user bursts by control of weighted sum of BS output. Each mobile should provide individual measurement per non-orthogonal user burst in DL for reports using the feedback to the Base Station

Downlink Structure:

For DL transmission up to 4 different orthogonal streams are supported in 16m by pilot structure. For non-orthogonal superposition two simultaneous data streams with the same or different MCS may be transmitted on the same radio resource.

UL power:

Closed loop power control mechanism using layer individual power adjust commands

Open loop power control using knowledge of layer specific path loss information in the MS

Data and Pilot subcarrier individual leveling for non-orthogonal superposition

Uplink Structure:

For 16e in uplink the user bursts are controlled by the BS Power Control to have same power density at the common UL RX in the BS if using the same MCS.

To support non-orthogonal superposition in UL, different input power targets for UL at the antenna input connector of the BS per layer are required.

We propose to install a mechanism providing configurable pilot power boosting in uplink.

The pilot tone power of 0, 3 or 6 dB above the per data tone power according to the number of orthogonal pilot patterns shall be further modified by a flexible value from the set {-2.5 dB; 0 dB; 2.5 dB; 5 dB} TBD.

Different pilot boosting values can be chosen for different layers. This variable pilot boosting can e.g. be used to mitigate the pilot interference from different layers and depends on the scenario.

# Text Proposal for SDD

-------------------------------  Text Start  ---------------------------------------------------

10 Medium Access Control Sub-Layer

10.x Power Control

10.x.x DL Power Control

Power control in DL supports Multi-User MIMO applications. If the transmission in Multi-User MIMO is using superposition of non-orthogonal signals the Tx signal is a weighted sum of signals for multiple users sharing the same OFDMA resource. The weight shall be adjustable within a specific range.

10.x.y UL Power Control

Power control in UL supports Multi-User MIMO applications.

Variable pilot boosting values are signaled to each terminal.

Uplink transmissions by two non-orthogonal superposed signals are on a shared OFDMA resource. The control of each signal is done by individual UL power offset adjustments provided by the DL Control Structure.

11 Physical Layer

11.6 DL Control Structure

11.6.2.3.1.2 User-specific control information

In case of non-orthogonal superposition in DL, the user specific control information includes the transmit power allocated to each different user signal.

For uplink transmission the user specific control information includes additional user specific transmit power offsets to be used by the terminals only when transmitting in UL allocations reserved for non-orthogonal superposition.

-------------------------------  Text End  ---------------------------------------------------

# Abbreviations

BS	Base Station

CINR	Carrier-to-Interference and Noise Ratio

CN	Carrier to Noise Ratio

DL	Down Link

MCS	Modulation and Coding Scheme

MS	Mobile Station

UL	Up Link