| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Clean-up of TTG/RTG and Irregular Subframe in IEEE 802.16m SDD and Amendment Working Document |
| Date Submitted | 2009-01-12 |
| Source(s) | Jaeweon Cho, Hokyu Choi, Samsung Electronics Co., Ltd. Sean McBeath Huawei Technologies Mo-Han Fong Nortel Networks Sassan Ahmadi Intel Corporation Sungho Moon, Jin Sam Kwak LG Electronics | +82-31-279-5796 jaeweon.cho@samsung.com smcbeath@huawei.com mhfong@nortel.com sassan.ahmadi@intel.com msungho@lge.com |
| Re: | IEEE 802.16m-08/052, “Call for Comments and Contributions on Project 802.16m System Description Document (SDD)”. Target topic: Call for Comment on the SDD draft (IEEE 802.16m-08/003r6; Section 11.3, 11.4, 11.5, 11.6). IEEE 802.16m-08/053r1, “Call for Comments and Contributions on Project 802.16m Amendment Working Document”. Target topic: Call for Comment on Amendment Working Document Text (IEEE 802.16m-08/050; Section 15.3.2, 15.3.3, 15.3.5). |
| Abstract | The contribution proposes to change TTG/RTG lengths and irregular subframe structure defined in the current 802.16m SDD draft and Amendment working document, in order that 802.16m BS shall smoothly support a mix of 802.16m and legacy MSs on the same RF carrier. |
| Purpose | To be discussed and adopted by TGm for the 802.16m SDD and Amendment Working Document. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Clean-up of TTG/RTG and Irregular Subframe in 
IEEE 802.16m SDD and Amendment Working Document

Jaeweon Cho, Hokyu Choi

Samsung Electronics Co., Ltd.

Sean McBeath

Huawei Technologies

Mo-Han Fong

Nortel Networks

Sassan Ahmadi

Intel Corporation

Sungho Moon, Jin Sam Kwak

LG Electronics

# Problem Statement and Suggested Remedy

In the current draft of 802.16m SDD [1] and Amendment working document [2], TTG and RTG are secured in the following way:

- TTG

  - By puncturing the last one OFDMA symbol in the last DL subframe

  - Hence, its length is fixed to one OFDMA symbol time.

- RTG

  - An idle time in a frame is utilized for RTG.

However, such way has a problem that TTG/RTG is not compatible with legacy system, i.e. not the same lengths as defined in WiMAX Forum Mobile System Profile, R1.0 [3]. The TTG/RTG lengths in 802.16m SDD [1] and in WiMAX Profile R1.0 [3] are listed up and compared in the table below.

| Bandwidth (MHz) | TTG (s) | RTG (s) |
| --- | --- | --- |
|  | SDD (1symbol) | WiMAX R1.0 | SDD (idle time) | WiMAX R1.0 |
| 5/10/20 | 102.857 | 105.714 | 62.86 | 60 |
| 8.75 | 115.2 | 87.2 | 46.4 | 74.4 |
| 7 | 144 | 188 | 104 | 60 |

We can see a large difference in the TTG/RTG values between the two documents. Such difference has a direct impact on legacy support operation at 802.16m BS. To solve this problem, we suggest the following changes to both 802.16m SDD draft [1] and Amendment working document [2]:

- Change the lengths of TTG and RTG to the same values defined in WiMAX Profile R1.0.

- Change 6-symbol subframe with idle symbol (type-1 short subframe) to 5-symbol subframe

  - It is noted that to allow TTG with a different length from one symbol time, 5-symbol subframe is need to be defined.

# Proposed Text Changes in IEEE 802.16m SDD [1]

[Remedy 1: Replace Table 2 in page 60 with the following Table (Note: This new table includes also numerology of 1/16 CP for 7MHz, 8.75MHz and 1/4 CP proposed by comment #318 and #320, respectively, in IEEE 802.16m-09/0002.)]

| Nominal Channel Bandwidth (MHz) | 5 | 7 | 8.75 | 10 | 20 |
| --- | --- | --- | --- | --- | --- |
| Over-sampling Factor | 28/25 | 8/7 | 8/7 | 28/25 | 28/25 |
| Sampling Frequency (MHz) | 5.6 | 8 | 10 | 11.2 | 22.4 |
| FFT Size | 512 | 1024 | 1024 | 1024 | 2048 |
| Sub-Carrier Spacing (kHz) | 10.937500 | 7.812500 | 9.765625 | 10.937500 | 10.937500 |
| Useful Symbol Time Tu (µs) | 91.429 | 128 | 102.4 | 91.429 | 91.429 |
| Cyclic Prefix (CP) Tg=1/8 Tu | Symbol Time Ts (µs) | 102.857 | 144 | 115.2 | 102.857 | 102.857 |
|  | FDD | Number of OFDM symbols per Frame | 48 | 34 | 43 | 48 | 48 |
|  |  | Idle time (µs) | 62.857 | 104 | 46.40 | 62.857 | 62.857 |
|  | TDD | Number of OFDM symbols per Frame | 47 | 33 | 42 | 47 | 47 |
|  |  | TTG + RTG (µs) | 165.714 | 248 | 161.6 | 165.714 | 165.714 |
| Cyclic Prefix (CP) Tg=1/16 Tu | Symbol Time Ts (µs) | 97.143 | 136 | 108.8 | 97.143 | 97.143 |
|  | FDD | Number of OFDM symbols per Frame | 51 | 36 | 45 | 51 | 51 |
|  |  | Idle time (µs) | 45.71 | 104 | 104 | 45.71 | 45.71 |
|  | TDD | Number of OFDM symbols per Frame | 50 | 35 | 44 | 50 | 50 |
|  |  | TTG + RTG (µs) | 142.853 | 240 | 212.8 | 142.853 | 142.853 |
| Cyclic Prefix (CP) Tg=1/4 Tu | Symbol Time Ts (µs) | 114.286 |  |  | 114.286 | 114.286 |
|  | FDD | Number of OFDM symbols per Frame | 42 |  |  | 42 | 42 |
|  |  | Idle time (µs) | 199.98 |  |  | 199.98 | 199.98 |
|  | TDD | Number of OFDM symbols per Frame | 42 |  |  | 42 | 42 |
|  |  | TTG + RTG (µs) | 199.98 |  |  | 199.98 | 199.98 |

Table 2 OFDMA parameters for IEEE 802.16m

[Remedy 2: Change the text from line 19 on the page 60 to line 1 on the page 61, in 11.4.1., as follows:]

There are two three types of subframes depending on the size of cyclic prefix: 1) the type-1 subframe which consists of six OFDMA symbols, and 2) the type-2 subframe that consists of seven OFDMA symbols, and 3) the type-3 subframe which consists of five OFDMA symbols. In both subframe types, some of symbols may be idle symbols.

[Remedy 3: Change the text from line 17 to 20 on the page 61, in 11.4.1.1., as follows:]

Figure 25 illustrates an example TDD frame structure with DL to UL ratio of 5:3. Assuming OFDMA symbol duration of 102.857µs and a CP length of 1/8 Tu, the lengths of type-1 subframe and type-3 subframe is are 0.617 ms and 0.514 ms, respectively. In Figure 25, the last DL subframe, i.e., DL SF4, is a type-13 short subframe whose last OFDMA symbol is an idle symbol to accommodate the gap required to switch from DL to UL. TTG and RTG are 105.714 µs and 60µs, respectively.

[Remedy 4: Replace Figure 25 in page 62 with the following Figure]

Figure 25 Frame Structure with type-1 and type-3 subframes in TDD duplex mode (CP=1/8Tu)

[Remedy 5: Change the text from line 3 to 9 on the page 63, in 11.4.1.2., as follows:]

For nominal channel bandwidths of 5, 10, and 20 MHz, an IEEE 802.16m frame for a CP of 1/16 Tu shall have five type-1 subframes and three type-2 subframes for FDD, and six type-1 subframes and two type-2 subframes for TDD. The subframe preceding a DL to UL switching point shall be a type-1 subframe.

Figure 27 illustrates an example of TDD and FDD frame structure with a CP of 1/16 Tu. Assuming OFDM symbol duration of 97.143 μs and a CP length of 1/16 Tu, the length of type-1 and type-2 subframes are 0.583 ms and 0.680 ms, respectively. TTG and RTG are 82.853 µs and 60 µs, respectively.

[Remedy 6: Replace Figure 27 in page 63 with the following Figure]

Figure 27 TDD and FDD Frame Structure with CP of 1/16 Tu (DL to UL ratio of 5:3)

[Remedy 7: Change the text from line 6 to 11 on the page 74, in 11.5.1., as follows:]

A physical resource unit (PRU) is the basic physical unit for resource allocation that comprises Psc consecutive subcarriers by Nsym consecutive OFDMA symbols. Psc is 18 subcarriers and Nsym is 6 OFDMA symbols for type-1 subframes, and Nsym is 7 OFDM symbols for type-2 subframes, and Nsym is 5 OFDMA symbols for type-3 subframes. A logical resource unit (LRU) is the basic logical unit for distributed and localized groups. A LRU is 18*6 subcarriers for type-1 subframes, and 18*7 subcarriers for type-2 subframes, and 18*5 subcarriers for type-3 subframes. Note that the LRU includes in its numerology the number of pilots that are used in a PRU, and may include control information.

[Remedy 8: Change the text from line 5 to 6 on the page 75, in 11.5.2.1., as follows:]

Each PRU contains pilot and data subcarriers. The number of used pilot and data subcarriers depends on MIMO mode, rank and number of multiplexed AMS as well as the type of the subframe, i.e., type-1, or type-2, or type-3.

[Remedy 9: Change the text from line 4 to 6 on the page 80, in 11.5.3., as follows:]

The pilot pattern of the type-3 subframe consisting of 5 OFDM symbols is obtained by deleting the third OFDM symbol of the type-1 subframe. The pilot pattern of the type-2 subframe is obtained by adding the third OFDM symbol of the type-1 subframe to the end of the type-1 subframe.

[Remedy 10: Change the text from line 7 to 9 on the page 82, in 11.6.2.1, as follows:]

The number of used pilot and data subcarriers depends on MIMO mode, rank and number of multiplexed AMS and the type of resource allocation, i.e., distributed or localized resource allocations as well as the type of the subframe, i.e., type-1, or type-2, or type-3.

# Proposed Text Changes in Amendment Working Document [2]

[Remedy 1: Replace Table 647 in page 12 with the following Table (Note: This new table includes also numerology of 1/16 CP for 7MHz, 8.75MHz and 1/4 CP)]

Table 647 – OFDMA parameters

| The nominal channel bandwidth, BW (MHz) | 5 | 7 | 8.75 | 10 | 20 |
| --- | --- | --- | --- | --- | --- |
| Sampling factor, | 28/25 | 8/7 | 8/7 | 28/25 | 28/25 |
| Sampling frequency, (MHz) | 5.6 | 8 | 10 | 11.2 | 22.4 |
| FFT size, | 512 | 1024 | 1024 | 1024 | 2048 |
| Subcarrier spacing, (kHz) | 10.94 | 7.81 | 9.77 | 10.94 | 10.94 |
| Useful symbol time, (µs) | 91.4 | 128 | 102.4 | 91.4 | 91.4 |
| CP ratio, G = 1/8 | OFDMA symbol time, (µs) | 102.857 | 144 | 115.2 | 102.857 | 102.857 |
|  | FDD | Number of OFDMA symbols per 5ms frame | 48 | 34 | 43 | 48 | 48 |
|  |  | Idle time (µs) | 62.857 | 104 | 46.40 | 62.857 | 62.857 |
|  | TDD | Number of OFDMA symbols per 5ms frame | 47 | 33 | 42 | 47 | 47 |
|  |  | TTG + RTG (µs) | 165.714 | 248 | 161.6 | 165.714 | 165.714 |
| CP ratio, G = 1/16 | OFDMA symbol time, (µs) | 97.143 | 136 | 108.8 | 97.143 | 97.143 |
|  | FDD | Number of OFDMA symbols per 5ms frame | 51 | 36 | 45 | 51 | 51 |
|  |  | Idle time (µs) | 45.71 | 104 | 104 | 45.71 | 45.71 |
|  | TDD | Number of OFDMA symbols per 5ms frame | 50 | 35 | 44 | 50 | 50 |
|  |  | TTG + RTG (µs) | 142.853 | 240 | 212.8 | 142.853 | 142.853 |
| CP ratio, G = 1/4 | OFDMA symbol time, (µs) | 114.286 |  |  | 114.286 | 114.286 |
|  | FDD | Number of OFDMA symbols per 5ms frame | 42 |  |  | 42 | 42 |
|  |  | Idle time (µs) | 199.98 |  |  | 199.98 | 199.98 |
|  | TDD | Number of OFDMA symbols per 5ms frame | 42 |  |  | 42 | 42 |
|  |  | TTG + RTG (µs) | 199.98 |  |  | 199.98 | 199.98 |
| Number of Guard Sub-Carriers | Left | 40 | 80 | 80 | 80 | 160 |
|  | Right | 39 | 79 | 79 | 79 | 159 |
| Number of Used Sub-Carriers | 433 | 865 | 865 | 865 | 1729 |
| Number of Physical Resource Blocks (18x6) | 24 | 48 | 48 | 48 | 96 |

[Remedy 2: Change the text from line 36 to 41 on the page 14, in 15.3.3.1., as follows:]

There are two three types of subframes depending on the size of cyclic prefix:

1) the type-1 subframe which consists of six OFDMA symbols, and

2) the type-2 subframe that consists of seven OFDMA symbols, and

3) the type-3 subframe which consists of five OFDMA symbols. In both subframe types, some of symbols may be idle symbols.

[Remedy 3: Change the text from line 46 to 48 on the page 16, in 15.3.3.2.2., as follows:]

Figure 391 illustrates an example TDD frame structure with D:U = 5:3, which is applicable to the nominal channel bandwidths of 5, 10, and 20 MHz with G = 1/8. In Figure 391 the last DL subframe, i.e. DL SF4, is a type-3 subframe and the other subframes are type-1 subframes. TTG and RTG are 105.714 µs and 60µs, respectively.

[Remedy 4: Replace Figure 391 in page 17 with the following Figure]

Figure 391 Frame Structure with type-1 and type-3 subframes in TDD duplex mode 
for 5, 10, 20 MHz channel bandwidths (CP=1/8 Tb)

[Remedy 5: Change the text from line 41 to 55 on the page 17, in 15.3.3.3., as follows:]

For channel bandwidths of 5, 10, and 20 MHz, a FDD frame shall have five type-1 subframes and three type-2 subframes, and a TDD frame shall have six type-1 subframes and two type-2 subframes. The subframe preceding a DL to UL switching point shall be a type-1 subframe.

In the TDD frame, the first and last subframes within each frame shall be type-2 subframes. The last OFDMA symbol in a type-2 subframe preceding a DL to UL switching point shall be an idle symbol, which is used to accommodate the gap required to switch from DL to UL.

In the FDD frame, the first, fifth, and last subframes within each frame shall be type-2 subframes.

Figure 392 illustrates an example of TDD and FDD frame structure with a CP of 1/16 Tb. Assuming OFDMA symbol duration of 97.143 μs and a CP length of 1/16 Tb, the length of type-1 and type-2 subframes are 0.583 ms and 0.680 ms, respectively. TTG and RTG are 82.853 µs and 60 µs, respectively.

[Remedy 6: Replace Figure 392 in page 18 with the following Figure]

Figure 392 TDD and FDD Frame Structure with CP of 1/16 Tb (DL to UL ratio of 5:3)

[Remedy 7: Change the text from line 32 to 39 on the page 23, in 15.3.5.1., as follows:]

A physical resource unit (PRU) is the basic physical unit for resource allocation that comprises Psc consecutive subcarriers by Nsym consecutive OFDMA symbols. Psc is 18 subcarriers and Nsym is 6 OFDMA symbols for type-1 subframes, and Nsym is 7 OFDM symbols for type-2 sub frames, and Nsym is 5 OFDMA symbols for type-3 subframes. A logical resource unit (LRU) is the basic logical unit for distributed and localized resource allocations. A LRU is Psc·Nsym subcarriers for type-1 subframes, and type-2 subframes, and type-3 subframes. The LRU includes the pilots in (ref. TBD) that are used in a PRU. The effective number of subcarriers in an LRU depends on the number of allocated pilots.

# References

[1] IEEE 802.16m-08/003r6, “The Draft IEEE 802.16m System Description Document”

[2] IEEE 802.16m-08/050, “IEEE 802.16m Amendment Working Document”

[3] WiMAX Forum™ Mobile System Profile, Release 1.0 Approved Specification (Revision 1.4.0:  2007-05-02)