| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed SDD Text for MIMO HARQ |
| Date Submitted | 2009-01-05 |
| Source(s) | Cheng-Ming Chen, Yu-Tao Hsieh, Pang-An Ting, Jen-Yuan Hsu, Zheng Yan-Xiu, Richard Li ITRI Tao Wu, Yinwei Zhao, Qi Li, Hongjie Si, Chongli Liu Huawei Technologies Du Ying CATR Wataru Matsumoto, Toshiyuki Kuze Mitsubishi Electric Corporation Philip V. Orlik, Andreas F. Molisch, Zhifeng (Jeff) Tao, Jinyun Zhang Mitsubishi Electric Research Laboratories Robert Novak, Sophie Vrzic, Dongsheng Yu, Hosein Nikopourdeilami, Mo-Han Fong, Kathiravetpillai Sivanesan Nortel Networks Yakun Sun, Jungwon Lee Marvell Semiconductor Inc. | ythsieh@itri.org.tw liuchongli@huawei.com duying@mail.ritt.com.cn Matsumoto.Wataru@aj.MitsubishiElectric.co.jp rnovak@nortel.com, mhfong@nortel.com yakunsun@marvell.com |
| Re: | In response to IEEE 802.16m-08/052 “Call for Contributions and Comments on Project 802.16m System Description Document (SDD)” |
| Abstract | This contribution proposes SDD text to support STC HARQ |
| Purpose | Discussion and adoption by TG m. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed SDD Text for MIMO HARQ

Cheng-Ming Chen, Yu-Tao Hsieh, Pang-An Ting,

Jen-Yuan Hsu, Zheng Yan-Xiu, Richard Li

ITRI

Tao Wu, Yinwei Zhao, Qi Li, Hongjie Si, Chongli Liu

Huawei Technologies

Du Ying

CATR

Wataru Matsumoto, Toshiyuki Kuze

Mitsubishi Electric Corporation

Philip V. Orlik, Andreas F. Molisch, Zhifeng (Jeff) Tao, Jinyun Zhang

Mitsubishi Electric Research Laboratories

Robert Novak, Sophie Vrzic, Dongsheng Yu,

Hosein Nikopourdeilami, Mo-Han Fong, Kathiravetpillai Sivanesan

Nortel Networks

Yakun Sun, Jungwon Lee

Marvell Semiconductor Inc.

Introduction

In current SDD document, there are no definitions on what retransmission formats are supported for retransmission. This contribution proposes texts to support general description of MIMO HARQ.

Text Proposal

------------------------------------------------Start of text -----------------------------------------------------------

## 11.3.2 HARQ

11.13.2.5 MIMO HARQ

For HARQ subpacket retransmission, the mapping of bits or modulated symbols to spatial streams may beapplied to exploit spatial diversity with given mapping pattern, depending on the type of IR. In this case, the predefined set of mapping patterns should be known to both transmitter and receiver. The specific mechanism is FFS and it should be determined with the consideration of MIMO architecture and data processing.

STC subpacket combining should be supported for HARQ and benefit the performance of low-mobility environments such as the femtocell, hot zone, etc. For the case of 2 transmit antennas, STC subpacket combining scheme specified in IEEE 802.16e is reused by IEEE 802.16m, or alternatively, is enhanced by using STC code mapping of only partial information for HARQ re-transmissions. For the cases of 3 transmit antennas and 4 transmit antennas, the current design in IEEE 802.16e is enhanced either by introducing interference cancellation to spatial diversity and spatial multiplexing scenarios, or introducing STC code mappings for subsequent HARQ transmissions to fully exploit the spatial diversity for all bits or modulated symbols, or by using STC code mapping of only partial information for HARQ re-transmissions.

------------------------------------------------End of text ------------------------------------------------------------