| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Comments on A-MAP IE to Support A-MAP Occurrence Indication and Secondary Carrier Activation |
| Date Submitted | 2009-03-02 |
| Source(s) | Chieh-Yuan Ho, Ming-Hsien Wu, Ching-Yao Huang, I-Kang Fu, Yih-Shen Chen, Paul Cheng NCTU/MediaTek | IK.Fu@mediatek.com thorpe.ho@mediatek.com cyhuang@faculty.nctu.edu.tw |
| Re: | IEEE 802.16m-09/0012, “Call for Contributions on Project 802.16m Amendment Working Document (AWD) Content” – Comments on P802.16m AWD |
| Abstract | According to P802.16m SDD, assigned secondary carriers will not always be activated for saving unnecessary MS processing power and signaling overheads. In addition, the MS also need to know which sub-frame the MS doesn’t need to decode A-MAP for sleep or co-located coexistence operations. This contribution suggests adding the relative parameters into the proper A-MAP IE. |
| Purpose | For member’s review and adoption into P802.16m Amendment Working Document |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Comments on A-MAP IE to Support A-MAP Occurrence Indication and Secondary Carrier Activation

Chieh-Yuan Ho, Ming-Hsien Wu, Ching-Yao Huang, I-Kang Fu, Yih-Shen Chen, Paul Cheng

National Chiao Tung University (NCTU) / MediaTek

- Introduction

In the latest P802.16m System Description Document (SDD), the carrier which may be potentially used by the AMS is defined as the assigned carriers. The assigned carriers are supposed to be determined based on ABS and AMS hardware capabilities. Among the assigned carriers, some of the carriers will be activated for data transmission based on system requirements and called the active carriers. Since the primary carrier will always be one of the active carriers, the secondary carriers of AMS may be activated or be de-activated from time to time.

In addition, the ABS should also let AMS know which sub-frames that AMS should decode the A-MAP. Otherwise AMS have to process the signals received during each sub-frame and decode all the A-MAP to see whether there exists its a-MAP IE. This will largely increase AMS complexity and power consumption. It will also disturb the multi-radio coexistence operation and possible sleep operation. Therefore, A-MAP should also transmit the proper IE to notify AMS in which sub-frames it should decode the A-MAP IEs.

In order to fulfill member’s classification on assigned carrier and active carrier, the stage 3 standard shall define proper procedure and messaging support for secondary carrier activation and de-activation. This contribution reviews the possible operations of secondary carriers and suggests the necessary input into SFH and A-MAP IE for enabling secondary carrier activation. The detail procedure will be further discussed and harmonized with TGm members.

- Suggested AMS Operations

- Proposed Text Input to P802.16m Amendment Working Document

---------------------------------------------------------Start of the Text-----------------------------------------------------------

[Add the following text into P802.16m Amendment Working Document]

----------------------------------------------------------End of the Text-----------------------------------------------------------