| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Text Modifications on the Section 15.3.5.2.1 Subband Partitioning |
| Date Submitted | 2009-03-02 |
| Source(s) | HanGyu Cho, Jin Sam Kwak E-mail : hgcho@lge.com LG Electronics |
| Re: | “802.16m AWD”: IEEE 802.16m-09/0012. ”Call for Contribution on Project 802.16m Amendment Working Document (AWD) Content” Target topic: Call for Comments on Amendment Working Document |
| Abstract | The contribution proposes the text modification on the Section 15.3.5.2.1 to be included in the 802.16m amendment. |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Text Modifications on the Section 15.3.5.2.1 Subband Partitioning

HanGyu Cho, Jin Sam Kwak

LG Electronics

# Introduction

This contribution proposes some editorial-like text modifications on the section 15.3.5.2.1 Subband Partitioning to provide clear and complete text and equation for the IEEE 802.16m Amendment.

# Text proposal for inclusion in the 802.16m amendment

----------------------------------------------------------- Text Start---------------------------------------------------------

Adopt only the modified text in below.

## Advanced Air Interface

### Physical Layer

#### Downlink Physical Structure

##### Multi-Cell Resource Mapping

###### Subband Partitioning

The physical PRUs are first divided into subbands and minibands; a subband comprises N1 adjacent PRUs and a miniband N2 adjacent PRUs, where N1=4 and N2=1. Subbands are suitable for frequency selective allocations as they provide a continuous allocation of PRUs in frequency. Minibands are suitable for frequency diverse allocation and are permuted in frequency.

The number of subbands is denoted by KSB. The number of PRUs allocated to subbands is LSB = N1*KSB. A 5-bit (TBD) field called Subband Allocation Count (SAC) field determines the value of KSB. The SAC is transmitted in the BCH. The remainder of the PRUs are allocated to minibands. The number of minibands in an allocation is denoted by KMB. The number of PRUs allocated to minibands is denoted by LMB, where LMB = N2*KMB. The total number of PRUs is denoted as NPRU where NPRU = LSB + LMB. The maximum number of subbands that can be formed is denoted as Nsub where Nsub = NPRU/ N1.

PRUs are partitioned and reordered into two groups of subband PRUs, PRUSB, and miniband PRUs, PRUMB. The set of PRUSB is numbered from 0 to (LSB-1) and the set of PRUMB are numbered from 0 to (LMB-1). Equation (174) defines the mapping of PRUs into PRUSB s. Equation (176) defines the mapping of PRUs to PRUMBs. Figure 399 illustrates the PRU to PRUSB and PRUMB mapping for a 5 MHz bandwidth with SAC equal to 3.

; 							(174)

where

(175)

where {x}mod{y} is modulus when dividing x by y and GCD(x,y) is the greatest common devisor of x and y.

,                              (176)

where

(177)

------------------------------------------------------------Text End---------------------------------------------------------