| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Harmonized text related to the "Recommended AWD Text Proposal #8" in "C80216m-09_0558.doc (Group Resource Allocation A-MAP IE) |
| Date Submitted | 2009-03-08 |
| Source(s) | Roshni Srinivasan, Shweta Shrivastava, Rath Vannithamby Intel Corporation Andrea Bacioccola Nokia Xin Qi, Shashikant Maheshwari, Xiaoyi Wang Nokia Siemens Networks Kevin Power Fujitsu Guan Yanfeng ZTE Corporation Jason Junsung Lim, Seho Kim Samsung Electronics Co., Ltd. | roshni.m.srinivasan@intel.com andrea.bacioccola@nokia.com kevin.power@uk.fujitsu.com guan.yanfeng@zte.com.cn junsung.lim@samsung.com |
| Re: | 802.16m AWD |
| Abstract | The contribution proposes text for DL Control Structure section for inclusion in the 802.16m amendment. |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Harmonized text related to the "Recommended AWD Text Proposal #8" in "C80216m-09_0558.doc (Group Scheduling A-MAP IE)

Roshni Srinivasan, Shweta Shrivastava, Rath Vannithamby, Intel Corporation;

Andrea Bacioccola, Nokia; Xin Qi, Shashikant Maheshwari, Xiaoyi Wang, Nokia Siemens Networks;

Kevin Power, Fujitsu; Guan Yanfeng, ZTE Corporation

Jason Junsung Lim, Seho KimSamsung Electronics Co., Ltd.

# Introduction

As suggested in comment 141 in 80216m-09_0014, this contribution addresses additional material related to the "Recommended AWD Text Proposal #8 " in "C80216m-09_0558.doc" or its latest revision.

# Text proposal for inclusion in the 802.16m amendment

-------------------------------  Text Start  ---------------------------------------------------

4. Abbreviations and acronyms

# DL Control Structure

# Advanced Preamble

# DL Control Channels

# Superframe Header

# Primary Superframe Header

# Secondary Superframe Header

# Advanced MAP (A-MAP)

# Non-user Specific A-MAP

# Assignment A-MAP

# HARQ Feedback A-MAP

# Power Control A-MAP

# Resource Mapping of DL Control Channels

# Superframe Header

# Primary Superframe Header

# Secondary Superframe Header

# Advanced MAP (A-MAP)

# Non-user Specific A-MAP

# Assignment A-MAP

# HARQ Feedback A-MAP

# Power Control A-MAP

# DL Control Information Elements

# Broadcast Control Information Elements

# P-SFH IE

# S-SFH IE

# Unicast Control Information Elements

# Non-user-specific A-MAP IE

# Assignment A-MAP IE

[  ------------------- Recommended AWD Text Proposal #8 --------------------]

      - Group Resource Assignment Allocation A-MAP IE

Group control information is used to allocate resources and/or configure resources to one or multiple mobile stations within a user group.

Group scheduling requires two operations

- Assignment of a user to a group. In order to add a user to a group in the DL or UL, the ABS shall transmit a [Group Configuration MAC management message] [Group Configuration A-MAP IE]

- Allocation of resources to users within a group. In order to assign resources to one or more users in a group, the ABS shall transmit the DL/UL Group Resource Allocation A-MAP IE. The DL/UL Group Resource Allocation A-MAP IE is included in user-specific resource assignment in an A-MAP region. The GRA A-MAP IE contains bitmaps to indicate scheduled users and also signal resource assignment, MCS, resource size. ABS may use GRA A-MAP IE to allocate DL resources to one or multiple mobile stations within a user group.

DL/UL Group Resource Allocation A-MAP IE

| Syntax | Size in bits * | Description/Notes |
| --- | --- | --- |
| A-MAP IE Type | [4] | TBD A-MAP IE types distinguish between UL/DL, SU/MU, OL/CL MIMO operation, persistent/non-persistent allocation, basic/extended IEs including GRA |
| Resource Offset | [6][8] | Indicates starting LRU for resource assignment to this group |
| ACID | TBD | TBD Required for explicit assignment of a single ACID group. Not required if implicit cycling of ACIDs starting from an initial ACID value is used as in 802.16e |
| HARQ ReTx Indicator | TBD | TBD Indicates whether this group resource assignment IE is for HARQ retransmissions or initial transmission |
| User Bitmap Size | [2][5] | TBD Size of the user bitmap; may not be needed if user bitmap size is included in configuration message/A-MAP IE |
| User Bitmap | Variable | Bitmap to indicate scheduled users in a group. The size of the bitmap is equal to the User Bitmap Size |
| Resource Allocation Bitmap descriptor | TBD | TBD MCS group type, packet/resource size type information or attributes required to decode resource assignment bitmap |
| Resource Assignment Bitmap | Variable | Bitmap to indicate MCS/resource size for each scheduled user |
| Padding | Variable | Padding to reach byte boundary |
| MCRC | [16] | 16 bit masked CRC |

[Editor’s Note: the bellowing IE is a placeholder for using a special type of A-A-MAP IE to configure a group, if tgm decide to use Mac Management Message for configuring a group, then this IE is not needed.].

      - [Group configuration A-MAP IE

Group configuration A-MAP IE is used for initiating and maintaining a group for resource assignment. ]

[  ----------------End of Recommended AWD Text Proposal #8 -----------------]

# HARQ Feedback A-MAP IE

# Power Control A-MAP IE

-------------------------------  Text End  ---------------------------------------------------