| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Text for the IEEE 802.16m AWD on HARQ Feedback Channel Index |
| Date Submitted | 2009-04-27 |
| Source(s) | Yujian Zhang, Hujun Yin, Yi Hsuan Intel Corporation | +86-10-82611515 {yujian.zhang,hujun.yin,yi.hsuan}@intel.com *<http://standards.ieee.org/faqs/affiliationFAQ.html |
| Re: | Category: AWD comments / Area: Chapter 15.3.6 (DL-CTRL) “Comments on AWD 15.3.6 DL-CTRL” |
| Abstract | Proposed text for HARQ Feedback Channel Index in P802.16m Amendment Working Document |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Text for the IEEE 802.16m AWD on HARQ Feedback Channel Index

Yujian Zhang, Hujun Yin, Yi Hsuan

Intel Corporation

# Introduction

The contribution proposes the text on HARQ Feedback Channel Index for 802.16m amendment [1]. The proposed text is developed so that it can be readily combined with IEEE P802.16 Rev2/D9 [2], it is compliant to the 802.16m SRD [3] and the 802.16m SDD [4], and it follows the style and format guidelines in [5]. Detailed design is given in [6].

# References

[1] IEEE 802.16m-09/0010r1a, “802.16m Amendment Working Document (AWD)”

[2] IEEE P802.16 Rev2/D9, “Draft IEEE Standard for Local and Metropolitan Area Networks: Air Interface 
for Broadband Wireless Access,” Jan. 2009.

[3] IEEE 802.16m-07/002r8, “802.16m System Requirements”

[4] IEEE 802.16m-08/003r8, “IEEE 802.16m System Description Document [Draft]”

[5] IEEE 802.16m-08/043, “Style guide for writing the IEEE 802.16m amendment”

[6] IEEE 802.16m-09/0947, “HARQ Feedback Channel Index”

# Text proposal for inclusion in the 802.16m amendment

------------------------------------------- Start of Proposed Amendment Text -----------------------------------------------

### 15.3.6.4.2.1 Non-user-specific A-MAP IE

Non-user-specific A-MAP IE consists of information that is not dedicated to a specific user or a specific group of users. It includes information required to decode assignment A-MAP IE. The size of the assignment A-MAP is indicated in the Non-user-specific A-MAP IE, in the unit of MLRUs. A-MAP IE also includes HF-A-MAP Index Parameter, which is used to indicate which transmission parameters are used to calculate HF-A-MAP index. The detailed information included in non-user specific information is TBD. The non-user specific A-MAP IE is shown in Table 660.

Table 660—Non-user specific A-MAP IE

| Syntax | Size [bits] | Notes |
| --- | --- | --- |
| Assignment A-MAP size | TBD | Indicate the size of assignment A-MAP in units of one or multiple MLRUs. |
| HF-A-MAP Index Parameter | 2 | Indicate which transmission parameters are used to calculate HF-A-MAP index. |

For each HF-A-MAP Index Parameter value j, the corresponding parameter set M(j)={mi} is as follows:

- 00: STID

- 01: STID, MCS

- 10: STID, Resource index

- 11: STID, Resource index, MCS

When HF-A-MAP index signaled in A-MAP is n, number of HF-A-MAPs configured is NHF-A-MAP, HF-A-MAP Index Parameter value is j, the associated HF-A-MAP index is .

--------------------------------------------- End of Proposed Amendment Text ----------------------------------------------