| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Text proposal on Quick Access Message Format and CDMA IE Allocation (AWD-15.2.11) |
| Date Submitted | 2009-07-06 |
| Source(s) | Jie Hui Yuan Zhu Xiangying Yang Intel | E-mail: xiangying.yang@intel.com |
| Re: | Category: AWD comments / Area: Chapter 15.2.11 |
| Abstract | This contribution proposes text for quick access message and CDMA IE Allocation format |
| Purpose | Adopt proposed text. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Text proposal on Quick Access Message Format and CDMA IE Allocation (AWD-15.2.11)

Jie Hui, Yuan Zhu, Xiangying Yang

Intel

- Introduction

The text change #1 in this contribution proposes details on quick access message contents to be included in Section 15.2.11.1.5.1 quick access message format of AWD.

The text change #2 propose removing Masking Indicator in CDMA_IE_allocation. Scrambling this 4-bit indicator can cause higher misdetection probability, while overhead saving is very marginal. It is suggested that this information is to carried in a regular field in the CDMA_IE_allocaiton

- Proposed Test

Text proposal #1

--------------------------------text#1 start-----------------------------------------------

15.2.11.1.5.1 quick access message format

When 3-step BW-REQ procedure is used, in step-1 the quick access message carries 12 bit information including MS addressing information with TBD quick access sequences carrying additional BW-REQ information. The information bits are defined in the following format.

[Add the following text]

Both the 12-bit quick access message and the selected BWREQ preamble index out of total 24 (FFS) sequences carry BWREQ related information. The 10bit MS BWREQ-ID is carried in quick access message. The BWREQ-ID is allocated during network entry. The quick access sequence selection is generated by a pseudo-random function (taking values from 0~23) of frame number, BWREQ-ID and input Selection-ID (also taking values from 0~23). Given a frame number and BWREQ-ID, the quick access sequence is a one-to-one mapping function of Selection-ID.

The remaining 2 bits in quick access message are used differently based on Selection-ID as explained below.

- When AMS uses quick access message to request bandwidth, it sets Selection-ID to be the corresponding F-ID. The 2 remaining bits in quick access message carries request size information, where the size granularity is defined during connection setup for this flow.

- When AMS uses quick access message to request aGPS adaptation for a particular F-ID, it sets the Selection-ID to be a reserved value (13~23) negotiated during connection setup, and indicates the adaptation request in the 2 remaining bits in quick access message.

-------------------------------text#1 end-------------------------------------------

Text proposal #2

--------------------------------text#2 start-----------------------------------------

AMS decodes the IE and checks the MCRC field by its specific 12-bit RA-ID and 2-bit Allocation Type 4-bit Masking Indicator. The RA-ID is calculated by a hash function with the AMS' random access attributes (i.e., frame number index, sub-frame number index, opportunity index and code index). Masking indicator indicates the identifier used for CRC masking, as shown in Table 36.

Table 35—CDMA Allocation A-MAP IE format

| SyntaxSize | (bits) | Notes |
| --- | --- | --- |
| CDMA_Allocation_A-MAP IE() { |  | — |
| A-MAP IE Type | 4 |  |
| Allocation Type | 2 | 00: unsynchronized ranging 01: synchronized ranging 10: BWREQ 11: resved |
| Resource assignment Information | TBD | Each bit indicates the decoding status of BR code in the corresponding BR opportunity.0b0: No BR code is detected, 0b1: At least one code is detected |
| MCS | 5 | Modulation and coding scheme used for the burs |
| MCRC | 16 | CRC masked by RA-ID and Masking Indicator |
| } |  |  |

--------------------------------text#2 end-----------------------------------------