| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | AWD-15.2.3.1.1 Generic MAC Header with a Length Flag Field |
| Date Submitted | 2009-07-06 |
| Source(s) | Baowei Ji, Farooq Khan, Zhouyue Pi, Ying Li Samsung Telecommunications America | bji@sta.samsung.com +1-972-761-7167 |
| Re: | 802.16m AWD: IEEE 802.16m-09/0028r1, “Call for Comments and Contributions on Project 802.16m Amendment Content” |
| Abstract | Propose to add a Length Flag field to GMH for the flexibility of supporting various data burst without large overhead. |
| Purpose | To be discussed and adopted by TGm for 802.16m amendment working document (AWD) |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Generic MAC Header with a Length Flag Field

Baowei Ji, Farooq Khan, Zhouyue Pi, Ying Li

Samsung Telecommunications America

# Introduction

Figure 1 and Figure 2 show the header format for IPv4 and IPv6, respectively. Both headers include a 16-bit length field for payload, supporting an IP packet as long as 65535 bytes.

Figure 1: IP Header format (IPv4)

Figure 2: IP Header format (IPv6)

Table 741 of AWD (09/0010r2) lists various burst sizes, which could be as large as 14400 bytes.

Table 741: Burst Size (AWD, Page 320)

However, the Length field of the GMH is fixed at 11 bits, as shown in Table 1 of the AWD.

Table 1: IEEE 802.16m GMH format (AWD, Page 10)

| Syntax | Size (bit) | Notes |
| --- | --- | --- |
| Generic MAC Header () { | - |  |
| FlowID | 4 | Flow Identifier |
| EH | 1 | Extended header presence indicator |
| Length | 11 | Length of the payload |
| } | - |  |

To use 11-bit “Length” field in the GMH has the following limitations: (1) Any higher layer packets larger than 2043 bytes cannot fit into one MAC PDU---possibly large overhead due to this artificial fragmentation requirement;  (2) In order to meet user throughput requirement, a number MAC PDUs have to be packed into one data burst---possibly multiplicative growth of overhead because each MAC PDU requires at least one GMH and one FPEH.

In other words, the 11-bit “Length” field forces the necessity of MAC PDU concatenation in order to support any data bursts larger than 2048 bytes. For example, to support a data burst of 14400 bytes, as many as 8 MAC PDUs have to concatenated (14400 = 2048x7 + 64). Each MAC PDU has at least GMH (2B) and FPEH (>= 2B). Hence, the total header could be 32 bytes.

Another potential problem with MAC PDU concatenation is the shortage of ARQ sequence number. SN is of 10 bits, which means the ARQ window size is of 512. One 14400-byte data burst needs 8 SNs, which means there is no SN available after 64 subframes (i.e., 512/8) if the same AMS is allocated a 14400B data burst in each subframe. Even we assume 4:4 DL/UL ratio, the ARQ window will be fully occupied after 3.2 superframes, which is only about 64 msec. Note that to meet the highest data rate requirement, more than one 14400B data burst may need to be assigned to the same AMS in a subframe, this further reduces the available ARQ SN. The bottom line is the ARQ may not function properly because of the quickly consumption of SN due to the concatenation of MAC PDUs.

# Suggested proposal

We propose to specify a Length-Flag field allowing both 10-bit and 18-bit MAC PDU length field.

The extra implementation complexity for supporting this flexibility is almost none compared to using the fixed 2B GMH, given that it is just a logical determination of 2B vs. 3B GMH, as shown in the following two tables. Actually, the usage of GMH incurs much more complexity because it requires the usage of MEH for supporting multiple FlowID and a certain method for supporting MAC PDU more than 2047 bytes.

# Text to change in AWD

-------------------------------  Text Start  ---------------------------------------------------

[Page 11, line 4, Section 15.2.3.1.1, Replace Table 1 and Table 2 with the following two tables]

Table 1 --- GMH Format

| Syntax | Size (bit) | Notes |
| --- | --- | --- |
| Generic MAC Header () { | - |  |
| FlowID | 4 | Flow Identifier |
| EH | 1 | Extended header presence indicator |
| LF | 1 | Length flag |
| Length | variable | Length of payload |
| } | - |  |

Table 2 --- GMH Fields

| Names | Size (bit) | Description |
| --- | --- | --- |
| FlowID | 4 | This field indicates the service flow that is addressed. |
| EH | 1 | When set to '1', this field indicates that an Extended Header is present following this GMH. |
| LF | 1 | Length flag |
| Length | variable | LF = 0, 10-bit Length field LF = 1, 18-bit Length field |

[Replace subclause 15.2.17.1:]

-------------------------------  Text End  ---------------------------------------------------