| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed scheme on A-MAP region in the IEEE 802.16m AWD |
| Date Submitted | 2009-07-07 |
| Source(s) | Wei Xia, Yanfeng Guan, Ying Liu, Huiying Fang | E-mail: guan.yanfeng@zte.com.cn *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | Category: AWD comments / Area: Chapter 15.3.6 (DL-CTRL) “Comments on AWD 15.3.6 DL-CTRL” |
| Abstract | This contribution discusses the location and structure of A-MAP region, and proposes text on A-MAP region in the 802.16m AWD. |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed scheme on A-MAP region in the IEEE 802.16m AWD

Wei Xia, Yanfeng Guan, Ying Liu, Huiying Fang

ZTE Corporation

# 1 Introduction

In current AWD, each frequency partition may contain an A-MAP region. However, the following issues need to be discussed and solved:

- When FFR is used, the A-MAP region shall be located in reuse 1 frequency partition only or the highest power level reuse 3 frequency partition only?

- Suppose that the A-MAP region can be located in each frequency partition (FP), there are several scenarios: reuse 1 frequency partition only; the highest power level reuse 3 frequency partition only; both reuse 1 and highest power level reuse 3 frequency partitions; all the frequency partitions. If there is no indication on the location of A-MAP region, the AMS will assume that each FP contains A-MAP region and try to decode non-user specific (NUS) A-MAP in each FP, but it can not confirm that the NUS information is decoded successfully as the NUS information is not appended with CRC.

- For some crucial broadcast MAC management messages, such as RNG-RSP for initial ranging code, MOB_NBR_ADV, short time delay and reliable transmission should be guaranteed. To help AMS quickly decode the A-MAP IE for these messages, these crucial messages should be transmitted in a predefined FP instead of in multiple FPs. The AMS just need to decode broadcast messages in a FP and the blind decoding complexity decrease.

- For Assignment A-MAP region, the current structure in AWD makes blind detection complexity and false detection probability decreases, it is reasonable that Assignment A-MAP region can be located in each FP.

- Regarding HARQ feedback and power control information, if they are located in every FP, the AMS have to know the size of HARQ A-MAP and PC A-MAP in each FP. Otherwise, the AMS will mistake the channel index. Furthermore, these control information are different from the data bursts, it is unnecessary that making them distributed in multiple FPs.

# 2 Location of A-MAP region

Since that the current Assignment A-MAP structure in AWD results in lower decoding complexity and signaling overhead, it is reasonable that A-MAP region may be located in each frequency partition when FFR is used.

The ABS shall define a primary frequency partition in which the crucial broadcast MAC management messages and HARQ A-MAP and PC A-MAP are transmitted.

If the frequency resource is composed of reuse 1 and reuse 3 frequency zone, either the reuse 1 FP or the highest power level reuse 3 FP can be defined as the primary frequency partition depending on system conditions, such as traffic load, power boosting and the interference level. For different application scenarios, either link quality or higher spectrum efficiency can be chosen to achieve through the flexible configuration of primary frequency partition.

The primary frequency partition may be changed in a period and the ABS shall inform the AMS of the primary frequency partition in the S-SFH (TBD). Furthermore, the ABS shall indicate the other frequency partitions whether contains an A-MAP region through non-user specific A-MAP in the primary frequency partition.

# 3 Structure of A-MAP region

For the primary frequency partition, the A-MAP region consists non-user specific A-MAP, HARQ feedback A-MAP, power control A-MAP and assignment A-MAP. For other frequency partitions, the A-MAP region consists of non-user specific A-MAP and assignment A-MAP.

# 4 References

[1] IEEE 80216m-09_0010r2. Part 16: Air Interface for Fixed and Mobile Broadband Wireless Access Systems. Advanced Air Interface(working document), June, 2009.

# Proposal Text #1 for inclusion in the 802.16m amendment

-------------------------------  Text  Start  ---------------------------------------------------

15.3.6.2.2

…

In the DL subframes where the A-MAP regions can be allocated, each frequency partition may contain an A-MAP region. An A-MAP region, if present, shall occupy the first few distributed LRUs in a frequency partition. The ABS shall define a primary frequency partition in which the crucial broadcast MAC management messages and HARQ A-MAP and PC A-MAP are transmitted. The primary frequency partition may be changed in a period and the ABS shall inform the AMS of the primary frequency partition in the S-SFH (TBD). Furthermore, the ABS shall indicate the other frequency partitions whether contains an A-MAP region through non-user specific A-MAP in the primary frequency partition. If frequency resource of a DL Subframe is composed of reuse 3 and reuse 1 frequency zone, the highest power level frequency partition in reuse 3 frequency zone may contain an A-MAP region. Either the frequency partition in reuse 1 frequency zone or the highest power level frequency partition in reuse 3 frequency zone can be defined as the primary frequency partition depending on system conditions, such as traffic load, power boosting and the interference level.

The structure of an A-MAP region is illustrated in the example in Figure 473. The resource occupied by each A-MAP physical channel may vary depending on the system configuration and scheduler operation. For the primary frequency partition, the A-MAP region consists non-user specific A-MAP, HARQ feedback A-MAP, power control A-MAP and assignment A-MAP. For other frequency partitions, the A-MAP region consists of non-user specific A-MAP and assignment A-MAP.

-------------------------------  Text  End  ---------------------------------------------------