| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Text Related to Signaling Header for the IEEE 802.16m Amendment |
| Date Submitted | 2009-07-06 |
| Source(s) | Kiseon Ryu, Eun-Jong Lee, Jeonki Kim, Ronny Kim, JinSam Kwak LG Electronics | Voice: +82-31-450-1910 E-mail: ksryu@lge.com |
| Re: | IEEE 802.16m-09/0028r1, “Call for Contributions on Project 802.16m Amendment Content (draft)”. |
| Abstract | The contribution proposes the text of Signaling Header section to be included in the 802.16m amendment working document. |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Text Related to Signaling Header for the IEEE 802.16m Amendment

Kiseon Ryu, Eun-Jong Lee, Jeonki Kim, Ronny Kim, JinSam Kwak

LG Electronics

# Introduction

The 16m AWD for MAC PDU format section should include the description of MAC Signaling Header. Bandwidth Request, Feedback, UL Tx Power Report, CQICH Allocation Request Header can be specified as 16m MAC Signaling Header. To support bandwidth stealing of the UL resource assigned by PA or GRA which is used the compact header, bandwidth stealing extended header should also be defined.

The standalone signaling header contents and size are optimized with considering the cell edge user to perform contention based BR procedure. To provide more reliability and resource overhead reduction of standalone signaling header, the size of standalone signaling header shall be optimized as minimum HARQ burst size.

# References

IEEE 802.16m-07/002r4, “802.16m System Requirements.”

IEEE 802.16m-08/003r9, “IEEE 802.16m System Description Document”

IEEE 802.16m-09/0010r2, “IEEE 802.16m Amendment Working Document”

IEEE P802.16 Rev2/D9, “Draft IEEE Standard for Local and Metropolitan Area Networks: Air Interface 
for Broadband Wireless Access,” January 2009.

IEEE 802.16m-08/043, “Style guide for writing the IEEE 802.16m amendment.”

# Text proposal for the IEEE 802.16m amendment

----------------------------------------------------- Start of the text ----------------------------------------------------------

## Extended header

The list of defined extended headers is given in Table x.6.

Table x.6 – Description of Extended header types

| Extended header type | Name | Description |
| --- | --- | --- |
| - | Fragmentation and packing extended header | See 15.2.x.2.1 |
| TBD | Fragmentation extended header | See 15.2.x.2.2 |
| TBD | Multiplexing extended header | See 15.2.x.2.3 |
| TBD | Bandwidth stealing header | See 15.2.x.2.4 |
| TBD | Reserved |  |

## Bandwidth Stealing Extended Header (BSEH)

The Bandwidth stealing extended header (BSEH) is used to transmit other MPDUs not belonging to the connection with persistent allocation or group resource allocation through the resource region which is allocated by PA or GRA. When a bandwidth stealing is needed at the resource region where the compact header is used, EH field in CMH shall be set to ‘1’ and this BSEH follows the CMH. The format of BSEH is as shown in table xx.

Table xx. Bandwidth Stealing Extended Header format

| Syntax | Size (bit) | Notes |
| --- | --- | --- |
| BSEH () { | - |  |
| Last | 1 | Last Extended Header indication 0 = Another extended header follows BSEH 1 = another extended header does not follow BSEH |
| Type | TBD | BSEH type |
| FID | 4 | Flow ID |
| Rsvd | TBD | Reserved bits are added at the end of FPEH for byte alignment |
| } |  |  |

The fields of the bandwidth stealing extended header are defined in Table xx-1.

Table xx-1. Bandwidth Stealing Extended Header fields

| Name | Length (bit) | Description |
| --- | --- | --- |
| Last | 1 | When the “Last” bit is set, this extended header is the last one. If this bit is not set, another extended header will follow the current extended header. |
| Type | TBD | Extended header type field. |
| FID | 4 | Flow Identifier. This field indicates the service flow that is addressed. This field is 4 bits long. |

## MAC Signaling Header

Signaling header shall be sent standalone or concatenate with other MAC PDUs. To send the signaling header through the UL resource assigned anonymously, STID shall be included in the signaling header. One FID is reserved for MAC signaling header. The value of FID for MAC signaling header is TBD.

MAC signaling header is illustrated in Table 16.

Table 16. MAC Signaling Header Fields

| Name | Length (bit) | Description |
| --- | --- | --- |
| FlowID | 4 | Flow Identifier. This field indicates the MAC signaling header. The value is TBD. |
| Type | 4 | MAC signaling header type. |
| Contents | 24 | MAC signaling header contents. |

Table 17. Type field encodings for MAC signaling header type

| Type field (3 bits) | MAC Signaling Header Type |
| --- | --- |
| 0000 | BR with STID |
| 0001 | BR without STID |
| 0010 | BR with UL Tx Power Report |
| 0011 | Feedback Header |
| 0100 | CQICH Allocation Request Header |
| 0101 - 1111 | Reserved |

## BR with STID Header

To send the signaling header through the UL resource assigned anonymously, STID shall be included in the BR header. 6 bytes including CRC is used for BR Header, and 16 bit CRC can be appended at the end of the BR contents. Detailed contents for BR Header format are illustrated in Table 18.

Table 18. Anonymous BR Header field

| Name | Length (bit) | Description |
| --- | --- | --- |
| FID | 4 | Flow Identifier. This field indicates MAC signaling header |
| Type | 4 | MAC signaling header type. |
| BR Size | 7 | Burst size index of UL bandwidth requested by the AMS. The BR is for the FID. The request shall be independent of the physical layer modulation and coding. |
| BR FID | 4 | The FID for which UL bandwidth is requested. |
| STID | 12 | STID of which AMS requests UL bandwidth. |
| Reserved | 1 |  |
| CRC | 16 | 16 bit PHY CRC |

## BR without STID Header

BR Header without STID is sent through UL resource assigned by unicast assignment A-MAP, and dedicated UL resource assigned to the AMS. Without STID, BR size in BR Header is 19 bits. BR type shall be included to indicate whether BR type is increment or aggregate.

Table 19. Dedicated BR Header field

| Name | Length (bit) | Description |
| --- | --- | --- |
| FID | 4 | Flow Identifier. This field indicates MAC signaling header |
| Type | 4 | MAC signaling header type. |
| BR Type | 1 | Indicates whether the requested bandwidth is incremental or aggregate. 0: incremental 1: aggregate |
| BR Size | 7 | Burst size index of UL bandwidth requested by the AMS. The BR is for the FID. The request shall be independent of the physical layer modulation and coding. |
| BR FID | 4 | The FID for which UL bandwidth is requested. |
| Reserved | 12 |  |
| CRC | 16 | 16 bit PHY CRC |

## BR and UL Tx Power Report Header

BR Header with UL Tx Power Report is sent through UL resource assigned by unicast assignment A-MAP, and dedicated UL resource assigned to the AMS. UL Tx power level in dBm for the burst that carries this header.

Table 20. BR and UL Tx Power Report Header field

| Name | Length (bit) | Description |
| --- | --- | --- |
| FID | 4 | Flow Identifier. This field indicates MAC signaling header |
| Type | 4 | MAC signaling header type. |
| BR Type | 1 | Indicates whether the requested bandwidth is incremental or aggregate. 0: incremental 1: aggregate |
| BR Size | 7 | Burst size index of UL bandwidth requested by the AMS. The BR is for the FID. The request shall be independent of the physical layer modulation and coding. |
| UL Tx Power | 8 | UL Tx power level in dBm for the burst that carries this header. The value shall be estimated and reported for the burst. |
| BR FID | 4 | The FID for which UL bandwidth is requested. |
| Reserved | 4 |  |
| CRC | 16 | 16 bit PHY CRC |

## Feedback Header

Feedback Header is used for Interference Mitigation. Detailed format is TBD.

## CQICH Allocation Request Header

The CQICH allocation request header is sent by the AMS to request the allocation/deallocation/change of a CQICH. The CQICH allocation request header is illustrated in Table 23.

Table 23. CQICH Allocation Request Header

| Name | Length (bit) | Description |
| --- | --- | --- |
| FlowID | 4 | Flow Identifier. This field indicates MAC signaling header. The value is TBD. |
| Type | 4 | MAC signaling header type. This field indicates the CQICH Allocation Request header |
| Alloc Type | 1 | Indicates whether the CQICH is newly allocated or its type/period is changed. 0: Request that CQICH is newly allocated. 1: Request that CQICH type/period is changed. |
| Preferred Period (p) | 3 | CQICH allocation period which the AMS prefers. The value is defined in units of 2^(p-1) frames. If the value is set to zero, it means that the AMS requests the CQICH de-allocation. |
| MIMO Feedback type | 3 | Indicate AMS’ preferred MIMO operation 0b000: OL distributed 0b001: OL localized 0b010: CL distributed 0b011: CL localized 0b100: SU 0b101: MU MaxMt = 2 0b110: MU MaxMt = 3 0b111: MU MaxMt = 4 |
| CQICH Index | 5 | Index of the CQICH of which the AMS requests the preferred period. In case of new allocation of CQICH, this field is ignored. |
| STID | 12 | STID of which AMS sends this header. |
| CRC | 16 | 16 bit PHY CRC |

---------------------------------------------------------- End of the text --------------------------------------------------------------