| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | TLV vs. ASN.1 Encoding |
| Date Submitted | 2009-08-29 |
| Source(s) | Joey Chou, Muthaiah Venkatachalam, Jose Puthenkulam, Intel | E-mail: joey.chou@intel.com |
| Re: | TGm AWD: |
| Abstract | This contribution proposes MAC management messages. |
| Purpose | Adopt proposed text. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

TLV vs. ASN.1 Encoding

Joey Chou, Muthaiah Venkatachalam, Jose Puthenkulam

Intel

- Introduction

This contribution evaluates both TLV and ASN.1 encodings. AS an example, it encodes an AAI_REG-REQ message, using TLV and ASN.1 methods to understand the structure and efficiency of both methods.

OSS ASN.1 compiler http://www.oss.com/ was used with unaligned PER encoding option to generate most compact ASN.1 encoding.

- TLV

Table 1 shows the AAI_REG-REQ message that contains a message type and 48 TLVs, including compound and non-compound TLVs.

Table 1: AAI_REG-REQ Messages

|  | Messages | Type (Bytes) | Length (Bytes) | Value (Bits) |
| --- | --- | --- | --- | --- |
|  |  |  |  | Information | Padding |
| 0 | Message type |  |  |  |  |
| 1 | ARQ parameters | 1 | 1 | Compound |  |
| 2 | ARQ Enable TLV | 1 | 1 | 1 | 7 bits |
| 3 | ARQ_WINDOW_SIZE TLV | 1 | 1 | 16 | 0 |
| 4 | ARQ_RETRY_TIMEOUT_Tx | 1 | 1 | 16 | 0 |
| 5 | ARQ_RETRY_TIMEOUT_Rx | 1 | 1 | 16 | 0 |
| 6 | ARQ_BLOCK_LIFETIME | 1 | 1 | 16 | 0 |
| 7 | ARQ_SYNC_LOSS_TIMEOUT | 1 | 1 | 16 | 0 |
| 8 | ARQ_DELIVER_IN_ORDER | 1 | 1 | 1 | 7 |
| 9 | ARQ_RX_PURGE_TIMEOUT | 1 | 1 | 16 | 0 |
| 10 | ARQ_BLOCK_SIZE | 1 | 1 | 8 | 0 |
| 11 | RECEIVER_ARQ_ACK_PROC_TIME | 1 | 1 | 8 | 0 |
| 12 | SS management | 1 | 1 | 1 | 7 |
| 13 | IP Management mode | 1 | 1 | 1 | 7 |
| 13 | IP version | 1 | 1 | 1 | 7 |
| 14 | No. of UL Transport CID | 1 | 1 | 16 | 0 |
| 15 | No. of DL Transport CID | 1 | 1 | 16 | 0 |
| 16 | CS capability | 1 | 1 | 7 | 1 |
| 17 | Max Classification rule | 1 | 1 | 16 | 0 |
| 18 | PHS support | 1 | 1 | 3 | 5 |
| 19 | ROHC support | 1 | 1 | 1 | 7 |
| 20 | ARQ support | 1 | 1 | 1 | 7 |
| 21 | DSx flow control | 1 | 1 | 8 | 0 |
| 22 | MCA flow control | 1 | 1 | 8 | 0 |
| 23 | Multicast polling group CID support | 1 | 1 | 8 | 0 |
| 24 | Maximum MAC data per frame support | 1 | 1 | compound |  |
| 25 | Maximum amount of MAC level data per DL frame | 1 | 1 | 16 | 0 |
| 26 | Maximum amount of MAC level data per UL frame | 1 | 1 | 16 | 0 |
| 27 | Packing support | 1 | 1 | 1 | 7 |
| 28 | MAC Extended rtPS support | 1 | 1 | 1 | 7 |
| 29 | Max no of bursts transmitted concurrently to the MS | 1 | 1 | 4 | 4 |
| 30 | Co-located coexistence capability supported | 1 | 1 | 4 | 4 |
| 31 | H-FDD sleep capabilities | 1 | 1 | 1 | 7 |
| 32 | Extended capability | 1 | 1 | 3 | 5 |
| 33 | Method for allocating IP address for the secondary management connection | 1 | 1 | 4 | 4 |
| 34 | MS HO process timer | 1 | 1 | 8 | 0 |
| 35 | MS HO Conn Parameter proc time | 1 | 1 | 8 | 0 |
| 36 | MS HO TEK proc time | 1 | 1 | 8 | 0 |
| 37 | HO supported | 1 | 1 | 7 | 1 |
| 38 | HO ready indication | 1 | 1 | 8 | 0 |
| 39 | BS switching timer | 1 | 1 | 16 | 0 |
| 40 | Mobility feature | 1 | 1 | 3 | 5 |
| 41 | Power Saving class | 1 | 1 | 10 | 6 |
| 42 | Sleep mode recovery time | 1 | 1 | 8 | 0 |
| 43 | MS prev IP addr | 1 | 1 | 192 | 0 |
| 44 | Idle mode timeout | 1 | 1 | 16 | 0 |
| 45 | ARQ ack type | 1 | 1 | 5 | 3 |
| 46 | MAC header | 1 | 1 | 17 | 7 |
| 47 | MA periodic ranging timer | 1 | 1 | 8 | 0 |
| 48 | MBS capability | 1 | 1 | 3 | 5 |
|  | Total | 48 bytes | 48 bytes | 568 bits | 120 bits |

AAI_REG-REQ message contains:

- 1 byte for message type

- 48 bytes for Type

- 48 bytes for Length

- 86 bytes for Value (568 information bits, 120 padding bits)

Total message size = 1 + 48 + 48 + 86 = 183 bytes = 1464 bits

Total information bits = 568 + 8 = 576 bits

Overhead = 1464 – 576 = 888 bits

- REG-REQ in ASN1 format

REGREQ DEFINITIONS AUTOMATIC TAGS ::= BEGIN

RegRequest ::= SEQUENCE {

messageType            OCTET STRING (SIZE(1)),

arqEnable              ENUMERATED {arqNotRequested,

arqRequested} OPTIONAL,

arqWindowSize          INTEGER (1..65535) OPTIONAL,

arqTxRetryTimeout      INTEGER (0..65535) OPTIONAL,

arqRxRetryTimeout      INTEGER (0..65535) OPTIONAL,

arqBlockLifetime       INTEGER (0..65535) OPTIONAL,

arqSyncLossTimeout     INTEGER (0..65535) OPTIONAL,

arqDeliverInOrder      ENUMERATED {orderNotPreserved,

orderPreserved} OPTIONAL,

arqRxPurgeTimeout      INTEGER (0..65535) OPTIONAL,

arqBlockSize           BIT STRING {m0(0), -- The minimum block size

m1(1), -- is equal to 2^(M+4).

m2(2), -- The maximum block size

m3(3), -- is equal to 2^(N+4),

n0(4), -- M<=6, N<=6, and M<=N

n1(5),

n2(6),

n3(7)} (SIZE(8)) OPTIONAL,

arqAckProcessingTime   INTEGER (0..255) OPTIONAL,

ssManagementSupport    ENUMERATED {no2ndMgmtConnection,

with2ndMgmtConnection} OPTIONAL,

ipManagementMode       ENUMERATED {unManagedMode,

ipManagedMode} OPTIONAL,

ipVersion              ENUMERATED {ipV4, ipV6} OPTIONAL,

numOfUlTransportCid    INTEGER (0..65535) OPTIONAL,

numOfDlTransportCid    INTEGER (0..65535) OPTIONAL,

csOptions              BIT STRING {atm(0),

ipCsIpV4(1),

ipCsIpV6(2),

ethernetCs(3),

ethernetCsIpV4(4),

ethernetCsIpV6(5),

gpcs(6),

packetCsIp(7)} (SIZE(8)) OPTIONAL,

maxClassificationRule  INTEGER (0..65535) OPTIONAL,

phsSupport             BIT STRING {atmPhs(0),

packetPhs(1),

gpcsPhs(2)} (SIZE(3)) OPTIONAL,

rohcSupport            BIT STRING {rohcSupported(0),

rohcNotSupported(1)} (SIZE(2)) OPTIONAL,

arqSupport             BIT STRING {arqSupported(0),

arqNotSupported(1)} (SIZE(2)) OPTIONAL,

dsxFlowControl         INTEGER (0..255) OPTIONAL,

mcaFlowControl         INTEGER (0..255) OPTIONAL,

maxMulticastPollongGrp INTEGER (0..255) OPTIONAL,

maxMacDataPerDlFrame   INTEGER (0..65535) OPTIONAL,

maxMacDataPerUlFrame   INTEGER (0..65535) OPTIONAL,

packingSupport         BIT STRING {packingSupported(0),

packingNotSupported(1)} (SIZE(2)) OPTIONAL,

extendedRtpsSupport    BIT STRING {extRtpsSupported(0),

extRtpsNotSupported(1)} (SIZE(2)) OPTIONAL,

maxNumConrruentBurst   INTEGER (1..16) OPTIONAL,

coexistanceCapability  BIT STRING {pcsBasedMode1(0),

pcsBasedMode2(1),

sleepModeAfterPcs(2),

amcForPcsMode(3)} (SIZE(4)) OPTIONAL,

hfddSleepCapability    BIT STRING {hfddSleepModeSupport(0)} (SIZE(1)) OPTIONAL,

extendedCapability     BIT STRING {arqMap(0),

bsControlledHo(1),

grpParameterChange(2)} (SIZE(3)) OPTIONAL,

ipAddrAllocationMethod BIT STRING {dhcp(0),

mobileIpv4(1),

dhcpV6(2),

ipV6StatelessAddr(3)} (SIZE(4)) OPTIONAL,

hoProcOptMsTimer       INTEGER (0..255) OPTIONAL,

msHoProcessTime        INTEGER (0..255) OPTIONAL,

msHoTekProcessMsTime   INTEGER (0..255) OPTIONAL,

handoverSupport        BIT STRING {mdhoFbssho(0),

mdhoDlRfCombining(1),

mdhoDlSoftCombiningSingleMap(2),

mdhoDlRfCombiningMultipleMap(3),

mdhoUlMultiTransmission(4),

seamlessHo(5),

additionalActionTime(6)} (SIZE(7)) OPTIONAL,

hoReadyTimer           INTEGER (0..255) OPTIONAL,

intraFaHandoverTimer   INTEGER (0..15) OPTIONAL,

interFaHandoverTimer   INTEGER (0..15) OPTIONAL,

intraFftHandoverTimer  INTEGER (0..15) OPTIONAL,

mobilitySupport        BIT STRING {arqMap(0),

bsControlledHo(1),

grpParameterChange(2)} (SIZE(3)) OPTIONAL,

psClassSupported       BIT STRING {psClassType1Supported(0),

psClassType2Supported(1),

psClassType3Supported(2)} (SIZE(3)) OPTIONAL,

totalPsInstances       INTEGER (0..31) OPTIONAL,

sleepModeRecoveryTime  INTEGER (0..255) OPTIONAL,

prevMsIpAddr           OCTET STRING (SIZE(24)),

idleModeTimeout        INTEGER (0..65535) OPTIONAL,

acqAckType             BIT STRING {slectiveAckEntry(0),

cumulativeAckEntry(1),

slecAndCumuAckEntry(2),

seqBlockAckEntry(3)} (SIZE(4)) OPTIONAL,

macHeaderSupport       BIT STRING {brUlTxPowerReport(0),

brCinrReport(1),

cqichAllocationReport(2),

brUlSleepControl(3),

snReport(4),

feedbackReport(5),

sduSnExtHeaderAndPara(6),

sduSnExtHeader(7),

dlSleepControl(8),

feedbackRequest(9),

mimoModeFeedback(10),

ulTxPowerReport(11),

miniFeedback(12),

snRequest(13)} (SIZE(14)) OPTIONAL,

sduSnTxPeriod          INTEGER (0..7) OPTIONAL,

msPeriodRngTimer       INTEGER (0..255) OPTIONAL,

mbsCapability          BIT STRING {inServingBsOnly(0),

macroDiversity(1),

nonMacroDiversity(2)} (SIZE(3)) OPTIONAL}

END

TOTAL LENGTH: = 626 bits

- Overhead (Control bit map) = 50 bits

- Information = 576 bits

- Macros

ASN.1 compiler can generate Macros to help accessing each field in the ASN.1 message. The following lists an example of ASN.1 macros.

/* allocates memory for RegRequest_PDU */

#define oss_RegRequest_new_pdu(world) \

(RegRequest *)ossGetInitializedMemory(world, sizeof(RegRequest))

/* gets "messageType" field value */

#define oss_RegRequest_messageType_get(inp) \

(inp)->messageType

/* sets "messageType" field value */

#define oss_RegRequest_messageType_set(outp, messageType_) \

(outp)->messageType = (messageType_)

/* Macros for "messageType" field operate with '_OctStr' type; you may use

* macros after this type declaration to create its values */

/* gets "arqEnable" field value */

#define oss_RegRequest_arqEnable_get(inp) \

(inp)->arqEnable

/* sets "arqEnable" field value */

#define oss_RegRequest_arqEnable_set(outp, arqEnable_) \

{ \

(outp)->bit_mask[arqEnable_present_byte] |= arqEnable_present; \

(outp)->arqEnable = (arqEnable_); \

}

/* checks if "arqEnable" field value is present */

#define oss_RegRequest_arqEnable_is_present(inp) \

((inp)->bit_mask[arqEnable_present_byte] & arqEnable_present)

- Conclusion

AAI_REG-REQ message encoded in TLV requires 183 bytes (1464 bits)

AAI_REG-REQ message encoded in ASN.1 requires 626 bites

ASN.1 can save 838 bits. The saving comes from:

- TLV needs 1 byte for Type, and 1 bytes for Length. There are 48 TLVs that equals to 96 bytes. ASN1 uses a control bit map to indicate the presence of each parameter. So, it only needs 50 bits.

- ASN1 uses unaligned PER encoding, so no padding bits are needed

838 bits (ASN.1 saving) = 8 * 96 (type and length) + 120 (padding) – 50 (control bits)