| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Text for the IEEE 802.16m/D1 on E-MBS Configuration Message and E-MBS Control Channel |
| Date Submitted | 2009-08-30 |
| Source(s) | Yujian Zhang, Kamran Etemad, Huaning Niu, Changlong Xu, Jong-kae Fwu, Hujun Yin Intel Corporation | +86-10-82611515 yujian.zhang@intel.com *<http://standards.ieee.org/faqs/affiliationFAQ.html |
| Re: | IEEE 802.16m-09/0037 Call for Contributions on Project 802.16m Amendment Content P802.16m/D1: E-MBS |
| Abstract | Proposed text for the IEEE 802.16m/D1 on E-MBS Configuration Message and E-MBS Control Channel |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Text for the IEEE 802.16m/D1 on E-MBS Configuration Message and E-MBS Control Channel

Yujian Zhang, Kamran Etemad, Huaning Niu, Changlong Xu, Jong-kae Fwu, Hujun Yin

Intel Corporation

# Introduction

This contribution proposes text for E-MBS configuration message and E-MBS control channel to be included in 802.16m amendment. The contribution is compliant to the 802.16m SRD [1] and the 802.16m SDD [2], and it follows the style and format guidelines in [3].

# Overview

According to SDD [2], the following structure for E-MBS is proposed:

- In the first superframe of MSI, S-SFH indicates the presence of E-MBS Configuration Message using an E_MBS_FLG bit in SPx [TBD]. When the E_MBS_FLG bit is set to 1, then the E-MBS Configuration Message is transmitted in that super-frame as the 1st assignment A-MAP channel with a reserved STID.

- E-MBS Configuration Message contains information for E-MBS resource region and PHY parameters for E-MBS MAP.

- E-MBS MAP contains information for each E-MBS allocation. Information for all allocations is jointly coded.

# References

[1] IEEE 802.16m-07/002r8, “802.16m System Requirements”

[2] IEEE 802.16m-09/003r9a, “IEEE 802.16m System Description Document (SDD)”

[3] IEEE 802.16m-08/043, “Style guide for writing the IEEE 802.16m amendment”

-------------------------------  Start Text Proposal ---------------------------------------------------

15.3.6.2.3 Enhanced Multicast Broadcast Service Configuration Message (E-MBS Configuration Message)

The E-MBS Configuration Message carries information to locate E-MBS resource region and PHY parameters for E-MBS MAP.

In the first superframe of MSI, S-SFH indicates the presence of E-MBS Configuration Message using an E_MBS_FLG bit in SPx [TBD]. When the E_MBS_FLG bit is set to 1, then the E-MBS Configuration Message is transmitted in that super-frame as the 1st assignment A-MAP channel with a reserved STID.

15.3.6.2.4 Enhanced Multicast Broadcast Service MAP (E-MBS MAP)

The E-MBS MAP carries control information for enhanced multicast broadcast service.  The E-MBS MAP consists of non-user specific control information. The E-MBS MAP, when present, is transmitted at the beginning of E-MBS resource region during one E-MBS scheduling interval.

……

15.3.6.5 DL Control Information Elements

15.3.6.5.4 Unicast Control Information Elements

15.3.6.5.4.13 E-MBS Configuration Message IE

Table xxx describes the E-MBS Configuration Message IE used for indicating E-MBS resource region and PHY parameters for E-MBS MAP.

Table 677: E-MBS Configuration Message IE

| Syntax | Size in bits | Description/Notes |
| --- | --- | --- |
| E-MBS-Configuration-Message_IE () { | - | - |
| E-MBS Resource Pattern | 3 | Indicates the starting subframe index for E-MBS transmissions. |
| MCS | 2 | MCS level for E-MBS MAP |
| Resource Size | [5] | Number of DRUs occupied by E-MBS MAP |
| Reserved | TBD | Reserved bits |
| Padding | Variable | Padding to reach byte boundary |
| } |  |  |

15.3.6.5.5 E-MBS Control Information Elements

15.3.6.5.5.3 E-MBS MAP IE

Table yyy describes the fields in a E-MBS MAP IE used for indicating assignment for E-MBS data in the DL.

Table 6yyy: E-MBS MAP IE

| Syntax | Size in bits | Description/Notes |
| --- | --- | --- |
| E-MBS-MAP_IE() { | - | - |
| E-MBS Zone identifier | 7 | E-MBS Zone identifier corresponds to the identifier provided by the ABS at connection initiation |
| Number of allocations | 7 | Number of allocation specified |
| For (j=0;j<Number of allocations; j++) { |  | For loop where each loop element specifies information for one allocation. |
| RCID | variable | Specifies the station ID in RCID format, type defined by RCID Type |
| MCS | [4] | Depends on supported modes, 16 modes assumed as baseline |
| E-MBS MEF | 1 | E-MBS MIMO Encoding Format 0b00 – SFBC 0b01 – VE |
| If (E-MBS MEF == 0b01){ |  |  |
| Mt | 1 | Number of streams 0b0 = 1 stream 0b1 = 2 streams |
| } |  |  |
| E-MBS Resource | TBD | Indicates resource allocation |
| } |  |  |
| Padding | Variable | Padding to reach byte boundary |
| } |  |  |

-------------------------------------- End of Text Proposal -------------------------------------------