| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | ARQ operation in 16m Relay (Relay) |
| Date Submitted | 2009-08-30 |
| Source(s) | Youngbin Chang, Rakesh Taori, Anil Agiwal, Hyunjeong Kang Samsung Electronics | E-mail: yb.chang@samsung.com Phone: +82-31-279-5519 *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | Call for Contributions on Project 802.16m Amendment Content: IEEE802.16m-09/0037 |
| Abstract | This contribution mainly proposes the ARQ operation in 16m Relay system |
| Purpose | To be discussed and adopted in 802.16m AWD |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

ARQ operation in 16m Relay

Youngbin Chang, Rakesh Taori, Anil Agiwal, Hyunjeong Kang

Samsung Electronics

# Introduction

This contribution proposes the ARQ operation at AMS, which is align with SDD agreement.

# Text proposal

============================= Start of Proposed Text ========================

[Add the text in the appropriate section as follows]

15.x.x ARQ mechanism

The ARS performs ARQ operation with ABS in the relay link and AMS in the access link.

In downlink, ABS generates and sends an ARQ block to ARS in the relay link. If the ARQ block is corrupted in the relay link, ARS shall send a NACK to ABS, and then ABS shall prepare and perform retransmission. If ARS receives the ARQ block correctly in the relay link, ARS shall forward the ARQ block to the AMS in the access link. In the access link, if the ARQ block is corrupted and the ARS receives a NACK from AMS, ARS shall prepare and perform retransmission to AMS. If ARS receives an ACK from MSs and forwards MS’s ACK to ABS. ABS shall clear the buffer and update ARQ window.

In uplink, AMS generates and sends ARQ block to ARS in the access link. If the ARQ block is corrupted in the access link, ARS sends a NACK to AMS, and then AMS shall prepare and perform retransmission. If ARS receives the ARQ block is correctly in the access link, ARS shall forward ARQ block to the ABS. In the relay link, if the ARQ block is corrupted and ARS receives a NACK from ABS, ARS shall prepare and perform retransmission. If ARS receives an ACK from ABS, ARS shall forward BS’s ACK to each MS. the AMS shall clear the buffer and update the ARQ window.

============================== End of Proposed Text ========================