| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Changes Related to CDMA Allocation A-MAP IE for Grant in 802.16m/D3 (16.2.11) |
| Date Submitted | 2010-01-07 |
| Source(s) | Jisoo Park, Namsuk Lee, Sookjin Lee, Yongseouk Choi ETRI | jsp@etri.re.kr |
| Re: | IEEE 802.16 Working Group Letter Ballot Recirculation #30b on IEEE P802.16m/D3 |
| Abstract | The contribution proposes the text changes to CDMA Allocation A-MAP IE in 802.16m/D3. |
| Purpose | To discuss and adopt the proposed text in the next revision of 802.16m amendment draft. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Changes Related to CDMA Allocation A-MAP IE for Grant in 802.16m/D3 (16.2.11)

Jisoo Park, Namsuk Lee, Sookjin Lee, Yongseouk Choi

ETRI

# Introduction

In the current draft for HARQ issue, HARQ operation without the capability information of AMS such as the data burst processing time (Tproc) should be applied to MAC control messages at initial ranging and BR process with broken quick access message including STID. It is necessary to clarification for HARQ operation in the case of that ABS doesn’t know AMS capability including the data burst processing time (Tproc).

This contribution propose the text changes to CDMA Allocation A-MAP IE for grant related to HARQ operation defined in the current 80216m draft [1].

# Motivation

In the current draft [1] for initial ranging and BR procedures, ABS should provide UL bandwidth by CDMA Allocation A-MAP IE as the grant for BW-REQ message. If AMS tries initial ranging process or BR process that ABS is unable to decode the quick access message including STID of the corresponding AMS, ABS can’t recognize the capability of the data burst processing time (Tproc) to be used to calculate HARQ timing schedule for HARQ operation. But HARQ operation should be applied to unicast MAC control message for MAC management reliability of initial ranging process or BR process as well as unicast data traffic in both downlink and uplink, respectively. For example, although the ABS does not know the data burst processing time (Tproc) of the AMS at initial ranging or BR process, the corresponding AMS should transmit AAI_RNG-REQ message to be applied to HARQ operation at initial ranging. Also, AAI_RNG-RSP, AAI_SBC-REQ and AAI_SBC-RSP messages should be applied to HARQ operation.

In the current draft, there are 3 types of HARQ frame offsets for HARQ operation defined in the section <<16.2.14 HARQ function>> for FDD and TDD, respectively as follows;

- DL HARQ feedback offset z,

- UL HARQ subpacket(data burst) transmission offset v,

- UL HARQ feedback offset w.

These offsets are set to 0 or 1 according to the following parameters by predefined mathematical formula;

- number of AAI subframes for FDD or TDD (DL and UL),

- TTI length of a data burst,

- assignment A-MAP and and data burst position using AAI subframe index,

- data burst processing time (Tproc).

The value ‘1’ of these offsets means that the allocation position (AAI subframe index) of HARQ feedback or HARQ subpacket(data burst) transmission should be moved to next frame as the size of offset value; otherwise the allocation position is not moved and it is tightly fast served.

However, if ABS doesn’t know the data burst processing time (Tproc) of AMS, ABS may allocate the resource of DL HARQ feedback or UL HARQ subpacket Tx/ReTx in every frame for being successful of HARQ operation. It may be waste of the radio resource in this case for the corresponding AMS with large value of Tproc. Of course, it may be need to do that for any other purpose. It should be also considered not only for UL HARQ operation of UL bandwidth requested in above mentioned case and UL HARQ feedback, but for DL HARQ operation for DL data burst transmission as its responses with MAC control message and DL HARQ feedback in UL. So it is necessary to be flexible for the usage of the resource for that case by ABS.

As this reason, it is necessary to clarify HARQ operation to set temporarily HARQ frame offsets to support these MAC control messages until ABS detects the data burst processing time (Tproc) of AMS.

Additionally, a data burst may occupy contiguous multiple AAI subframe with long TTI transmission not only for the motive or purpose of the usage of long TTI, but also for the reason that a specific frame partition ratio for TDD had been proposed to be only supported for the data burst with the long TTI [2]. If the number of DL AAI subframes (D) is less than the number of UL AAI subframes (U) in TDD frame partition, only long TTI transmission is used for TDD uplink process, since this TDD frame partition is not expected to be a commonly used configuration such as 3:5, and then have been proposed to be only supported for the data burst with the long TTI [2]. So it needs to add the field of Long TTI Indicator in the CDMA Allocation A-MAP IE.

# Proposal

In this contribution, it is proposed to the text changes to add the temporary indicator to set temporarily HARQ frame offsets for HARQ operation without the capability information of AMS until ABS detects the data burst processing time (Tproc) of AMS and to include a clarification for the transmission length of data burst with default or long TTI for above that reason in CDMA Allocation A-MAP IE.

# References

- IEEE P802.16m/D3, “Draft Amendment to IEEE Standard for Local and Metropolitan Area Networks- Part 16: Air Interface for Broadband Wireless Access Systems,” December 8, 2009.

- Roshni Srinivasan, Hujun Yin, Yi Hsuan, Hyunkyu Yu, “Proposed Changes Related to Allocation Relevance in the DL and UL Basic Assignment A-MAP Information Elements in the 802.16m AWD (AWD - 15.3.6.5.2.2),” C802.16m-09/1329r1, July 2009.

# Proposed Changes for inclusion in the 802.16m/D3

[Added texts and figures marked in blue font with underline and removed texts and figures marked in red font with strikeout]

------------------------------------------------------ Start of the Text -------------------------------------------------------

[Remedy: the text changes in Table 743 of page 209, section 16.2.11.2 Grant as follows]

Table 743– CDMA Allocation A-MAP IE* format

| Syntax | Size (bits) | Notes |
| --- | --- | --- |
| CDMA_Allocation_A-MAP IE() { |  |  |
| A-MAP IE type | 4 | CDMA Allocation A-MAP IE |
| If MCRC is masked with RAID and masking indicator for BR { |  |  |
| Resource Assignment Information | TBD |  |
| Long TTI Indicator | 1 | Indicates number of AAI subframes spanned by the allocated resource. 0b0: 1 AAI subframe (default) 0b1: 4 UL AAI subframes for FDD or all UL AAI subframes for TDD If number of DL AAI subframes, D is less than number of UL AAI subframes, U, Long TTI Indicator = 0b1. |
| HFA | 3 | HARQ Feedback Allocation [If ABS assigns HFA implicitly, this parameter is unnecessary.] |
| Temporary HARQ Offset Indicator | 1 | Indicates whether HARQ frame offsets (i.e. DL HARQ feedback offset z, UL HARQ subpacket Tx offset v and UL HARQ feedback offset w) for HARQ operation is temporarily set or not. 0b0: not applicable 0b1: every HARQ frame offset (z, v, w) is set to 1 If Temporary HARQ Offset Indicator = 0b1, AMS shall maintain all HARQ frame offsets as ‘1’ for HARQ operation until ABS detects the data burst processing time Tproc of AMS. |
| Reserved | TBD |  |
| } |  |  |
| Else if MCRC is masked with RAID and masking indicator for Ranging { |  |  |
| Resource Assignment Information | TBD |  |
| Long TTI Indicator | 1 | Indicates number of AAI subframes spanned by the allocated resource. 0b0: 1 AAI subframe (default) 0b1: 4 UL AAI subframes for FDD or all UL AAI subframes for TDD If number of DL AAI subframes, D is less than number of UL AAI subframes, U, Long TTI Indicator = 0b1. |
| HFA | 3 | HARQ Feedback Allocation |
| Temporary HARQ Offset Indicator | 1 | Indicates whether HARQ frame offsets (i.e. DL HARQ feedback offset z, UL HARQ subpacket Tx offset v and UL HARQ feedback offset w) for HARQ operation is temporarily set or not. 0b0: not applicable 0b1: every HARQ frame offset (z, v, w) is set to 1 If Temporary HARQ Offset Indicator = 0b1, AMS shall maintain all HARQ frame offsets as ‘1’ for HARQ operation until ABS detects the data burst processing time Tproc of AMS. |
| Reserved | TBD |  |
| } |  |  |
| MCRC | 16 | CRC masked by RA-ID and Masking Indicator |
| } |  |  |

* A 16 bit CRC is generated based on the contents of the CDMA Allocation A-MAP IE. The CRC is masked by RA-ID and Masking Indicator.

------------------------------------------------------- End of the Text -------------------------------------------------------