| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposal on Broadcast Burst Resource Indication |
| Date Submitted | 2010-03-04 |
| Source(s) | Xianming Chen, Yanfeng Guan, Huiying Fang, Lei Zhang ZTE Corporation | guan.yanfeng@zte.com.cn |
| Re: | Comment on “DRAFT Amendment to IEEE Standard for Local and metropolitan area networks, P802.16m/D4” 16.3.6.5.2.1 Non-user-specific A-MAP IE & 16.3.6.5.2.4 Assignment A-MAP IE |
| Abstract | This contribution proposes text on Broadcast Burst Resource Indication. |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposal on Broadcast Burst Resource Indication

Xianming Chen, Yanfeng Guan, Huiying Fang, Lei Zhang

ZTE Corporation

# Introduction

In the current 802.16m draft amendment [1], broadcast assignment AMAP is defined and used for broadcast burst attribute description and resource indication.

# Problem

When a unicast assignment AMAP, such as DL Basic Assignment AMAP, was not received correctly by an AMS, the corresponding burst could be re-transmitted by ABS through HARQ function.

When a broadcast assignment AMAP was not received correctly by an AMS, the corresponding burst could not be re-transmitted by ABS, as HARQ function could not be used for broadcast burst transmission.

Therefore, it is necessary to make the probability of decoding broadcast assignment AMAP correctly higher than that of decoding unicast assignment AMAP correctly.

In other hand, both broadcast assignment AMAP and NUS need be received by each AMS, and in reuse 1 frequency partition, current NUS code rate (1/12) is more robust than unicast assignment AMAP code rate (1/4 or 1/8), but current broadcast assignment AMAP code rate is the same as unicast/multicast assignment AMAP code rate (1/4 or 1/8) in D4.

In addition, CRC detection method for broadcast A-AMAP is not fully accurate, and error detection may happen.

Therefore, it is not reasonable for current broadcast burst resource indication method using broadcast assignment AMAP.

# Proposed Method

Use NUS Extension to specify the information used for decoding broadcast message, and NUS Extension code rate is determined to unicast or multicast A-AMAP code rate set implicitly as follows:

| Unicast/multicast A-AMAP MCS set (Reuse 1 FP) | Unicast/multicast A-AMAP MCS set (High Power Reuse 3 FP) | NUS Extension MCS (Reuse 1 FP) | NUS Extension MCS (High Power Reuse 3 FP) |
| --- | --- | --- | --- |
| QPSK 1/2，QPSK 1/4 | QPSK 1/2 | QPSK 1/8 | QPSK 1/4 |
| QPSK 1/2，QPSK 1/8 | QPSK 1/4 | QPSK 1/12 | QPSK 1/4 |

# References

[1] "DRAFT Amendment to IEEE Standard for Local and metropolitan area networks Part 16: Air Interface for Broadband Wireless Access Systems Advanced Air Interface", P802.16m/D4 Feb. 2010.

# Proposed Text

----------------------------------------------------------- Start of the Proposed Text  --------------------------------------

Remedy 1: Line 4-10, Page 459,16.3.6.5.2.1 Non-user-specific A-MAP IE

If the non-user specific A-MAP extension flag in the non-user specific A-MAP is set, the non-user specific A-MAP extension mayshall be used to specify the information used to decode the PGID Info, AAI-TRF-IND, AAI-PAG-ADV, and other broadcast messages. The PHY structure for this extension is the same as the non-user specific A-MAP. The MCS of the non-user specific A-MAP extension is determined according to that of the unicast or multicast A-AMAP, implicitly. Table X describes the MCS of the non-user specific A-MAP extension.

Table X – MCS Mapping Rule between NUS Extension and A-AMAP IE

| Unicast/multicast A-AMAP MCS Set (Reuse 1 FP) | Unicast/multicast A-AMAP MCS (High Power Reuse 3 FP) | NUS Extension MCS (Reuse 1 FP) | NUS Extension MCS (High Power Reuse 3 FP) |
| --- | --- | --- | --- |
| QPSK 1/2，QPSK 1/4 | QPSK 1/2 | QPSK 1/8 | QPSK 1/4 |
| QPSK 1/2，QPSK 1/8 | QPSK 1/4 | QPSK 1/12 | QPSK 1/4 |

NUS Extension A-MAP allocates resource for a broadcast burst. All broadcast MAC control messages transmitted in an AAI subframe shall be included in a broadcast burst. Table Y describes the fields in an NUS Extension A-MAP.

Table Y – NUS Extension A-MAP Format

| Syntax | Size (bit) | Description/Notes |
| --- | --- | --- |
| Function Index | 1 | 0: This IE carries broadcast assignment information 1: This IE carriers ranging channel allocation information |
| If (Function Index == 0){ |  |  |
| Burst Size | 6 | Burst size as indicated in the first 64 entries of Table 923 |
| Resource Index | 11 | 5 MHz: 0 in first 2 MSB bits + 9 bits for resource index 10 MHz: 11 bits for resource index 20 MHz: 11 bits for resource index Resource index includes location and allocation size |
| Long TTI Indicator | 1 | Indicates number of AAI subframes spanned by the allocated resource. 0b0: 1 AAI subframe (default) 0b1: 4 DL AAI subframes for FDD or all DL AAI subframes for TDD |
| Transmission Format | 1 | 0b0: no time domain repetition 0b1: with time domain repetition |
| Repetition | 2 | 0b00: no more repetition of the same burst 0b01: the same burst will be transmitted one more time 0b10: the same burst will be transmitted two more times 0b11: the same burst will be transmitted three more times |
| Reserved | TBD | Reserved bits |
| } else if (Function Index == 1){ |  |  |
| Number of Ranging Opportunities (N) | 2 | TBD |
| For (i=0; i<N; i++){ |  |  |
| Subframe index | 3 |  |
| } |  |  |
| Reserved |  |  |
| } |  |  |

Remedy 2: Line 17, Page 460, 16.3.6.5.2.4 Assignment A-MAP IE

Table 818 -- Assignment IE Types

| A-MAP IE Type | Usage |
| --- | --- |
| 0b0000 | DL Basic Assignment A-MAP IE |
| 0b0001 | UL Basic Assignment A-MAP IE |
| 0b0010 | DL Subband Assignment A-MAP |
| 0b0011 | UL Subband Assignment A-MAP IE |
| 0b0100 | Feedback Allocation A-MAP IE |
| 0b0101 | UL Sounding Command A-MAP IE |
| 0b0110 | CDMA Allocation A-MAP IE |
| 0b0111 | DL Persistent Allocation A-MAP IE |
| 0b1000 | UL Persistent Allocation A-MAP IE |
| 0b1001 | Group Resource Allocation A-MAP IE |
| 0b1010 | Feedback Polling A-MAP IE |
| 0b1011 | BR-ACK A-MAP IE |
| 0b1100 | Broadcast Assignment A-MAP IE UL CSM Beamforming A-MAP IE |
| 0b1101 | UL CSM Beamforming A-MAP IE Reserved |
| 0b1110 | Reserved |
| 0b1111 | Extended Assignment A-MAP IE |

CRC Mask

A 16 bit CRC is generated based on the contents of assignment A-MAP IE and is masked by 16 bit CRC mask using the bitwise XOR operation.

Table 819—Description of CRC Mask

| Masking prefix | Description |
| --- | --- |
| 0b0 | CRC is masked by 1 bit Masking prefix, 3 bit message type indicator, and 12 bit Masking Code The 3-bit type indicator shall be set/interpreted as follows. 000: 12 bit Masking Code refers to an STID (i.e. CRC mask = 0000¦ Masking Code) 001: 12 bit Masking Code used to mask broadcast assignment A-MAP IE, BR-ACK A-MAP IE, and group resource allocation A-MAP IE, which is described in Table 820 (i.e. CRC mask = 0001¦ Masking Code). |
| 0b1 | CRC is masked by 1 bit Masking prefix, and 15 bit RAID (i.e. CRC mask = 1¦RAID) |

Table 820—Description of the Masking Code for type indicator 001

| Decimal value | Description |
| --- | --- |
| 0 | Used to mask broadcast assignment A-MAP IE Used to mask BR-ACK A-MAP IE |
| 1 | Used to mask BR-ACK A-MAP IE |
| 2 1 – 64 4095 | Used to mask group resource allocation A-MAP IE (group ID) |

Remedy 3: Delete: 16.3.6.5.2.4.13 Broadcast Assignment A-MAP IE

-----------------------------------------------------------End of the Proposed Text   ----------------------------------------