| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed changes to partially configured carrier(16.2.8.1) |
| Date Submitted | 2010-07-09 |
| Source(s) | Soojung Jung, Eunkyung Kim, Jaesun Cha, Sungcheol Chang, Hyun Lee, Chulsik Yoon ETRI | E-mail: sjjung@etri.re.kr |
| Re: | IEEE 802.16 Sponsor Ballot on P802.16m/D6 |
| Abstract | Proposed text to modify description of partially configured carrier. |
| Purpose | To be discussed and adopted by TGm |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed changes to partially configured carrier (16.2.8.1)

Soojung Jung, Eunkyung Kim, Jaesun Cha, Sungcheol Chang, Hyun Lee, Chulsik Yoon

ETRI

# 1. Introduction

According to section in 16.3.3.7, the frame configuration and indexing does not include DL only frame in TDD mode. Therefore partially configured carrier is defined only for FDD. We propose to modify the description of partially configured carrier.

# 2. Text Proposal

------------------------------------------------------------Start of the Text--------------------------------------------------------

[Modify the text on the page 4, line 45 as follows]

3.106 partially configured carrier: A carrier with only downlink transmission in TDD or a downlink carrier without paired UL carrier in FDD mode and configured with all control channels to support downlink transmission.

[Modify the text on the page 304, line 17 as follows]

Partially Configured Carrier: A carrier configured for downlink only transmission in TDD or a downlink carrier without paired UL carrier in FDD mode. The partially configured carriers may be used only in conjunction with a primary carrier and cannot operate standalone to offer AAI services for an AMS.

[Modify the text on the page 436, line 42 as follows]

In a TDD frame with DL/UL ratio of D : U, the first contiguous D AAI subframes and the remaining U AAI subframes are assigned for DL and UL, respectively, where D + U = 8 for 5, 10 and 20 MHz channel bandwidths, D + U = 7 for 8.75 MHz channel bandwidth, and D + U = 5 for 7 MHz channel bandwidth. The ratio of D : U shall be selected from one of the following values: 8:0, 6:2, 5:3, 5:2, 4:3, 4:4,3:4 or 3:5 for 5, 10 and 20 MHz channel bandwidths, and 4:2, 3:3, 3:2 or 2:3 for 7 MHz channel bandwidth and 5:2, 4:3,4:2, 2:4 or 3:4 for 8.75 MHz channel bandwidth.

-------------------------------------------------------------End of the Text--------------------------------------------------------

# References

- IEEE P802.16m/D6, “Advanced Air Interface (Draft),” May. 2010.