| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Clarification on BR-ACK A-MAP IE (Section 16.3.5.5) |
| Date Submitted | 2010-09-08 |
| Source(s) | Hyunkyu Yu, Jaehyuk Jang Samsung Electronics Co., Ltd. | hk.yu@samsung.com |
| Re: | Comments on IEEE P802.16m/D8 for IEEE 802.16 WG SB_16m. |
| Abstract | The contribution clarifies the text about BR-ACK A-MAP IE. |
| Purpose | To be discussed and adopted by TGm |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Clarification on BR-ACK A-MAP IE (Section 16.3.5.5)

Hyunkyu Yu, Jaehyuk Jang

# Introduction

This contribution clarifies the text about BR-ACK A-MAP IE.

- HFA start offset

  - This field currently has 3 bits. But, 6 bits are required to indicate the start resource index of HFA.

- Reserved

  - BR-ACK A-MAP IE is not segmentable, and thus the reserved bits should be set to obtain total 40 bits.

# Proposed Text Changes

[Change the following text, at line 41 in page 648, section 16.3.5.5.2.4.12, as]

------------------------------------------------Start proposed text----------------------------------------------------------------

16.3.5.5.2.4.12 BR ACK A-MAP IE

The BR Acknowledgement A-MAP IE indicates the decoding status of the BR opportunities in the UL frame identified by BR ACK offset BR_ACK_Offset. All the successfully received preamble sequences, if present, shall be included in an ascending order. BR opportunities are encoded in ascending order based on the number of the uplink subframe in which they are contained in a single or multiple BR-ACK A-MAP IEs. The maximum number of BR ACK A-MAP IEs in a subframe is 2. The BR-ACK A-MAP IE is not segmentable. In addition, the BR-ACK A-MAP IE also includes the allocation information for the fixed sized BR header (refer to 16.2.2.1.3.1). The UL resource and HFA shall be allocated to the preamble sequences whose grant indicator is ‘1’. The allocations shall be ordered based on the index of preamble sequences arranged in an ascending order. If UL resource for the BR header is not allocated through the BR-ACK A-MAP IE, CDMA Allocation A-MAP IE is used for the UL resource allocation. For the UL HARQ burst allocated through the BR-ACK A-MAP IE, the maximum number of the HARQ retransmissions is set to the default value defined in 16.2.14.2. Non-adaptive HARQ re-transmission is used.

Table 861—BR-ACK A-MAP IE*

| Syntax | Size in bits | Description/Notes |
| --- | --- | --- |
| BR-ACK_A-MAP_ IE() { | - | - |
| A-MAP IE Type | 4 | BR-ACK A-MAP IE |
| … | … | … |
| if (MSB of resource start offset != 0b11) { |  |  |
| … | … | … |
| HFA start offset | 3 6 | This field is start offset of HARQ Feedback Allocation. |
| … | … | … |
| } |  |  |
| … | … | … |
| Grant indicator | 1 | To indicate whether grant of BR Header for the BR preamble sequence index is included or not If this bit is set, the UL resource is allocated. 0b0: No UL resource allocation 0b1: UL resource allocation for BR with STID header |
| … | … | … |
| Reserved | variable | For byte alignment To reach 40-bit assignment A-MAP IE size. |
| } |  |  |

*...

-------------------------------------------------End proposed text----------------------------------------------------------------