| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Updates to Annexes T and U in IEEE P802.16m/D10 |
| Date Submitted | 2010-12-17 |
| Source(s) | Reza Arefi Roshni Srinivasan, Intel Corporation Barry Lewis Jeongho Park Samsung Electronics Roger Marks WiMAX Forum | reza.arefi@intel.com roshni.m.srinivasan@intel.com barry.lewis@samsung.com jeongho.jh.park@samsung.com r.b.marks@ieee.org *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | IEEE Sponsor Ballot of P802.16m/D10 |
| Abstract | This contribution proposes updates to Annex T and U containing radio specifications. |
| Purpose | This is proposed as the basis of a 802.16m Sponsor Ballot Recirc comment. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Copyright Policy | The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Updates to Annexes T and U in IEEE P802.16m/D10

Roshni Srinivasan, Reza Arefi, Intel Corp.

Barry Lewis, Jeongho Park, Samsung Electronics

Roger Marks, WiMAX Forum

This contribution proposes changes to Annexes T & U in P802.16m/D10. Changes to subclause 2 that are consistent with the proposed update are also included.

Proposed text is underlined in blue, text in P802.16m/D10 that has been deleted is marked in red and struck through and text in P802.16m/D10 is shown in black.

References

[1] Recommendation ITU-R SM.329-10, for sections U.1.2 and U.2.2

[2] ITU-R 5D/542 (IEEE L802.16-09/010Xr5), Submission of a candidate IMT-Advanced RIT based on IEEE 802.16, October 2009.

___________________________Begin Proposed Text Change #1______________________

2. Normative references

WiMAX Forum WMF-T23-005-R015v04, “WiMAX Forum® Mobile Radio Specification,” September 2010.

___________________________End Proposed Text Change #1______________________

--------------------------------------------Begin Proposed Text Change #2--------------------------------

Annex T

(NormativeInformative)

Supported Frequency Bands for WirelessMAN-Advanced Air Interface

The standard supports deployment of the WirelessMAN-Advanced Air Interface in all bands identified for IMT in ITU-R Radio Regulations. In addition, the standard supports deployment of the WirelessMAN-Advanced Air Interface in non-IMT bands below 6 GHz allocated to the Fixed Service and/or Mobile Service. See the table below for more information on some, but not all, of the bands in which the standard can be deployed.

Table T.1 Some of supported frequency bands

| UL AMS Transmit Frequency (MHz) | DL AMS Receive Frequency (MHz) | Duplex Mode |
| --- | --- | --- |
| 2300-2400 | 2300-2400 | TDD |
| 2305-2320, 2345-2360 | 2305-2320, 2345-2360 | TDD |
| 2345-2360 | 2305-2320 | FDD |
| 2496-2690 | 2496-2690 | TDD |
| 2496-2572 | 2614-2690 | FDD |
| 3300-3400 | 3300-3400 | TDD |
| 3400-3600 | 3400-3600 | TDD |
| 3400-3500 | 3500-3600 | FDD |
| 3600-3800 | 3600-3800 | TDD |
| 1710-1770 | 2110-2170 | FDD |
| 1920-1980 | 2110-2170 | FDD |
| 1710-1755 | 2110-2155 | FDD |
| 1710-1785 | 1805-1880 | FDD |
| 1850-1910 | 1930-1990 | FDD |
| 1710-1785, 1920-1980 | 1805-1880, 2110-2170 | FDD |
| 1850-1910, 1710-1770 | 1930-1990, 2110-2170 | FDD |
| 698-862 | 698-862 | TDD |
| 776-787 | 746-757 | FDD |
| 788-793, 793-798 | 758-763, 763-768 | FDD |
| 788-798 | 758-768 | FDD |
| 698-862 | 698-862 | TDD/FDD |
| 824-849 | 869-894 | FDD |
| 880-915 | 925-960 | FDD |
| 698-716, 776-793 | 728-746, 746-763 | FDD |
| 1785-1805, 1880-1920, 1910-193, 2010-2025, 1900-1920 | 1785-1805, 1880-1920, 1910-193, 2010-2025, 1900-1920 | TDD |
| 450-470 | 450-470 | TDD |
| 450.0-457.5 | 462.5-470.0 | FDD |

Subclause 1.1 of WiMAX Forum WMF-T23-005-R015v04 identifies some of the bands in which systems

based on the standard can be deployed, along with the channel bandwidth and duplex mode.

--------------------------------------------End Proposed Text Change #2--------------------------------

--------------------------------------------Begin Proposed Text Change #3--------------------------------

Annex U

(Normative)

Radio Specifications for WirelessMAN-Advanced Air Interface

WirelessMAN system transmitters shall conform with unwanted emission specifications. “Subclause 2.1.1 of WiMAX Forum WMF-T23-005-R015v04 specifies the center frequency step size for

the WirelessMAN-Advanced Air Interface.”

“Subclause 2.1.2 of WiMAX Forum WMF-T23-005-R015v04 specifies the RF profile for the Wireless-

MAN-Advanced Air Interface.”

“Subclause 2.1.3 of WiMAX Forum WMF-T23-005-R015v04 specifies the power class profile for the WirelessMAN-Advanced Air Interface.”

“Subclauses 2.1.4-2.2.6 of WiMAX Forum WMF-T23-005-R015v04 specify the unwanted emissions requirements for the WirelessMAN-Advanced Air Interface.”

Local and regional regulations should be consulted for unwanted emission specifications for the appropriate frequency band for each WirelessMAN-Advanced band class. In the absence of any local/regional regulation the following specifications shall apply.

This annex uses the following definitions:

- ChBW				Nominal channel bandwidth

- fc					Channel center frequency

- (f					Absolute value of frequency offset from fc

- Integration Bandwidth 	The frequency range over which the emission power is integrated

- Fue          				Upper edge of the band (either uplink or downlink whichever larger)

U.1 AMS Specifications

U.1.1 AMS spectral masks

The following tables U.1, U.2 and U.3 specify the out-of-band emission requirements for AMSs.

Table U.1 AMS Channel Mask for 5 MHz Bandwidth

| No | ∆f (MHz) | Integration Bandwidth (kHz) | Maximum Allowed Emission Level (dBm/Integration Bandwidth) as measured at the antenna port |
| --- | --- | --- | --- |
| 1 | 2.5 ( f < 3.5 | 50 | -13 |
| 2 | 3.5 ( f ( 12.5 | 1000 | -13 |

Note: The first measurement position with a 50 kHz filter is at (f equal to 2.525 MHz; the last is at (f equal to 3.475 MHz. The first measurement position with a 1 MHz filter is at (f equal to 4.0 MHz; the last is at (f equal to 12.0 MHz.

Table U.2 AMS Channel Mask for 10 MHz Bandwidth

| No | ∆f (MHz) | Integration Bandwidth (kHz) | Maximum Allowed Emission Level (dBm/Integration Bandwidth) as measured at the antenna port |
| --- | --- | --- | --- |
| 1 | 5 ( f < 6 | 100 | -13 |
| 2 | 6 ( f ( 25 | 1000 | -13 |

Note: The first measurement position with a 100 kHz filter is at (f equal to 5.050 MHz; the last is at (f equal to 5.950 MHz. The first measurement position with a 1 MHz filter is at (f equals to 6.5 MHz; the last is at (f equal to 24.5 MHz.

Table U.3 AMS Channel Mask for 20 MHz Bandwidth

| No | ∆f (MHz) | Integration Bandwidth (kHz) | Maximum Allowed Emission Level (dBm/Integration Bandwidth) as measured at the antenna port |
| --- | --- | --- | --- |
| 1 | 10 ( f < 11 | 200 | -13 |
| 2 | 11 ( f ( 50 | 1000 | -13 |

Note: The first measurement position with a 200 kHz filter is at (f equal to 10.1 MHz; the last is at (f equal to 10.9 MHz. The first measurement position with a 1 MHz filter is at (f equal to 11.5 MHz; the last is at (f equal to 49.5 MHz.

U.1.2 AMS spurious emissions requirements

The following table specifies the spurious emission requirements for AMSs.

Table U.4 AMS Spurious Emissions Requirements

| No | Spurious Emission Frequency, f | Measurement bandwidth | Maximum Allowed Emission Level (dBm) |
| --- | --- | --- | --- |
| 1 | 9 kHz ( f < 150 kHz | 1 kHz | -36 |
| 2 | 150 kHz ( f < 30 MHz | 10 kHz | -36 |
| 3 | 30 MHz ( f < 1000 MHz | 100 kHz | -36 |
| 4 | 1 GHz ( f < 5Fue | 30 kHz, if 2.5ChBW ( ∆f < 10ChBW 300 kHz, if 10ChBW ( ∆f < 12ChBW 1 MHz , if 12ChBW ( ∆f | -30 |

U.1.3 AMS Power classes

Table U.5 provides the list of AMS power classes.

Table U.5 AMS Power Classes

| Class Identifier | Pnom (dBm) |
| --- | --- |
| Power Class 1 | 20 |
| Power Class 2 | 23 |
| Power Class 3 | 26 |

In Table U.5, Pnom is the declared maximum conducted transmit power.

In the power classes of Table U.5, tolerances are not included. In general, tolerances associated with Pnom depend on various parameters including MCS level, spectrum band span (associated with band edge), etc.  Generic and band-specific tolerances associated with these parameters may be added, if applicable.

U.2 ABS Specifications

U.2.1 ABS spectral masks

The following tables U.6, U.7 and U.8 specify the out-of-band emission requirements for ABSs.

Table U.6 ABS Channel Mask for 5 MHz Bandwidth

| No | ∆f (MHz) | Integration Bandwidth (kHz) | Maximum Allowed Emission Level (dBm/Integration Bandwidth) as measured at the antenna port |
| --- | --- | --- | --- |
| 1 | 2.5 ( f < 7.5 | 100 | -7-7(f -2.55)/5 |
| 2 | 7.5 ( f ( 12.5 | 100 | -14 |

Note: The first measurement position with a 100 kHz filter is at (f equal to 2.550 MHz; the last is at (f equal to 12.450 MHz.

Table U.7 ABS Channel Mask for 10 MHz Bandwidth

| No | ∆f (MHz) | Integration Bandwidth (kHz) | Maximum Allowed Emission Level (dBm/Integration Bandwidth) as measured at the antenna port |
| --- | --- | --- | --- |
| 1 | 5 ( f <10 | 100 | -7-7(f -5.05)/5 |
| 2 | 10 ( f <15 | 100 | -14 |
| 3 | 15 ( f (25 | 1000 | -13 |

Note: The first measurement position with a 100 kHz filter is at (f equal to 5.05 MHz; the last is at (f equal to 14.95 MHz. The first measurement position with a 1 MHz filter is at (f equal to 15.5 MHz; the last is at (f equal to 24.5 MHz.

Table U.8 ABS Channel Mask for 20 MHz Bandwidth

| No | ∆f (MHz) | Integration Bandwidth (kHz) | Maximum Allowed Emission Level (dBm/Integration Bandwidth) as measured at the antenna port |
| --- | --- | --- | --- |
| 1 | 10 ( f < 15 | 100 | -7-7(f -10.05)/5 |
| 2 | 15 ( f < 20 | 100 | -14 |
| 3 | 20 ( f ( 50 | 1000 | -13 |

Note: The first measurement position with a 100 kHz filter is at (f equal to 10.05 MHz; the last is at (f equal to 19.95 MHz. The first measurement position with a 1 MHz filter is at (f equal to 20.5 MHz; the last is at (f equal to 49.5 MHz.

U.2.2 ABS spurious emissions requirements

The following table specifies the spurious emission requirements for ABSs.

Table U.9 ABS Spurious Emissions Requirements

| No | Spurious Emission Frequency, f | Measurement bandwidth | Maximum Allowed Emission Level (dBm) |
| --- | --- | --- | --- |
| 1 | 9 kHz ( f < 150 kHz | 1 kHz | -36 |
| 2 | 150 kHz ( f < 30MHz | 10 kHz | -36 |
| 3 | 30 MHz ( f < 1000 MHz | 100 kHz | -36 |
| 4 | 1 GHz ( f < 5Fue | 30 kHz, if 2.5ChBW ( ∆f < 10ChBW 300 kHz, if 10ChBW ( ∆f < 12ChBW 1 MHz, if 12ChBW ( ∆f | -30 |

------------------------------------------End Proposed Text Change #3--------------------------------