| Title | LB Issue- #:25 Comments:524 |
| --- | --- |
| Date Submitted | September 2006 |
| Source(s) | Vivek Gupta |  |
| Ref: |  |
| Abstract | This contribution provides resolutions for LB-#1 Issue related to specifying Vendor specific codes for LinkDown indication. |
| Purpose | Discuss and adopt in the draft. |
| Notice | This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

Remedy 1:

Add following text on page 78, line 16, Draft D01.09

“The reason code for Link_Down may be one or combination of the following reasons. Vendors may specify their own specific reasons by using the vendor specific reason code range.

“