| Project | IEEE 802.21 MIHS <http://www.ieee802.org/21/> |
| --- | --- |
| Title | Clarification of MIH_LINK_SAP |
| DCN | 21-06-0784-00-0000 |
| Date Submitted | November 2006 |
| Source(s) | Kentaro Ishizu, Yoshia Saito, Masahiro Kuroda, Ryoichi Komiya | NICT |
| Re: | IEEE 802.21 session #17 in November 2006 |
| Abstract | This document clarifies the definition of MIH_LINK_SAP which is currently ambiguous in the specification. |
| Purpose | Discuss and adopt in the draft |
| Notice | This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that IEEE 802.2 may make this contribution public. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

This document describes proposals to the IEEE 802.21 standard draft D02.00.

We propose to clarify MIH_LINK_SAP as a media-independent interface between MIHF and lower layers.

We propose to modify the text of D02 as below ((1) – (4)).

- Replace “technology dependent interface (media specific SAPs)” by “technology independent interface (the MIH_LINK_SAP)” in the last paragraph in section 1.2

- Replace “the abstract media-dependent interface” by “the media independent interface” in section 5.5

- MIH_LINK_SAP: This represents the media independent interface of MIHF with the lower layers of the protocol stacks.

- Move description on MIH_LINK_SAP from 7.1.1 to 7.1.2

- Move section 5.6.1.1 to under 5.6.2 with modification as below

This SAP defines the media independent link layer interface between MIHF and different link layer technologies. Amendments of the link-layer technologies are suggested to have MIH_LINK_SAP.

(5) Modify 5.6 and 5.6.1 with the following text and figure specified in blue

- Service Access Points (SAPs)

The MIHF exchanges messages with other layers and functional planes using Service Access Points (SAPs). Each SAP consists of a set of service primitives that specify the information to be exchanged and the format of the information exchanges.

The specification of the MIHF includes the definition of SAPs that are media-independent (i.e., transparent to the interface types that the mobile node may support) and recommendations to define or extend other SAPs that are media-dependent. Media-independent SAPs allow the MIHF to provide services to the upper layers of the mobility-management protocol stack, the link layers, the network management plane, and the data bearer plane. The MIH_SAP and associated primitives provide the interface from MIHF to the upper layers of the mobility-management stack. Upper layers need to subscribe with MIHF as users to receive MIHF generated events and also for link layer events that originate at layers below the MIHF but may be passed on to MIHF users through MIHF. MIHF users may directly send commands to the local MIHF using the service primitives of the MIH_SAP. For communication between two remote MIHF, the propagation from the local MIHF to the remote MIHF relies on MIH protocol messages.

Media-dependent SAPs allow the MIHF to use services from the lower layers of the mobility management protocol stack and their management planes. All inputs (including the events) from the lower layers of the mobility-management stack into the MIHF are provided through existing media-specific SAPs such as MAC SAPs, PHY SAPs, and LLC SAPs. Link Commands generated by the MIHF to control the PHY and MAC layers during the handover are part of the media specific MAC/PHY SAPs and are already defined elsewhere.  Figure 12 shows the key MIHF related SAPs for different networks.

- Figure 12 depicts the general SAP model for the media-independent handover. MIHF provides four Service Access Points: The MIH_LINK_SAP provides interface between the MIHF and link-layer technologies such as IEEE 802.2, 802.3, 802.11, 802.16 and 3GPP/2. Amendments are suggested to the technologies to have MIH_LINK_SAP.

- The MIH_SAP provides interface between the MIHF and upper layers of the mobility-management stack. The upper layers need to subscribe with MIHF as users to receive MIHF generated events and also for link layer events that originate at layers below the MIHF but may be passed on to MIHF users through MIHF. MIHF users may directly send commands to the local MIHF using the service primitives of the MIH_SAP. For communication between two remote MIHF, the propagation from the local MIHF to the remote MIHF relies on MIH protocol messages.

- The MIH_NMS_SAP provides interface between the MIHF and the Network Management System (NMS). The NMS configures parameters in the MIHF.

- The MIH_NET_SAP provides interface between the MIHF and the transport services on the local node to communicate with the MIHF on a remote node.

- Relationship between different MIHF SAPs

- Media Dependent SAPs

Each technology specifies its own technology dependent SAPs. MIH_LINK_SAP would be mapped to the technology dependent SAPs.