| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | IEEE 802.16g Update for IEEE 802.21 MIH Information Service Support before Network Entry |
| Date Submitted | November, 2006 |
| Source(s) | Ronny Kim, Jin Lee LG Electronics, Inc. 533,Hogye-1dong,Dongan-gu, Anyang-shi, Kyongki-do, Korea | Voice: +82-31-450-1879 Fax: +82-31-450-7912 [mailto: ronny, jins978@lge.com] |
| Re: | IEEE 802.16 Session #16 in Dallas |
| Abstract | This contribution proposes the updates of IEEE 802.16g D5 document in order to support IEEE 802.21 Media Independent Information Services. |
| Purpose | Update 802.16g draft to support Media Independent Handover |
| Notice | This document has been prepared to assist IEEE 802.16. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy and Procedures | The contributor is familiar with the IEEE 802.16 Patent Policy and Procedures <http://ieee802.org/16/ipr/patents/policy.html>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard." Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication. Please notify the Chair <mailto:chair@wirelessman.org> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.16 Working Group. The Chair will disclose this notification via the IEEE 802.16 web site <http://ieee802.org/16/ipr/patents/notices>. |

# Information Service through 802.16 before Network Entry Procedure

Ronny (Yong-Ho) Kim, Jin Lee 
LG Electronics, Inc.

# 1. Introduction

# In order for MS to enter 802.16 network for the first time, MS shall obtain UCD and DCD then will commence network entry procedure by initiating initial ranging procedure. In handover between technologies, e.g., handover from IEEE 802.11 network to IEEE 802.16 network, or in roaming between IEEE 802.16 networks, it has become important to perform network selection. Therefore, it is beneficial for MS to acquire network selection related information before network entry so the MS could make more informed decision about which network is efficient to associate with.

1.1 Interworking procedures: MIH Information Services

This clause describes the actions and the procedures to enable network selection for IEEE 802.16 MS as well as the seamless interworking of a multi-access capable MSs with other non-802.16 access technologies or when other non-802.16 specific network protocols are involved. It specifies the transport mechanisms to advertising services for network selection or other purposes while clients are in the un-associated state. IEEE 802.21 MIH capability is included in the DCD in order for MSs to use network selection using IEEE 802.21 Information service. IEEE 802.21 Information service is used for Queries and Query Responses. The network selection information delivery mechanism using IEEE 802.21 Information service is supported using two options:

i) Multicast mechanism

ii) Unicast mechanism

# Multicast Mechanism

The MS obtains the IEEE 802.21 capability from DCD. In the IEEE 802.21 capability indications of DCD, three key services supported by the current BS are indicated. When information service capability is indicated, after initial ranging procedure, MS can send Queries embedded in MOB_MIH-MSG without entering network. BS can identify MSs with MIH capability with MAC version received from the MS during initial ranging procedure. Upon receipt of MOB_MIH-MSG MAC management message BS generates a MOB_MIH-MSG with Query ID TLV, Cycle TLV and Multicast CID TLV. NCMS of the BS forwards or proxies the query request to the backbone network to retrieve the query results. This NCMS procedure with backbone network is out of scope of IEEE 802.16g and shall not specified in the draft. The response message from the backbone network (information server) will be queued in the BS for multicast delivery at later time. BSs scheduling information of multicast delivery is informed to the MS in the Cycle TLV of MOB_MIH-MSG which was transmitted to the MS. MS shall monitor the frame indicated by Cycle TLV. If the MOB_MIH-MSG message is not delivered MS shall monitor next cycle for the message. MS can wait until predetermined counter is exhausted. While waiting for the frame indicated by Cycle TLV, MS does not need to remain active. BS shall only transmit the MOB_MIH-MSG with Query Response only in the frame indicated by Cycle TLV. MOB_MIH-MSG is delivered using Multicast CID given to the MSs. MOB_MIH-MSG carrying Query Response MIH frame TLV includes Query ID, corresponding Query Request Frame (optional), Query result frame which is received from the backbone network. When encapsulating query response MIH frame is too big to include in the MOB_MIH-MSG message, MIH frame can be fragmented using Fragmentation/ Packing TLV. When query response MIH frame which is transmitted using same Multicast CID is small enough to combine, multiple small MIH frames can be packed using Fragmentation/Packing Information TLV. The following figure shows the message sequence.

# Figure 1. Network Selection information delivery using multicast delivery method.

# Unicast Mechanism

The MS obtains the IEEE 802.21 capability from DCD. In the IEEE 802.21 capability indications of DCD, three key services supported by the current BS are indicated. When information service capability is indicated, after initial ranging procedure, MS can send Queries embedded in MOB_MIH-MSG without entering network. BS can identify MSs with MIH capability with MAC version received from the MS during initial ranging procedure. Upon receipt of MOB_MIH-MSG MAC management message BS generates a MOB_MIH-MSG with Query ID TLV and Cycle TLV. NCMS of the BS forwards or proxies the request to the backbone network to retrieve the query results. This NCMS procedure with backbone network is out of scope of IEEE 802.16g and shall not specified in the draft. The response message from the backbone network (information server) will be queued in the BS for unicast delivery at later time. BSs scheduling information of query response delivery is informed to the MS in the Cycle TLV of MOB_MIH-MSG which was transmitted to the MS. MS shall check whether MIH_Polling_IE is included in the UL-MAP of the frame indicated by Cycle TLV. When MIH_Polling_IE exists in the UL-MAP, MS shall send MOB_MIH-MSG message with Query ID TLV which was received from the BS. Upon receipt of the MOB_MIH-MSG with the Query ID, BS can make sure whether MS still stays to receive Query response message and BS transmits MOB_MIH-MSG containing Query Response to the MS with the primary CID. BS only includes MIH_Polling_IE in the UL-MAP when the Query Response is received from the backbone network. MS can wait the delivery of MIH_Polling_IE until predetermined counter is exhausted. While waiting for the frame indicated by Cycle TLV, MS does not need to remain active. MOB_MIH-MSG carrying Query Response MIH frame TLV includes Query ID TLV, and Query result frame TLV which is received from the backbone network. Because the primary management connection is used for the unicast delivery, packing or fragmentation of the MOB_MIH-MSG message is achieved using the mechanism described in the IEEE 802.16 2004 specification. The following figure shows the message sequence.

# Figure 2. Network Selection information delivery using unicast delivery method.

# 2. Proposed Text Change

# Remedy 1:

MIH Capability advertisement through DCD shall carry more capabilities using reserved bits.

[In 11.4.1 DCD channel encoding, page 20, line 15, Modify]:

| Name | Type | Length | Value | PHY Scope |
| --- | --- | --- | --- | --- |
| MIH Capability Support | 55 | 1 | Indicates the capability of IEEE 802.21 Media Independent Handover Services. Setting each bit to 1 indicates corresponding service is supported. Setting bit # 0 to 1 indicates MIH services indicated through bit #1~3 are supported by the current BS. Setting more than one of bit #1~3 without setting bit #0 indicates existence of an MIH service entity within the Layer 2 broadcast domain of the current BS. In this case transport MIH MAC management message (MOB_MIH-MSG) shall not be supported by the BS. Bit #0=MIH (Media Independent Handover) Capability not supported 1=MIH Capability supported Bit #1 = Event Service support Bit #2 = Command Service support Bit #3 = Information Service support Bit #4~7: reserved | All |

# Remedy 2:

In order for an MS to negotiate MIH capability, MIH capability negotiation during registration is added in the current draft. However, more detailed capability negotiation is required.

[In 11.7.26 MIH Capability Supported TLV, page 20, line 55, modify]:

The "MIH Capability Supported" TLV indicates if MIH is supported. MS and BS that support the MIH handover function shall identify themselves by inclusion of the MIH capability supported. MS and BS that do not support the 802.21 MIH handover function shall not support the MOB_MIH-MSG management message. However, BS may indicate the existence of the MIH service entity within the layer 2 broadcast domain of the current BS by setting bit # 0 to be 0 and corresponding services bits of MIH service entity to be 1. In this case, BS doesn’t support MOB_MIH-MSG MAC management message and MN shall access the MIH service entity using layer 2 data frames.

[In 11.7.26 MIH Capability Supported TLV, page 21, line 32,modify and  move to line 61 page 20]:

| Type | Length | Value | Scope |
| --- | --- | --- | --- |
| 46 | 1 | Indicates the capability of IEEE 802.21 Media Independent Handover Services. Setting each bit to 1 indicates corresponding service is supported. Setting bit # 0 to 1 indicates MIH services which further indicated through bit #1~3 are supported. In REG-RSP transmitted from BS, more than one of bit #1~3 without setting bit #0 may be set which indicates existence of an MIH service entity within the Layer 2 broadcast domain of the current BS. In this case transport MIH MAC management message (MOB_MIH-MSG) shall not be supported by the BS. Bit #0=MIH (Media Independent Handover) Capability not supported 1=MIH Capability supported Bit #1 = Event Service support Bit #2 = Command Service support Bit #3 = Information Service support Bit #4~7: reserved | REG-REQ REG-RSP |

# Remedy 3:

When MOB_MIH-MSG is used to carry IEEE 802.21 information service Query response either over Multicast CID or Primary management CID, MOB_MIH-MSG may include several TLVs.

When delivery method is multicast, fragmentation and packing TLV is included to fragment the long size Query response MIH frame or pack small size Query response MIH frames. Cycle TLV for MS power management, Delivery Method and Status TLV, Multicast CID TLV, Query ID TLV are added for network selection information service access.

[In 11.20 MIH message encoding, page 25, line 47, Modify: Remove Name Column, Insert Scope Column]:

11.20 MIH message encodings

11.20.1 MIH Function frame

These This TLV is used to management frames carry MIHF Frame described in subclause 8.2.1 of IEEE Std 802.21 under L2 transport option 2 of Table 1723, subclause 8.2. MIH function frame shall be received transmitted using C-XXX-IND primitive from/to NCMS.

| Name | Type | Length | Value | Scope |
| --- | --- | --- | --- | --- |
| MIHF_Frame_package | ?? | variable | MIHF Frame described in subclause 8.2.1 of IEEE 802.21 under transport option 3 of Table 17, subcluse 8.2. | MOB_MIH-MSG |

[In 11.20 MIH message encoding, page 25, line 47, Insert]:

11.20.1 MIH Frame fragmentation and packing

# This TLV shall only be included when MOB_MIH-MSG is transmitted over Multicast CID. This TLV shall be located before MIH Function frame TLV.

| Type | Length | Value | Scope |
| --- | --- | --- | --- |
| ?? | 1 | Indicates whether one MIH Function frame is fragmented into several MIH Function frame TLVs. Also indicates whether more than 2 MIH Function frames are packed into a one MIH Function frame TLV. Bit #0: indicates whether packing is used (when there are more than two MIH frames in a MIH Function frame TLV) Bit #1: indicates whether one MIH frame is fragmented or not Bit #3~4: indicates first fragment, continuing fragment, last fragment. 0b01: first fragment 0b10: continuing (middle) fragment 0b11: last fragment Bit #4~7: Sequence number. When fragmentation is used, BS shall assign a sequence number randomly. Number is increased by one for continuing fragment transmission. | MOB_MIH-MSG |

11.20.2 Cycle

# Cycle TLV is included to indicate when Query Response is expected. MS shall only to check the cycle for the MOB_MIH-MSG transmission in case of multicast transmission method or the MIH_Polling_IE in the UL-MAP in case of unicast transmission method, and MS can switch to power saving mode while waiting for the Cycle.

| Type | Length | Value | Scope |
| --- | --- | --- | --- |
|  | 1 | Cycle in which the Query Response may be transmitted. | MOB_MIH-MSG |

11.20.3 Delivery Method and Status Code

This TLV is included in order for MS and BS to negotiate preferred delivery method (multicast or unicast). BS may transmit the status of the requested information. When MS include this TLV, MS shall set the status code as to be null (0x0000).

| Type | Length | Value | Scope |
| --- | --- | --- | --- |
|  | 1 | Bit #0: Unicast Bit#1: Multicast Bit#2~6: Status code 0x0000: Null 0x0001: MIH_Not_Supported 0x0002: Requested_Delivery_Method_Not_Supported 0x0003: Request_Info_Not_Available 0x0004: Response_Not_Received Bit#7: Reserved | MOB_MIH-MSG |

11.20.4 Multicast CID

When delivery method is set to be multicast, BS shall include this TLV for future Query Response delivery.

| Type | Length | Value | Scope |
| --- | --- | --- | --- |
|  | 2 | Multicast CID | MOB_MIH-MSG |

11.20.5 Query ID

Query ID is returned by the BS in the MOB_MIH-MSG for the MS’s Query request to indicate that a backbone query through NCMS is being carried out on behalf of the MS. When the MS transmit the MOB_MIH-MSG polled by MIH_Polling_IE, the MS shall use the Query ID to retrieve the response. The Query ID is included in the MOB_MIH-MSG carrying Query Response in both unicast and multicast delivery methods.

| Type | Length | Value | Scope |
| --- | --- | --- | --- |
|  | 1 | To be used for request to retrieve the response in the unicast mechanism. BS shall include this TLV in MOB_MIH-MSG carrying Query Response. | MOB_MIH-MSG |

# Remedy 4:

In order to deliver MIH Frame that contains network selection information, MOB_MIH-MSG may support either multicast or unicast. Therefore, MOB_MIH-MSG could be transmitted using Multicast CID or Primary mangement CID.

[In 6.3.2.3 MAC management message, page 12, line 46, Modify Table 14 as indicated]:

Table 14 - MAC management messages

| Type | Message name | Message description | Connection |
| --- | --- | --- | --- |
| 67 | MOB_MIH-MSG | MIH Payload Transfer | Primary management Multicast |

[In 6.3.2.3.62 MIH Payload Transfer (MOB_MIH-MSG) message, page 14, line 6, Modify as it follows]:

The 802.16 entity may send or receive the MOB_MIH-MSG message to or from the peer 802.16 entity in order to convey MIHF Frames carrying the 802.21 MIH Protocol messages. The message shall be transmitted on the Primary Management connection or Multicast connection.

# Remedy 5:

Management CID related timer T9 Timer operation and counter Update

[In 11.4.1 DCD channel encoding, page 20, line 15, Modify]:

Table 343 – Parameters and constants

| System | Name | Time reference | Minimum Value | Default Value | Maximum Value |
| --- | --- | --- | --- | --- | --- |
| BS | T9 | Registration Timeout, the time allowed between the BS sending a RNG-RSP (success) to an SS, and receiving a SBC-REQ from that same SS. When BS receives MOB_MIH-MSG, the BS stops T9 timer. | 300ms | 300ms |  |
| BS | T47 | CID Timeout, the time allowed between receiving a MOB_MIH-MSG from an SS, and receiving a SBC-REQ from the same SS. If the BS does not receive a SBC-REQ within the time, management CIDs shall be released. |  |  |  |
| MS, BS | Query Retry Counter | MS: In case of multicast method, MS shall monitor the cycle for transmission of MOB_MIH-MSG up to the Query Retry Counter value. BS: In case of unicast method, BS shall poll the MS to deliver MOB_MIH-MSG carrying Query Response up to the Query Retry Counter value. | 3 | 3 |  |

# Remedy 7:

[8.4.5.4.4.1 UL-MAP Extended IE format, page 16, line 3, Insert subsection 8.4.5.4.4.1 as it follows]:

8.4.5.4.4.1 UL-MAP Extended IE format

Table 290a. Extended UIUC Code Assignment for UIUC 15

| Extended UIUC | Usage |
| --- | --- |
| 00 | Power_control_IE |
| 01 | Mini-subchannel_allocation_IE |
| 02 | AAS_UL_IE |
| 03 | CQICH_Alloc_IE |
| 04 | UL_Zone_IE |
| 05 | PHYMOD_UL_IE |
| 06 | MIMO_UL_Basic_IE |
| 07 | UL-MAP_Fast_Tracking_IE |
| 08 | UL_PUSC_Burst_Allocation_in_Other_Segment_IE |
| 09 | Fast_Ranging_IE |
| 0A | UL_Allocation Start IE |
| 0B | MIH_Polling_IE |
| 0B0C…0F | Reserved |

[8.4.5.4.29 MIH_Polling_IE, page 16, line 32, Insert subsection 8.4.5.4.29  as it follows]:

8.4.5.4.29 MIH_Polling_IE

BSs scheduling information of query response delivery is informed to the MS in the Cycle TLV of MOB_MIH-MSG which was transmitted to the MS. In case of unicast delivery method, MS shall check whether this IE is included in the UL-MAP of the frame indicated by Cycle TLV. When this IE exists in the UL-MAP, MS send MOB_MIH-MSG message in the assigned region in the IE with Query ID TLV which was received from the BS. MS may be able to wait the delivery of MIH_Polling_IE until predetermined counter, Query Retry Counter is exhausted.

Table 302z. MIH_Polling_IE

| Syntax | Size | Notes |
| --- | --- | --- |
| MIH_Polling_IE () { |  |  |
| Extended UIUC | 4bits | MIH_Polling = 0x0B |
| Length | 4bits |  |
| Query ID | 16bits |  |
| Duration | 10 bits | OFDMA slots for the uplink bandwidth |
| Reserved |  |  |
| } |  |  |