| Project | IEEE 802.21 Media Independent Handover Services <http://www.ieee802.org/21/> |
| --- | --- |
| Title | MIH Handover Protocol |
| Date Submitted | March 9, 2007 |
| Source(s) | Junghoon Jee, Eunah Kim ETRI 161 Gajeong-Dong, Yuseong-Gu Daejeon, 305-700, KOREA | Voice: +82-42-860-5126 Fax: +82-42-861-5404 {jhjee, eakim}@etri.re.kr |
| Re: | IEEE 802.21 Session #NN in Caribe Royale Resort, Orlando |
| Abstract | This contribution proposes amendments of section 8, Media independent handover protocol. The proposed modification of the overall structure of the section 8 is suggested in this version of the document. The complete texts will be filled up by updating this document. |
| Purpose | Adoption |
| Notice | This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

- Background

The # 4372 of LB_1c pointed out the need for restructure of the section 8, Media Independent Handover Protocol section. Even if the contribution 21-07-0083 provides a table of contents for restructuring the section 8, complete texts for the modification was not provided. This contribution provides the complete amendments for the section 8. Through this initial version of this contribution, some modification of the overall structure of the section 8 is revisited. After having a consensus about the overall structure of the section 8, the complete texts will be filled up by updating this document.

2. Suggested Remedy

Restructure the section 8 with the following structure.

8. Media Independent Handover Protocol

8.1 Introduction

8.2 Protocol Description

8.2.1 Protocol Considerations

8.2.1 Transport Methods

8.2.2 Acknowledgement

8.2.3 Congestion Control

8.2.2 Protocol Operation

8.2.2.1 MIH Function Discovery

8.2.2.2 MIH Capability Discovery

8.2.2.3 MIH Registration

8.2.2.4 MIH Handover

8.2.2.4.1 Mobile-Initiated Handover

8.2.2.4.2 Network-Initiated Handover

8.2.3 Protocol state machine

8.3 Message Formats

8.3.1 General Message Format

8.5.1.1 Protocol Header

8.5.1.1.1 Fixed Fields

8.5.1.1.2 Optional Fields

8.5.1.2 Protocol Payload

8.3.2 Protocol Identifiers

8.5.2.1 MIH Function Identifier

8.5.2.2 Session Identifier

8.5.2.3 Transaction Identifier

8.3.3 Protocol Messages

8.3.3.1 Messages for service management service category

8.3.3.2 Messages for event service category

8.3.3.3 Messages for command service category

8.3.3.4 Messages for information service category

8.3.4 Protocol Parameters

8.3.4.1 Link event list

8.3.4.2 Link command list

8.3.4.3 MIH event list

8.3.4.4 MIH command list

8.3.4.5 Transport list

8.3.4.6 MIIS Query type list

8.3.4.7 Mobile Node MAC address

8.3.4.8 PoA MAC address

8.3.4.9 Access router MAC address

8.3.4.10 Link type

8.3.4.11 IP address

8.3.4.12 Time interval

8.3.4.13 Status

8.3.4.14 Current link identifier

8.3.4.15 New link identifier

8.3.4.16 IP renewal flag

8.3.4.17 IP address configuration methods list

8.3.4.18 Link down reason code

8.3.4.19 Confidence level

8.3.4.20 Unique identifier

8.3.4.21 Capability flag

8.3.4.22 Number of parameters

8.3.4.23 Link quality parameter type

8.3.4.24 Parameter old value

8.3.4.25 Parameter new value

8.3.4.26 Link status parameters type

8.3.4.27 Handover mode

8.3.4.28 Link action

8.3.4.29 Link configure parameters type

8.3.4.30 PoA list

8.3.4.31 Link parameter threshold

8.3.4.32 Handover status

8.3.4.33 Error code

8.3.4.34 Link resource parameters type

8.3.4.35 Resource retention status

8.3.4.36 Link status parameters response

8.3.4.37 Link configure parameter value

8.3.4.38 MIIS query parameters

8.3.4.39 MIIS Query response

8.3.4.40 Link resource parameter values

8.3.4.41 IP address information status

8.3.4.42 Register request code

8.3.4.43 Register validity period

8.3.4.44 Link going down reason

8.3.4.45 Max response size