IEEE P802.22
Wireless RANs

| Nextwave Broadband WRAN Proposal Outline |
| --- |
| Date: 2006-06-07 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Ramon Khalona | Nextwave Broadband | 12670 High Bluff Drive San Diego, CA 92130 U.S.A. | 858-480-3172 | rkhalona@nextwavetel.com |

The PHY call started at 6AM PT on June 20 and lasted approximately one hour.  The attendance table is given at the end of the minutes.  We discussed a single contribution by Runcom (“IEEE 802.22 deployment Scenarios with Reuse 1 utilizing FUSC and PUSC concept”), which was presented by Eli Sofer.  This contribution presents the subchannel allocations for DL and UL in more detail than presented previously, especially for the Fully Used Subcarriers (FUSC) and Partially Used Subcarriers (PUSC) options that are allowed for the DL (PUSC only is used for the UL). These subcarrier allocations are based on 802.16e.  The contribution also presents deployment scenarios for both PUSC and FUSC (DL only) and simulation results, which only include mobility scenarios using the ITU-B channel model for vehicular applications.  These results, while not directly applicable to 802.22 since CPEs are assumed to be fixed, do give an idea of performance results that can be expected.

A question that arose among several participants (Philips, ETRI, CRC) was whether a more uniform pilot allocation among symbols would give better performance, especially when taking into account phase noise effects.  Philips pointed out that a simple phase noise model could be used, similar to that adopted for 802.11n and Monisha Ghosh volunteered to share that model with the group so that we can adapt it to our purposes.

Philips also pointed out that for 802.22 stationary applications we do not need to worry so much about subcarrier allocations as in 802.16e where mobility is involved, since the channel is likely to be less frequency selective and the resulting multipath is more likely to be influenced by the geometry of the application.

Eli Sofer took an action item to send out a document with simulation parameters that would be applicable for 802.22 and request comments from participants before the next call.

We also had a brief discussion about a contribution from Motorola that was presented at the September 05 meeting (22-05-0084-01 Propagation) on propagation measurements carried out in several environments.  These measurements were carried out in the FM band around 100 MHz using an observation bandwidth of 200 KHz (commercial FM channel bandwidth).  Gerald (CRC) commented that while the narrow observation bandwidth would have a tendency to smear the delay profile, that similar measurements at CRC carried out at 100 MHz and at 1.5 GHz had confirmed that the multipath delay profile varies slightly with frequency and that it is more directly influenced by geometry.  In conclusion, the results in the Motorola contribution, while not directly applicable to the UHF band, can still be useful in helping predict performance.

Next Call:  The next PHY call will take place on 6/27 at 7 PM PT.  The main agenda item is to discuss ETRI’s contribution on Single Channel OFDMA Parameters and to look at results from their simulations.  We will also look at a simulation plan to decide on subcarrier allocation as a result of Runcom’s proposal and the document that will be sent by Eli.

Attendance:

|  | May 30 | Jun 6 | Jun 13 | Jun 20 |
| --- | --- | --- | --- | --- |
| Myungsun Song |  | X | X | X |
| Kwangzin Go |  | X | X |  |
| Sung Hyun Hwang |  | X | X | X |
| Jung Sun Um |  | X | X | X |
| Patrick Pirat | X |  |  |  |
| John Benko |  | X | X |  |
| Soo-Young Chang | X | X | X |  |
| Edward Au | X | X | X |  |
| Ying-Chang Liang | X | X |  | X |
| Zander Zhongding Lei | X | X | X | X |
| Wing Seng Leon | X | X | X | X |
| Chang Long Xu | X | X | X | X |
| Anh Tuan Hoang | X |  |  |  |
| Yonghong Zeng |  | X |  |  |
| Steve Kuffner | X | X |  | X |
| Ramon Khalona | X | X | X | X |
| Monisha Ghosh | X | X |  | X |
| Carlos Cordeiro | X |  |  |  |
| Eli Sofer |  | X | X | X |
| David Mazzarese |  | X |  | X |
| Baowei Ji |  |  | X |  |
| Wendong Hu |  | X |  |  |

# Text boxes

Notice: This document has been prepared to assist IEEE 802.22. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s).  The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.

Release: The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication.  The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.22.

Patent Policy and Procedures: The contributor is familiar with the IEEE 802 Patent Policy and Procedures

<http://standards.ieee.org/guides/bylaws/sb-bylaws.pdf>, including the statement "IEEE standards may include the known use of patent(s), including patent applications, provided the IEEE receives assurance from the patent holder or applicant with respect to patents essential for compliance with both mandatory and optional portions of the standard."  Early disclosure to the Working Group of patent information that might be relevant to the standard is essential to reduce the possibility for delays in the development process and increase the likelihood that the draft publication will be approved for publication.  Please notify the Chair <Carl R. Stevenson> as early as possible, in written or electronic form, if patented technology (or technology under patent application) might be incorporated into a draft standard being developed within the IEEE 802.22 Working Group. If you have questions, contact the IEEE Patent Committee Administrator at <patcom@ieee.org>.

Abstract

This document contains the minutes from the PHY conference call on June 20 2006.