## Slide 1: Tutorial: Gigabit Ethernet Over Plastic Optical Fiber (GEPOF)
IEEE 802 plenary session
3 November 2014

## Slide 2: Panel
Bob Grow, GEPOF SG Chair, RMG Consulting
Carlos Pardo, KDPOF
Naoshi Serizawa, Yazaki Corporation
Thomas Lichtenegger, Avago Technologies

## Slide 3: Outline
Overview of proposed p802.3bv project
Technical / Economic Feasibility
Home networking market
Automotive market
Industrial market
Support
Summary and questions

## Slide 4: Overview of proposed p802.3bv project
Objectives
History of Previous Ethernet Over POF Activities
VDE standard development

## Slide 5: Objectives
Preserve the IEEE 802.3/Ethernet frame format utilizing the IEEE 802.3 MAC
Preserve minimum and maximum frame size of the current IEEE 802.3 standard
Support full duplex operation only
Support a data rate of 1000 Mb/s at the MAC/PLS service interface
For the automotive environment:
  Specify operation over at least 15m of POF with 4 POF connections
  Specify operation over at least 40m of POF with no POF connections
For the home and industrial environment specify operation over at least 50m of POF with 1 POF connection
Maintain a bit error ratio (BER) better than or equal to 10-12 at the MAC/PLS service interface
Specify optional Energy-Efficient Ethernet for 1000 Mb/s over POF

## Slide 6: History of Previous Ethernet Over POF Activities
An Ethernet PHY project was initiated in VDE (Verband der Elektrotechnik Elektronik Informationstechnik)
Issues with the VDE document were raised by IEEE-SA
  Changes to draft requested
  It was also noted that such work appropriately belongs in IEEE 802.3
VDE choose to withdraw the document
Participants want to do the work in IEEE 802.3

## Slide 7: VDE standard development
VDE standardization was being driven by:
  Siemens, Avago, Phoneix Contact, Firecomms, Franhoufer Institute, POF-Application Center, Innodul, Teleconnect, Diemount, KDPOF, …
Multiple technical proposals considered:
  Modulation: NRZ, PAM-4, OFDM, PAM-16
  Coding: Reed Solomon, MLCC, BCH, LDPC
  Technical solutions adopted and specified in the VDE document

## Slide 8: Technical and Economic Feasibility
Introduction to POF
Introduction to light transmitter and receiver
Connections
Length objectives
How is the VDE proposal?
  Tradeoffs
  Non linearity
  Performance of the VDE standard

## Slide 9: Introduction to POF
MM-GOF for data-centers, office-LAN
core: ⌀ 50 or 62.5 μm
clad: ⌀ 125 μm
GI - Graded-Index
core: ⌀ 980 μm
clad: ⌀ 1000 μm
1mm SI-POF multimode NA 0.5
SM-GOF for long-distance transmission
core: ⌀ 8 μm
clad: ⌀ 125 μm
SI - Step-Index
Typical optical fibers
GEPOF target

## Slide 10: Introduction to POF
The Plastic Optical Fiber is made of 1mm PMMA
Proposed POF is Step Index (SI-POF) according to: IEC 60793-2-40 .ed.3:2009: Type A4a.2
< 18 dB/100m if equilibrium mode distribution launch
Optical bandwidth > 40 MHz at 100m
Negligible temperature dependence
Different jacketing available for various applications
Dual fiber full duplex operation

## Slide 11: Light transmission in SI-POF
Area of higher attenuation
that produces differential mode att.
Angle of rays in respect fiber axis is
intrinsically related to TEM mode
in step-index fibers
Differential mode delay
Relative mode delay
Mode mixing
Optische Nachrichtentechnik:: Olaf Ziemann

## Slide 12: Introduction to POF
Obtained with laser collimated light source
Notes: Important to note 650 nm valley and low attenuation in green for future

## Slide 13: Introduction to POF - mode mixing
POF has a big mode mixing effect
Bending and length brings the launching mode distribution into the Equilibrium Mode Distribution (EMD)
Bandwidth·sqrt (Length) Product and Attenuation/Length approximate constants in EMD
Typically, light sources are manufactured to launch almost EMD to have predictable performance and avoid excessive mode conversion in bends
Discontinuities and impurities
of PMMA speed up mode mixing
Irregularities in the core-clad
boundary also ease mode mixing
Optische Nachrichtentechnik:: Olaf Ziemann

## Slide 14: Bending
Optische Nachrichtentechnik:: Olaf Ziemann

## Slide 15: Bending
During bending the mode distribution changes
  Different mode distributions represents different channel responses in terms of bandwidth and attenuation
  Dynamic bending requires continuous equalization of the channel response
There are backup slides with detailed technical description of the optical channel

## Slide 16: Bending effects
Down to 5 mm. No losses at 25 mm bending radius (Automotive)
Bending reduce optical power, and destroy higher modes improving bandwidth
Objectives can be reached even with bending

## Slide 17: LED light source
650 nm (red) LED
  Qualified for automotive up to 95ºC (HTOL 3000 h)
  105ºC Automotive feasibility demonstrated
AOP: Average optical power coupled into fiber
Linearity
  -20 / -30 dBc typical. (2nd / 3rd harmonic distortion). Varies with temperature and manufacturer
Bandwidth (E to E @ -3 dB): Typically 75Mhz. Improved with driver pre-emphasis up to 150 MHz
Different launch condition depending on the manufacturer. After lens the launch Numerical Aperture is approximately 0.3
Temp | -40ºC | 0ºC | 20ºC | 70ºC | 85ºC | 95ºC | 105ºC
AOP | -1.8 dBm | -2.5 dBm | -3.0 dBm | -5.2 dBm | -5.8 dBm | -7.0 dBm | -7.5 dBm

## Slide 18: Receiver
Si-PIN Photo Diode(PD) is normally used
  400 um -> 600 um PD diameter
Both, PD pseudo-differential and PD single ended solutions are available
Might be embedded with TIA (Trans Impedance Amplifier) to reduce EMS (Electro Magnetic Susceptibility)
Low dependency of response with temperature
TIA bandwidth and noise depends on received power

## Slide 19: PD Responsitivity

## Slide 20: Connections (In-line connector)
From 1.0 dB to 2.5 dB attenuation
No real impact on bandwidth

## Slide 21: Length objectives consider application temperature & connection requirements
Root cause: LED AOP decrease with increased temperature
Automotive (-40ºC to +105ºC):
  15 m with 4 connections
  40 m no connections
Industrial and Home Networking (-20ºC to 85ºC):
  50 m with 1 connection
All three length objectives can be met with a single PHY specification

## Slide 22: VDE proposal
  Provided to 802.3 as a contribution
    Economical and technical feasibility
    SG has not adopted technical proposals
  PAM-16 with THP (312.5 Mbaud)
  Optimum solution for current LED, Fibre and PD and feasible TIA
THP is used to:
  Solve Inter Symbol Interference (ISI) in combination with high spectral efficiency coded modulation
  Allows whitening of TIA non-white noise
Notes: Need to acknowledge that graphs are unreadable, explain green line and axis and what curve means if kept.

## Slide 23: Sensitivity based on Shannon capacity
Info Source
Encoder
DAC
Driver + LED
POF
Variable Attenuator
Photo-diode
TIA
Antialias Filter
ADC
Equalizer
Decoder
Info Sink
M-PAM
ENOB
FS
ENOB
FS
Fc
Type
BER Tester
M-PAM
Coding
gain
Increase
Attenuation
While keeping
BER < 10-12
Measure
Sensitivity
(min power)

## Slide 24: Sensitivity for 15m + 4 connections
Target by link budget analysis
Symbol rate (MHz)
Sensitivity (dBm)
Sensitivity as function of M levels of PAM

## Slide 25: Sensitivity for 50m + 1 connections
25
Target by link budget analysis
Symbol rate (MHz)
Sensitivity (dBm)
Sensitivity as function of M levels of PAM

## Slide 26: VDE data encapsulation
Periodic transmission structure
  To have a fast link establishment (Less than 50 ms)
  To have big tolerance to clock frequency mismatch (>+-200 ppm)
  To have a fast negotiation of THP TX coefficients
  To track and equalize channel changes with temperature, bending and vibration
  To implement Low Power Idle mode (EEE)

## Slide 27: VDE encoding
MLCC with three levels based on BCH component codes
  Low cost implementation
  Low power implementation
  Coding gain of 6.7dB @ BER 10-12 with multi-stage hard decoding

## Slide 28: Non linearity
Driver + LED
POF
Photo-diode
TIA
Antialias Filter
POF non-linear channel
POF non-linear channel
Volterra’s series model
Linearizer
non-linear filtering
Linearized Channel

## Slide 29: Non linearity - capacity penalty
Capacity loss < 1dB for
SNRe < 30 dB
High spectral efficiency schemes are feasible

## Slide 30: VDE proposal performance
Sensitivity –19.0 dBm at output of the fiber for BER 10-12 & 50 m. (Compromise between vendors)
Latency of 25 us
Overhead of Headers, Pilots and encapsulation: 3.5%
Multi-protocol encapsulation
Complexity:
  50% of average 1000BASE-T implementation
Royalty free license LOA from KDPOF

## Slide 31: Home Network market
Bandwidth requirements on the Home Network
WiFi & PLC limitations
Benefits of POF in the Home Network
Length requirements
POF installation examples
POF as backhaul
European Home Network study
Other Market examples
Conclusions

## Slide 32: Bandwidth requirements on the home network
FTTH and other broadband access technologies offers increasing access speeds
  Smart Home services is pushing the required Home Network speed beyond 100 Mbps
    “All in the cloud”
    VPN – remote working
    4K video, multi-room DVR
    high speed Internet, Internet of things…
Gigabit Ethernet assures the home network will not be a bottleneck

## Slide 33: WiFi & PLC limitations
In many households (E.g., Europe, Latin America, etc.), neither Wi-Fi nor Power Line Communications (PLC) are able to provide high speeds with full house coverage
WiFi
  Additional attenuation in brick houses over wooden ones is around 3.5dB per wall and 12 dB per floor. (ITU-R M.1225 Appendix 1 to annex 2)
  WiFi channels are saturated in urban areas even with the new 5 GHz bands
PLC
  Noisy PLC limits speed and robustness
  Many ISPs stopped offering PLC due to unpredictable quality

## Slide 34: Benefits of POF in the Home Network
Easy to install
  Low qualification or light training required
  Connectorless option
  Cut and plug
Electro Magnetic Immune, Galvanic secure
  To be installed together with the mains
  To be installed in houses with electrical noise problems
Flexible and robust

## Slide 35: Length requirements in HN
50 m covers worst cases for:
  Europe, Asia, Latin America and Africa
US and Canada
  In big downtown areas, required lengths are similar to Europe ones
  50 m covers most HN length requirements
  What is a worst case is arguable

## Slide 36: Examples of POF installation at home

## Slide 37: POF as a backhaul interconnecting devices and WiFi AP´s
Optimal combinations of technologies: WiFi for mobility and Optical for broadband
Enables minimal power WiFi AP´s tailored to optimal room coverage: Less cross-talk and radiation
Distributes the broadband all over the home

## Slide 38: European home network study
What is happening in the Broadband Market in EU?
High growth of broadband connections
  Which leads to greater capacity consumption
  Which leads to greater speeds
This is also driven by the “multiscreen explosion” (increasing number of devices)
Data from “Broadband access in the EU: Situation at 1 July 2013”, on Tue, 25 Mar 2014

## Slide 39: European home network study
Operators are investing heavily in deploying networks: DSL, Coax, FTTH.
Data from “Broadband access in the EU: Situation at 1 July 2013”, on Tue, 25 Mar 2014

## Slide 40: European home network study
Ironically, the increase in nominal speed (beyond 20Mbps) is creating more dissatisfaction in some cases:
  For Wi-Fi connections (most common), there are typically problems with speed , particularly in EU thick-wall housing
  For PLC (sometimes used as an alternative by Operators), there are many interferences
  For Ethernet Cat 5/6 (best current solution), the problem is often times resistance by house owners to outside wall cabling
Operators need to find an easy way to “match expectations” between what they sell and what the customer perceives.

## Slide 41: European home network study
Telcos are typically finding several topologies for home networking in case of successful setup:
%cases(*) Cat5/6 Wifi
20% Router Wifi only - OK
20% Router Wifi + STB/PC in the same room OK OK
10% Router Wifi + STB/PC in the same room X(1) OK
25% Router Wifi + STB/PC in other room/s OK OK
15% Router Wifi + STB/PC in other room/s OK X(2)
10% Router Wifi + STB/PC in other room/s X(1) OK
STB = Set Top Box
1: Not OK, because of esthetical reasons
2: Not OK, because Wifi has difficulties in penetrating walls.
(*) Source: estimation by JAL21, based on industry reports and interviews.

## Slide 42: European home network study
Telcos are typically finding several topologies for home networking in case of successful setup:
%cases(*) Cat5/6 Wifi
20% Router Wifi only - OK
20% Router Wifi + STB/PC in the same room OK OK
10% Router Wifi + STB/PC in the same room X(1) OK
25% Router Wifi + STB/PC in other room/s OK OK
15% Router Wifi + STB/PC in other room/s OK X(2)
10% Router Wifi + STB/PC in other room/s X(1) OK
STB = Set Top Box
1: Not OK, because of esthetical reasons
2: Not OK, because Wifi has difficulties in penetrating walls.
(*) Source: estimation by JAL21, based on industry reports and interviews.
35% POF Opportunity (aprox).

## Slide 43: European home network study
High Broadband Population penetration
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Population Penetration HBB | 0.058 | 0.072 | 0.095 | 0.112 | 0.144 | 0.175 | 0.2
Total Population EU | 507.416.607 | 508.273.750 | 509.130.893 | 509.988.036 | 510.845.178 | 511.702.321 | 512.559.464
Total households EU | 219.203.974 | 219.574.260 | 219.944.546 | 220.314.831 | 220.685.117 | 221.055.403 | 221.425.689
Population HBB EU | 29.430.163 | 36.595.710 | 48.367.435 | 57.118.660 | 73.561.706 | 89.547.906 | 102.511.893
Households HBB EU | 12.713.831 | 15.809.347 | 20.894.732 | 24.675.261 | 31.778.657 | 38.684.695 | 44.285.138
POF Opportunity Households | 4.449.841 | 5.533.271 | 7.313.156 | 8.636.341 | 11.122.530 | 13.539.643 | 15.499.798
POF Opportunity connections | 17.799.364 | 22.133.084 | 29.252.624 | 34.545.364 | 44.490.120 | 54.158.572 | 61.999.192
POF opportunity in EU 2015 – 2020 is more than 15 mill. Households which represent approximately 60 million POF connections.
5,8%
7,2%
9,5%
11,2%
14,4%
17,5%
20%

## Slide 44: Other HN market opportunities
European retrofit and new houses
  3 M households per year
Latin America
  New construction in Mexico, Chile, etc. requires low traning network installation
Japan

## Slide 45: The Numbers of Fixed Broadband Access Service Systems Subscribers in Japan
Source: Japan Ministry of Internal Affairs and Communications
Broadband Access service spread widely in Japan

## Slide 46: Japanese Survey for the demand of Optical Wiring
Great demand for
easy and no training
wiring
Answers from Building industries,
Wiring contractors, Home network users,
System vendors, Device vendors,
Cable manufactures and the others
In Japan

## Slide 47: Conclusions
POF is an optimum media for Home Network backbone for many house construction types around the world
  Easy to install
  Can share the mains conduit
FTTH deployment, and new services requires a robust home network capable of handling new access bit rates
Copper is not usable in many old houses, where POF is usable

## Slide 48: Automotive
Automotive networking
Market potential
JASPAR
O-GEAR Project
Open Alliance TC7

## Slide 49: Automotive networking
Complements RTPGE/1000BASE-T1
  Addresses those applications that can’t be serviced with 1000BASE-T1 UTP cabling
  E.g., high electromagnetic noisy areas, galvanic isolation, long distances
POF is already used in automotive for information and entertainment with the MOST technology
  Re-use of current MOST LED will guarantee automotive qualification
  Leverages on already qualified connectors and cables
Relative cost
RTPGE UTP
POF
COAX
STP

## Slide 50: Market potential
As stated in RTPGE CFI (March 2012)
  Overall automotive Ethernet market up to 270 Million ports in 2019
Brings current automotive POF users to a fully seamless Ethernet solution
  Stronger Ethernet automotive market potential growth
Complementarity use of RTPGE and Gigabit POF solutions
 | RTPGE | GIG-POF
Weight | ✓ | ✓✓
EMI/EMC | ✓ | ✓✓✓
Galvanic Isolation | ✓ | ✓✓✓
Temperature | ✓✓ | ✓
Length | ✓ | ✓✓
Cost | ✓✓ | ✓

## Slide 51: JASPAR
One voice of JAPAN - JASPAR was established, in 2004, in order to pursue increasing development efficiency and ensuring reliability, by standardization and common use of electronic control system software and in-vehicle network which are advancing and complexing.
Board: TOYOTA, Nissan, Honda,
DENSO, Toyota Tsusho Electronics
Members: Regular: 75 / Associate: 56 (as of Jan. ’14)
WGs:
Next Generation High-Speed Network WG
Functional Safety WG
AUTOSAR/FlexRay Standardization WG
Multimedia Architecture WG
Bluetooth Conformance WG
Mobile Device Interface WG
Chair: TOYOTA
Nissan, Honda, Denso, Renesas Electronics, Sumitomo Electric, Murata Manufacture, Toyoda Gosei, Clarion, Bosch Japan, NXP Japan, Micrel Japan, Yazaki, Furukawa Electric, Toyota Central R&D Labs, Marvell Japan, TE Connectivity, Nippon Seiki, Fujitsu TEN, Nippon Seiki, Isuzu Motor, Clarion, Mitsubishi Electric, Fujitsu Semiconductor, Toshiba Information Systems, Hitachi Automotive Systems, Calsonic Kansei, Micware, OTSL, Analog Devices, Vector Japan, ETAS, Marvell Japan, Sunny Giken, Telemotive AG, Ricoh, MegaGhips, Tokai Rika
Recommendation's application
Network
Function profiles
Physical layer and wiring design
Data description format
Requirements Definitions of the WG
Next Generation High‐Speed Network WG

## Slide 52: Optical Network Systems for Automotive
No more measures against noise
Standardized test methods and components
Full automation manufacturing
Use proven technologies from other industries
Avoid price staging
1980
1990
2000
2010
2020
Peer to peer
D2B
MOST 25
MOST 150
IEEE1394
LAN
(POF)
More than 100,000,000 nodes
More than 150 car models
Over 10 years
Optical Communication in Cars
In-vehicle Optical Components
Header
Connector
POF
Model link
High speed
Scalability/Expandability
EMC/EMI
Dimensions
Weight
Small cable diameter
Small bending radius
Robustness
Features of Optical Components
Cost Competition Strategy

## Slide 53: International standardization and dissemination project for high-speed communication network performance over large core multimode optical fiber - Technology integration for O-GEAR: Optical Gigabit Ethernet for Automotive aRchitecture
OITDA (Project administrator)
9 companies
Problems
Assignment
Standardization
Design Tool Development
Develop simulation tools for optical link system which include mode conversion function of mode power distribution in SI-MMF defined by EAF. Link system design will be achieved in simple and low cost.
Physical Layer Development
Develop physical layer components which have bandwidth guaranteed wire harness and connector at 1 to 10 Gbps followed by JasPar requirements and IEEE802.3 Stds. Create int’l standards in IEC and ISO.
System Demonstration
In order to achieve higher reliability network system, demonstration of BER 10-14 at 1 Gbps Ethernet for automotive is the key target. Such lower BER will be required for future autonomous driving system and ADAS.
Promotion of Int’l Std.
De jure standards, IEC/ISO/IEEE, are required instead of traditional de-facto and OEM standards. Achieve low cost network systems with the use of international standardized components and systems.
No simulation tools of the system design for O-GEAR
No bandwidth guaranteed harness and connectors in high speed, 1 Gpbs - 10 Gbps
Required reliable system which target is similar to FlexRay, BER 10-12@10 Mbps
Toyota Central R&D Labs.
Team
Sponsored by METI Japan
Utsunomiya University
5 companies
AIST (a national institute)
6 companies
From Oct. 2014 to Mar. 2017

## Slide 54: Schedule, In-vehicle Gigabit Ethernet
 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Automotive |  |  |  |  |  |  |  |  |  | 
O-GEAR (Japan) |  |  |  |  |  |  |  |  |  | 
IEEE802.3 Ethernet for Automotive |  |  |  |  |  |  |  |  |  | 
1 G bps Car
Development for mass production
Product release
1 G bps Demonstration
1 G bps Ethernet Std.
1 G bps Cars
IEC/ISO Standards
Conformance Test Office
Support

## Slide 55: Open Alliance – TC7
Open Alliance has created a Technical Committee to support the Ethernet optical links in automotive
Participants to this group are:
  Avago, Broadcom, Cadence, C&S Delphi, Denso, Excelfore, Furukawa, KDPOF, Ruets, Sumitomo, TE, Toyota, Vittese, Yazaki
Goal of the group is: “Work on Gigabit‐Ethernet over POF solution for Automotive use”
  Summarize Automotive requirements and support IEEE802.3 GEPOF standardization activity.
  Create supplement documents/ Specifications (Connector interface, Footprint, test suits, etc.) for automobile installation

## Slide 56: Summary for Automotive Applications
Complementary technologies, electrical and optical, bring benefits for customers
Plastic optical fiber is a proven technology in automotive
Gigabit Ethernet enhances future applications
Member companies from JASPAR contributes to the standardization works

## Slide 57: Industrial market
Overview of industrial POF fibers
Evolution of POF based industrial Automation Network Systems
Environmental conditions
Factors of success of POF in industrial networking
Mechanical characteristics of POF
Industrial Example
How to terminate POF with an industrial connector
Conclusions

## Slide 58: Overview of industrial fibers
 | Polymer Optical Fiber | Hard Cladded Silica | Multimode | Singlemode
Shortform | POF | PCF | GOF-MM | GOF-SM
Standard IEC 60793-2 | A4a | A3c | A1a/ A1b | B1
Absorption [db/km] with λ [nm] | 230 660 | 6 850 | 3,0/ 3,5 850 | 0,5 1300
Core diameter [μm] | 980 | 200 | 50/ 62,5 | 9
best optical solution for short distances POF easy termination
POF
PCF
GOF-MM
GOF-SM

## Slide 59: Evolution of POF based Industrial Automation Network Systems
time
data rate
~10MBit/s
100MBit/s
1GBit/s
~1990
~2000
~2015
Fieldbus
Industrial Ethernet
Industrial Gbit Ethernet
Needed and wish from the industry
POF 70m
POF 50m
POF 50m
Fieldbus e.g. | ControlNet™
Industrial Ethernet e.g. | 
Industrial communication systems are successfully using POF since more than 20 years.
Volume is 1Mio nodes per year

## Slide 60: Environmental conditions
commercial: industrial:
MICE | 1 = Commercial environment covered by IEC 11801 | 2 = Light industrial environment | 3 = Heavy industrial environment
Mechanical | M1 | M2 | M3
Ingress | I1 | I2 | I3
Chemical | C1 | C2 | C3
EMC | E1 | E2 | E3
Three alternatives:
reinforce, e.g. with IP67-components ⇨ the trend with local automation
Isolation, e.g. with housings
seperation, e.g. in seperatet rooms
Tough solutions are required in Industrial applications!

## Slide 61: Factors of success of POF in Industrial Networking
Industrial Networking requires:
  EMC-resistant systems
  Environment-resistant systems
  Galvanic isolation
  Easy wiring
  Easy field termination
  Easy planning
POF fulfills the requirements for Industrial applications

## Slide 62: Mechanical Characteristics of POF
Fiber displacement caused by:
  Shock, Vibration and Temperature
  Fiber displacement results in slightly higher attenuation but no loss of connection
  e.g. Radial fber displacement of 100µm would result in a link down for 62.5µm MM fiber but has only a minor attenuation impact to a POF link
  POF has excellent bending and torsion properties. Tests have shown that the POF can withstand more than 1000k bending and torsion cycles
POF has mechanical advantages due to the large diameter and material
axial movement
radial movement

## Slide 63: Example robot cell in automotive industry
Cable length from the robot to the control cabinet typically 20 m
Welding tools and drives cause EMC-troubles
Rough environment
Field cable termination necessary
Data- and power cable very close
Low weight
Bending/torsion durability of POF
Monitoring of link quality
POF fulfills the requirements perfectly

## Slide 64: Termination of POF-Connectors
Remove cable coating
Pulling boot over wire
Cut the fiber
Remove isolation
Fix connector in the intake
Put wires in the boot
Tighten the screws
Done!
Attenuation max. 1,5 dB Fast and easy
Reliable process Field termination possible

## Slide 65: Conclusion
Industrial technology has:
  Applications with short link distance
Industrial requires:
  Robust solutions in respect of EMC and harsh environment
  Galvanic isolation
  Easy field cable termination
  Easy rules
POF is the best choice for communication systems in Industrial networking

## Slide 66: SUMMARY

## Slide 67: Summary
Three target markets have different: link length, number of connectors, and environmental constraints
  All three markets can be addressed by a single PHY
  Link budget allows for tradeoff of market constraints (e.g., fewer connectors for longer length)
Royalty Free IEEE LOA from KDPOF
  Covers technology adopted by VDE project if selected by TF
IEEE 802.3 is a global standard
  We need to address global requirements
  Not all markets have similar opportunities
  Users and vendors throughout the supply chain want an 802.3 GEPOF standard

## Slide 68: Future of POF
LENGTH
SPEED
MOST-150
100FX
over POF
MOST-25
GEPOF
GEPOF+ GREEN
10000 POF
15m -
50m -
100m -
25 Mbps -
150 Mbps -
100 Mbps -
1000 Mbps -
10000 Mbps -
Maybe GI-POF Maybe VCSEL
GREEN Light source

## Slide 69: SUPPORT
Support
Quotes

## Slide 70: Support
  Some of the companies encouraging IEEE 802.3 to develop GEPOF:
  Home Network

## Slide 71: Support
  Some of the companies encouraging IEEE 802.3 to develop GEPOF:
  Automotive

## Slide 72: Support
  Some of the companies encouraging IEEE 802.3 to develop GEPOF:
  Industrial and others

## Slide 73: Quotes
"The in-vehicle gigabit network will definitely be essential in the near future. Automobiles are vulnerable to noise, which is difficult to solve even with electric cables, especially in the Gigabit Ethernet. Thus, it is better to prepare a backup solution and I look forward to optical network standardization. However, cost reduction is a key factor for practical use in the automotive market; therefore, I hope everything goes well." Hideki Goto - Group Manager, Toyota Motor Corporation
"Gigabit over POF utilises proven Physical Layer components and harness assembly procedures that are well understood by the automotive industry. For this reason, JLR believe, that such a standardised technology could offer a potentially fast time to market for certain use cases of gigabit Ethernet within the vehicle cabin.” John Leslie - Communication Systems Technical Specialist, Jaguar Land Rover Limited

## Slide 74: Quotes
“… the only way to match expectations between the broadband speed we sell and what the customer perceives it´s the cable. I think POF is a great cable solution.” Mario Diaz - Director for Home Fiber and broadband Offering, Telefonica
“Vodafone, sees that POF is an easy way to "match expectations” between the broadband speed that we sell and what the customer perceives, potentially avoiding many problems with Wifi connections (and other problems in home networking) in a cost-effective way.” Juan Manuel Sánchez – Managing Director Vodafone Spain
‘‘In this market, engineers are already using FPGAs to run high speed links with their own protocols for a variety of industrial networking applications over POF. (…) In the telecommunications world companies such as Orange, Telecom Italia, and Swisscom for example have completed trials validating the business case for POF but to move the solution forward they need a GigE solution as GigE is now the technical base line. (…) It would be a cleaner solution if that usage were to a published standard ensuring interoperability and a level commercial playing field and benefiting from the robustness that an IEEE standard provides.’’ - Michael O’Gorman VP Marketing Firecomms

## Slide 75: QUESTIONS

## Slide 76: BACKUP SLIDES
Optical model for SI-POF

## Slide 77: Optical model for SI-POF
Power flow equation (Gogle’s eq.):
P is the optical power distribution in time instant (t), fiber length (z), propagation inner angle respect to fiber axis (θ) and wavelength (λ)
α is the Differential Mode Attenuation (DMA)
τ is the Relative Mode Delay (RMD)
Initial conditions (launching conditions):
Boundary conditions to solve PDE:
Differential mode delay
Relative mode delay
Mode mixing

## Slide 78: Optical model for SI-POF
The DMA from steady state Far Field Pattern (FFP) Q(θ) as*:
  γ(λ): characteristic attenuation of POF as function of wavelength
Q may be fitted by bi-sigmoid function*:
The RMD is given by:
  c is the vacuum light speed, ncore is the refractive index of core
The diffusion coefficient may be fitted by:
(*) Mateo et al., “Global characterization of optical power propagation in step-index plastic optical fibers”, Vol. 14, No. 20, OSA (2006)

## Slide 79: Optical model for SI-POF
Impulse response of SI-POF, including modal and chromatic dispersion:
where SPD is the sensitivity of photo-detector and ηPD is the directivity

## Slide 80: Introduction to POF - mode mixing
⬆︎ length 0 to 100 m
(mode mixing)
Launching UMD 0.5
Launching UMD 0.2
⬆︎ length 0 to 100 m
(mode mixing)
EMD
EMD
FFP for
under-filled launching condition
FFP for
over-filled launching condition
Uniform Mode Distribution (UMD)

## Slide 81: Introduction to POF - mode mixing
⬆︎ length
almost equal mode distribution
FFP for
EMD launching condition
LED + lens
launching MD
Real LED with almost EMD condition

## Slide 82: Effect of mode mixing in Attenuation and Bandwidth