## Slide 1: LinkSec Architecture
Robert Moskowitz
July, 2003
ICSAlabs

## Slide 2: LinkSec Network Model
Hop-by-hop model for Link Confidentiality
  Except where provider bridges facilitate virtual links between subscriber bridges
Terminology
  Provider ‘owns’ the network. A Provider may be the Corporate IT department
  Subscribers ‘use’ the network. E.G. a corporate employee or a paying customer.
  Transparency in security refers to 2 or more links appearing as a single link to the end devices with the intermediate bridges being transparent to the security services

## Slide 3: LinkSec Network Model
LinkSec delineates link ownership
  Provider link
  Joint link (Provider/Subscriber)
  Virtual link (Subscriber over Provider)
The Network is the collection of
  Links, Provider link interfaces, and Provider Authentication Servers (and related services)

## Slide 4: LinkSec Network Model
Primarily to protect the Provider network from attack and misuse
A Provider IEEE 802 Infrastructure
  Provider Links
  Cross-Provider Links
  Network attachment points
    Jointly controlled by Provider and Subscriber
Network Authentication
  Link Authorization
  Link confidentiality (privacy and integrity)

## Slide 5: Network Definition
For purposes here, a Network refers to Layer 2 infrastructure and Layer 3 provisioning services
The network is an entity in its own right that needs to be secure
The components of a network need various levels of security
Rest of the network
Network
Attachment
Point
The network
topology
Networked
Device
Network
Attachment
Point
Networked
Device
Networked
Device
Networked
Device
Networked
Device

## Slide 6: Security Services Components
Pre-existing trust between Authentication Server and
  Provider components
  Subscriber components
Targeted Trust is
  Between Attached devices and Network
  Between 2 attached devices in specific situations
Rest of the network
Network
Attachment
Point
Networked
Device
Network
Attachment
Point
Networked
Device
Networked
Device
Networked
Device
Authentication
Server
Established Trust
Target Trust

## Slide 7: Provider View Of LinkSec
Support billing
  No money, no network
    Binary, no provisioning implied
  Subscriber and cross-provider
Legal obligations
  Subscriber expectations
  Legal intercept function of deployment, not protocols
Control access to Network Attachment Points
  Know your Subscriber (i.e. link termination)

## Slide 8: Subscriber View of LinkSec
Network exists to service Subscribers
  LinkSec exists to protect subscribers from other subscribers
Trust in Network
  Authenticate the Provider
  Restriction of exposure
  Asynchronous: Subscriber assumes no attack from Provider, but Provider assumes attack from Subscriber
Trust in billing
  Only charged for real usage

## Slide 9: Peer View of LinkSec
2 Peer systems control the link
  Bi-directional control
  Either can initiate authentication
  Both play an equal role in controlling the authentication process
One system may take control of the link
  Typically based on link ownership
    e.g. 802.1ad Provider Bridge might always be the Responder, even if it initiated the authentication

## Slide 10: MAC View of LinkSec
The LinkSec Security Association is bound to the MAC addresses of interfaces on the link
  For an edge device this is its SOURCE address
    This can be used in filtering rules and relating keys to frames
  MAC addresses of Bridges never appear in forwarded datagrams
    This presents a challenge on shared media
    802.11 AP MACs are in the preamble

## Slide 11: Business-Driven Requirements
Provider Network centric
  IEEE 802 networks only
Provider link protection
  Intra-Provider, Inter-Provider, Subscriber to NAPs
Authentication always needed
  Helps limit mis-use of network
  Detects mis-wiring
Privacy and Integrity protection
  Data confidentiality

## Slide 12: More Business-Driven Requirements
Provider Bridge (802.1ad) transparency
  Customer data private from provider
    Including bridge management traffic
Multiple subscribers to one physical port
  e.g. 802.3ah and 802.11

## Slide 13: Business-Driven Requirements Not Included
Link Transparency
  Virtual, trusted links across hostile bridges
    Exception is 802.1ad Provider bridges
  Impact on multi-party Adhoc networks
Multiparty links
  E.G. 2 bridges on 802.3 with device ignorant of which is active
Legal Intercept
  Solved by deployment methodology not provisions in LinkSec

## Slide 14: Requirements Details
Multi-link model per network component
  Each network component (or node) has N points of connection to the network
  N = 1 is the degenerate case
Consider all links as ephemeral
  “permanent links” are just long-lived ephemeral links
  links change state as soon as link is lost

## Slide 15: More Requirements Details
Peer nature of Authentication
  Both ends of the link control the authentication process, even though one side starts the authentication
    The peers SHOULD be mutually authenticated (this is a function of a higher level service)
  One end may force a role of Initiator or Responder
  There should never be a race condition
    If both peers start authentication at the same time, one is gracefully terminated

## Slide 16: More Requirements Details
Layer Signalling of LinkSec
  Support for Handoff between NAPs
  No direct support of Handoff mechanisms in LinkSec. I.E. Transparency to handoff at layer 3
Confidentiality of Data frames
Integrity of Management frames
  These are specific media management frames not carried in data frames (e.g. 802.11 DISASSOCIATE)
  Minimally only accept control packets from authenticated links