## Slide 1: 802 Architecture Group
Website:
http://www.ieee802.org/1/files/public/802_architecture_group/
Joining the Email exploder:
http://www.ieee802.org/1/email-pages/joining.html

## Slide 2: Intent
Improve alignment between WG projects and existing 802 architecture by:
  Identifying current problems, omissions, conflicts, ramifications, and their potential resolution
  Identifying potential refinements or changes to the architecture
  Providing a regular forum in which such discussion can take place, in a lower pressure environment than is possible during the core Plenary cycle.

## Slide 3: Mechanism
A meeting per Plenary cycle
  Chaired by 802.1 Chair
  Time slot: 2-5 PM Sunday prior to Plenary
  Participants: Initially, WG Chairs plus one (or more) “architects” or “technical leads”; long term, whoever the Chair determines is appropriate/willing
  Meeting Topic: Architectural issues known to each WG & how they might be resolved
First meeting: July 2004

## Slide 4: Purpose
To actually have a recurring discussion on architectural issues
To improve cross-WG discussion/understanding
To promote a common view

## Slide 5: Outputs
Not detail document oriented
Consensus, frame of mind, consciousness raising
Maybe slideware if appropriate
Topics/thoughts for the focus of the next discussion
Encouragement to WGs to fix identified problems in appropriate ways
Simple architecture
Preservation of layering

## Slide 6: Actions
SEC to formally establish the activity as a SEC standing committee.
WG Chairs to appoint max 2 nominated participants per WG
  Qualifications for participants: Capable of generating a durable architecture. Capable of knowing the difference between an architecture, a product, and a standard. Respected within their WG as subject matter experts.
Report to SEC on status at each meeting.

## Slide 7: Known issues – 802.1
MAC Service definition (currently a revision PAR in place)
QoS – could be better expressed
Security expressed as a set of procedures after network entry
Management – scope and interface
  Commonality of MAC/PHY management interfaces (managed object definitions)
MIB definition for service discovery
Where work gets done – 802.1 vs 802.X
Process – ensuring due diligence
Max frame size
Position/location awareness

## Slide 8: Known issues – 802.3
QoS/class of service
  Timing, synchronous, guaranteed bandwidth, low jitter/latency, congestion management…
  Need a consistent architecture for QOS across 802 so we can switch between port types.
  Many questions coming from many new projects across the MAC groups.
Ethernet/TCP-IP interdependence
  Do we care about anything non-TCP?
  Yes, we care. Telecomunications, backplane, a lot of entertainment is UDP, SCTP
  Definitately need strong non-TCP support, Harder to say something other than IP is needed.
Security/link agg
  This should be generalized to above MAC layer 2 protocols over link agg.
  With 2 port bridge/media converter, can you run link agg on two parallel links with this in each?
  Do we need a new link agg in the future.
Dual homing/resilience/robustness
  Low priority - no advocates currently pushing specifics
  layer 3 solutions exist
  backplane might want it at some point. If so, it seems most appropriate for 802.1 so it could work across MAC types.
MAC Service definition
  No indication MAC to MAC client of readiness for another request. Thus commit to a request is ambiguous. When can you replace a low priority request with a low priority request?
  Would help QOS.
  Should we have a MA data request acknowledge?

## Slide 9: Known issues – 802.11
QoS/class of service
  Timing, synchronous, guaranteed bandwidth, low jitter/latency, congestion management…
Protocol definition vs scope
Security
Bridging compatibility – handling of multicasts
LLC – acts as a block to passing additional (e.g., QoS) parameters
Mesh
What is the (future) .11 architecture
  Structure of an AP
  DS
  …etc
(Signal) Power/channel management

## Slide 10: Dot15 802 Architecture Group Update
Tom Siep
Cambridge Silicon Radio
802.15 Liaison to 802 Architecture Committee
NOTE: Changes made as a result of 13-Mar-05 802 Architecture Group meeting are in BLUE

## Slide 11: Prioritized issues – 802.15
Issues
  LLC – acts as a block to passing additional (e.g., QoS) parameters
  QoS
  (Signal) Power/channel management
  64bit to 48 bit address mapping for bridging (new topic)
  Smaller than 100 octets allowed for minimum packet size
  Bridging compatibility – handling of multicasts, no clause 6 section for .1D
Non-Issues
  Are PANs different from WLANs?
  Security
  Mesh (work TBD)
  Architectural consistency across three MACs
Not architectural issues
Management Issues
{
Not addressed at Sunday meeting
}

## Slide 12: Other Groups Affected
LLC – acts as a block  802.1 and 802.2
QoS  802.1 and 802.2
(Signal) Power/channel management  802.1 and 802.2
64bit to 48 bit address mapping for bridging  802.1 and 802.2
Smaller than 100 octet packets  802.1 and 802.2
Bridging compatibility – internal problem being worked

## Slide 13: Work to be done by 802.15
Form plans to solve issues
Determine feasibility of plans
Study proposal to use IETF model for QoS – will it work for .15 TGs?
Characterize management function needs
Can’t do bridging 64 to 48 bit addresses – are we OK with this?

## Slide 14: LLC – acts as a block to passing additional (e.g., QoS) parameters
All 3 MAC need LLC support to requests to create/modify/terminate streams based on QoS parameters
Data needs to be able to be associated with a stream at the MAC SAP
QoS changes need to be communicated to the higher layers
Need to be able to inquire QoS characteristics of remote nodes

## Slide 15: Backup Slides

## Slide 16: Known issues – 802.15 (as presented at Sunday meeting in San Antonio)
Are PANs different from WLANs?
  We hope the answer is “No” (wrt the MAC service)
Security
  What functionality is needed
  Who does what aspect
Bridging compatibility – handling of multicasts, no clause 6 section for .1D
LLC – acts as a block to passing additional (e.g., QoS) parameters
Mesh (not the same as the .11 issue though)
QoS
Architectural consistency across three MACs
(Signal) Power/channel management

## Slide 17: QoS
Block asynchronous data
  Need block size to plan and allocate resources

## Slide 18: (Signal) Power/channel management
Need a way to pass (up and down) information that is important to wireless, for example
  Transmit power
  Regulatory domain
  Signal quality
  Coexistence information
  Other
Must be extensible

## Slide 19: Bridging compatibility – handling of multicasts, no clause 6 section for .1D
Compatibility with .1D
  15.1a – Bridging is handled in BNEP, which maps to Ethernet.
  15.3 – Annex A (normative) specifies compatibility
  15.4 – Annex A (normative) specifies compatibility
Multicasts
  15.1a – does not do multicast
  15.3 – Had multicast, being revised in current work
  15.4 – Had broadcast, being revised to include multicast in current work

## Slide 20: Known issues – 802.16
Security
  has to roll its own EAP transport as .1X/AF
  is above the LLC
  No PKI model in .1X/AF
  MBS – breaks security model
  Should schedule a joint meeting with 802.1
QoS
  See .21
Bridging compatibility – handling of multicasts, no clause 6 section for .1D
. MTU discovery
  Look at 802.1AD LLDP?

## Slide 21: Known issues – 802.17
Frame size
  Not dissimilar problem to dot-3 – will take their lead
CoS/QoS
  Look at intsrv/diffsrv
Security
  We have layering issues.

## Slide 22: Known issues – 802.20
Needs to support handoff – not clear how to deal with L2 handoff in current architecture
QoS
  No standard way to pass upper layer QoS requirements through to MAC level QoS parameters
  LLC acts as a block
  Relation to IntSrv/DifSrv mechanisms
Security
  has to roll its own EAP transport as .1X/AF
  is above the LLC
  No PKI model in .1X/AF
Compatibility between 802.20 frame and LLC frame

## Slide 23: Known issues – 802.21
QoS mapping across heterogeneous interfaces
  Ability of 802 MACs to support IntServ/DifServ (management interfaces, etc)?
  Tony to provide a pointer to the relevant RFCs
Authentication mechanisms – different mechanisms in different technologies
Security – how do you re-establish the security context
Service discovery
Power/channel management

## Slide 24: Known issues – 802.22
Goal to avoid all of the above

## Slide 25: Known issues – Broadband over Power lines (external project)
Will this be Bridgeable or will it only be routable (to 802 technologies)?
In order for the technology to be Bridgeable, then they should participate in this architecture group
Make liaison with 802 a requirement of the PAR
They should address coexistence (with other technologies)
Entity balloting would tend to disenfranchise a significant body of technical expertise from the balloting process. LMSC join as an entity?

## Slide 26: Action items
  Groups that have QOS on list to look at IETF intsrv/difsrv documents & identify specific things that would allow their MAC to better support these services
  Groups that have listed security issues to detail specific questions/issues regarding security
  Tutorial on service interface vs API

## Slide 27: Agenda for next meeting, Sunday July 17 2005, 2-5pm
Continue (.11 through .1) refinement and prioritisation of current issues list based on WG input (homework items from previous slide)
Report back on issues that are currently being addressed
Proposals for resolution of high priority issues that are not currently being addressed
Spend more time on QoS, especially support of intsrv/diffsrv by 802 MACs