## Slide 1: Metro Ethernet Forum OAM An Update
Matt Squire
Hatteras Networks

## Slide 2: Scoping the Problem
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
SONET
RPR
Ethernet
Provider A
Provider B
Provider C
Bridge
Problem:
When delivering an Ethernet service over a large, diverse network, how do you detect end-to-end connectivity problems (loss and degradation)?

## Slide 3: Scoping the Problem
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
SONET
RPR
Ethernet
Provider A
Provider B
Provider C
Bridge
MEF is looking at multi-domain service OAM mechanisms
Multi-hop
path

## Slide 4: Scoping the Problem
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
SONET
RPR
Ethernet
Provider A
Provider B
Provider C
Bridge
Multi-hop
path
Edge-to-edge Intra-Carrier OAM

## Slide 5: Scoping the Problem
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
SONET
RPR
Ethernet
Provider A
Provider B
Provider C
Bridge
Multi-hop
path
Edge-to-edge Inter-Carrier OAM

## Slide 6: Scoping the Problem
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
Bridge
SONET
RPR
Ethernet
Provider A
Provider B
Provider C
Bridge
Multi-hop
path
End-to-end Customer OAM

## Slide 7: Key Aspects of MEF OAM
Assumes Ethernet is only common denominator
  E.g. 802.3 Ethernet, Ethernet over SONET, RPR, etc.
  Must use Ethernet framing for OAM communications
Ethernet segments interconnected with forwarding entities (bridge, switch, etc.)
  Connectionless, like IP
  Segment can be real or virtual (see above)
  Must deal with multicast and frame replication issues
Must measure “per service” and be with data plane
  Can think service = VLAN for this discussion
  Out-of-band OAM not possible, not accurate with data plane
  OAM mixes with user data within core (only different at edges)

## Slide 8: Key Aspects of MEF OAM
Initial focus on “SLA” metrics
  Connectivity, latency, loss, jitter
  Includes discovery (multicast “ping”)
  Includes timestamped “ping” (connectivity test)
  Includes timestamped “hello” (connectivity verification)
Other function may follow later
  Traceroute (fault isolation), RDI/AIS (fault signaling), etc.
  No commitment on when/how – initial focus is “Phase I”
  CURRENTLY NOT DEALING WITH FAULT ISOLATION
Domain oriented
  Supporting hierarchical domains required
  Separation of customer and carrier OAM is a big thing
  Domain may be intra-provider, inter-provider, customer-customer, and other

## Slide 9: OAM Frame
01234567 89012345 67890123 45678901
+--------+--------+--------+--------+
| Dest MAC |
+--------+--------+--------+--------+
| Dest MAC | Source MAC |
+--------+--------+--------+--------+
| Source MAC |
+--------+--------+--------+--------+
| VLAN Ethertype | VLAN Tag |
| (Optional) |
+--------+--------+--------+--------+
| OAM | OAM | Version|
| EtherType | Level | |
+--------+--------+--------+--------+
| Rsvd | OpCode | Data |
+--------+--------+--------+--------+
|Data (OpCode specific, continued)… |
+--------+--------+--------+--------+
Uses a pretty generic frame format with very few fixed fields

## Slide 10: OAM Frame
01234567 89012345 67890123 45678901
+--------+--------+--------+--------+
| Dest MAC |
+--------+--------+--------+--------+
| Dest MAC | Source MAC |
+--------+--------+--------+--------+
| Source MAC |
+--------+--------+--------+--------+
| VLAN Ethertype | VLAN Tag |
| (Optional) |
+--------+--------+--------+--------+
| OAM | OAM | Version|
| EtherType | Level | |
+--------+--------+--------+--------+
| Rsvd | OpCode | Data |
+--------+--------+--------+--------+
|Data (OpCode specific, continued)… |
+--------+--------+--------+--------+
Destination MAC address can be
Well-known Multicast – for discovery and multicast tests
Unicast of peer station – for unicast tests
Well-known addresses default to MEF-defined but are configurable!
(important later)

## Slide 11: OAM Frame
01234567 89012345 67890123 45678901
+--------+--------+--------+--------+
| Dest MAC |
+--------+--------+--------+--------+
| Dest MAC | Source MAC |
+--------+--------+--------+--------+
| Source MAC |
+--------+--------+--------+--------+
| VLAN Ethertype | VLAN Tag |
| (Optional) |
+--------+--------+--------+--------+
| OAM | OAM | Version|
| EtherType | Level | |
+--------+--------+--------+--------+
| Rsvd | OpCode | Data |
+--------+--------+--------+--------+
|Data (OpCode specific, continued)… |
+--------+--------+--------+--------+
OAM frames are optionally tagged
OAM frames are “per-EVC” (Ethernet Virtual Connection)
[That’s a VLAN to you and me]
OAM frames are tagged/not as EVC is tagged/not
OAM frames for measurements follow the data path!

## Slide 12: OAM Frame
01234567 89012345 67890123 45678901
+--------+--------+--------+--------+
| Dest MAC |
+--------+--------+--------+--------+
| Dest MAC | Source MAC |
+--------+--------+--------+--------+
| Source MAC |
+--------+--------+--------+--------+
| VLAN Ethertype | VLAN Tag |
| (Optional) |
+--------+--------+--------+--------+
| OAM | OAM | Version|
| EtherType | Level | |
+--------+--------+--------+--------+
| Rsvd | OpCode | Data |
+--------+--------+--------+--------+
|Data (OpCode specific, continued)… |
+--------+--------+--------+--------+
MEF OAM uses a well-known EtherType
MEF assigned default
Can be configured (important later!)

## Slide 13: OAM Frame
01234567 89012345 67890123 45678901
+--------+--------+--------+--------+
| Dest MAC |
+--------+--------+--------+--------+
| Dest MAC | Source MAC |
+--------+--------+--------+--------+
| Source MAC |
+--------+--------+--------+--------+
| VLAN Ethertype | VLAN Tag |
| (Optional) |
+--------+--------+--------+--------+
| OAM | OAM | Version|
| EtherType | Level | |
+--------+--------+--------+--------+
| Rsvd | OpCode | Data |
+--------+--------+--------+--------+
|Data (OpCode specific, continued)… |
+--------+--------+--------+--------+
Need to come back to this one
(See “Security Wrinkle”)

## Slide 14: OAM Frame
01234567 89012345 67890123 45678901
+--------+--------+--------+--------+
| Dest MAC |
+--------+--------+--------+--------+
| Dest MAC | Source MAC |
+--------+--------+--------+--------+
| Source MAC |
+--------+--------+--------+--------+
| VLAN Ethertype | VLAN Tag |
| (Optional) |
+--------+--------+--------+--------+
| OAM | OAM | Version|
| EtherType | Level | |
+--------+--------+--------+--------+
| Rsvd | OpCode | Data |
+--------+--------+--------+--------+
|Data (OpCode specific, continued)… |
+--------+--------+--------+--------+
Usual versioning capability
Fixed v1 for now
Ignores anything higher

## Slide 15: OAM Frame
01234567 89012345 67890123 45678901
+--------+--------+--------+--------+
| Dest MAC |
+--------+--------+--------+--------+
| Dest MAC | Source MAC |
+--------+--------+--------+--------+
| Source MAC |
+--------+--------+--------+--------+
| VLAN Ethertype | VLAN Tag |
| (Optional) |
+--------+--------+--------+--------+
| OAM | OAM | Version|
| EtherType | Level | |
+--------+--------+--------+--------+
| Rsvd | OpCode | Data |
+--------+--------+--------+--------+
|Data (OpCode specific, continued)… |
+--------+--------+--------+--------+
Pretty simple op-code functions
(1/2) Connectivity Test Request/Response (layer two ping…)
(3) Connectivity Verification (periodic hello…)
Solicited and unsolicited connectivity checking

## Slide 16: A Security Wrinkle
Ethernet has the unfortunate property that packets may be sent to places they don’t need to go (e.g. MAC address is not known)
With OAM for a service provider environment,
  OAM must not “leak” out of the provider to other providers or the customer
  Customers and other providers must not be able to interfere with the carrier’s OAM
To deal with this, multi-hop OAM must filter OAM at the edges of the domain

## Slide 17: A Security Wrinkle
Bridge
Bridge
Bridge
Bridge
Provider A
OAM Barrier
OAM is required to create an OAM Barrier
No OAM in from the outside
No OAM out from the inside
Protects carrier OAM from interference and leaking
An OAM domain is defined to create this barrier

## Slide 18: A Security Wrinkle
Hierarchical Domains
1-octet domain level in OAM frame used to implement domains
Outermost customer-customer domain => 255 (0xFF)
Other domains hierarchically included
  A inside B implies
    Domain A Level <= Domain B Level
Level=255
L=200
L=195
L=64

## Slide 19: A Security Wrinkle
Hierarchical Domains
Requires port filtering by OAM EtherType and Domain Level
At edges of domain L
If (EtherType = OAM EtherType) and (Domain Level <= L)
DROP OAM PACKETS – can’t inject or leak
Level=255
L=200
L=195
L=64

## Slide 20: A Security Wrinkle
Hierarchical Domains
Requires filter by OAM EtherType and Domain Level
We realize this isn’t great, but
Hard requirement for multi-level domains with hard boundaries (e.g. no leaks)
Hard requirement for OAM in same path as data (e.g. no popping to CPU)
Hard requirement for working over switched networks (e.g. replication)
Although not ideal, seems like the best way to meet requirements
Level=255
L=200
L=195
L=64

## Slide 21: Why Am I Here?
MEF stuff underway, doesn’t want to wait for 802.1 OAM work for simple connectivity checking
  Too many people want something now
Mucho interest in MEF to be “compatible” with what .1 comes up with
  Everyone hates the idea of incompatible protocols or required replacements
So what can we do???

## Slide 22: Why Am I Here?
Easy parts
  Defining MEF protocols with configurable “well-known” MAC address info and configurable “well-known” EtherType
    Allows migration to IEEE defined addressing via config
  Other parameters also configurable
    Timeouts, delays, etc.
  Putting “as little as possible” in fixed headers
    Best chance at compatibility is to require little
      Version, domain level, op-code are only common fields
      Everything else op-code specific
    If one-octet op-code ok, if one-octet version number ok, leaves only the domain level

## Slide 23: Why Am I Here?
Hard part
  IF 802.1 accepts
    Same domain methods as MEF
  THEN
    Same frame format could be used and “compatibility” provided via new op-codes for additional function
  IF 802.1 accepts
    Same connectivity tests/verification as MEF
  THEN
    Same op-codes for connectivity test and verification could be used for both
Lots of people in MEF interested in seeing if we can work something out.

## Slide 24: Summary
MEF OAM Protocol work well underway
  Won’t wait
Defining “ping” and “hello”
  Connectivity test and verification (solicited and unsolicited ping)
  Not getting into fault isolation, just detection
Based on hierarchical domain model
  Requirement from carriers
Would be great if could “quickly” get consensus on fixed header aspects so MEF work could be designed as “compatible” (subset, phase 1, version 1, whatever) of larger 801.2 project