## Slide 1: Ethernet Connectivity Fault Management for Broadband
Yves Hertoghs, Wojciech Dec,
yves@cisco.com, wdec@cisco.com

## Slide 2: Ethernet OAM
IEEE 802.1ag, IEEE 802.3ah, MEF E-LMI, ITU-T
  Lots of stuff happening with regards to Operation & Management of Service Provider Ethernet Services
802.3ah; link level OAM
ELMI: at the UNI
802.1ag: service level OAM (per S-VLAN)
  Aka Connectivity Fault Management (CFM)
  This document focuses on using 802.1ag as a cornerstone for an Ethernet OAM scheme for DSL aggregation.
  It also introduces concepts to allow interworking of CFM with link level OAM schemes such as 802.3ah and ATM OAM

## Slide 3: A Generic Model
Maintenance End Point
Maintenance Intermediate Point
RG = Residential Gateway
BBNG = Broadband Network Gateway aka Router
RG
Access_Node
Aggr_Switch
Aggr_Switch
BBNG
Problems with this model:
  RG might not have MAC-address
  RG might only be able to run ‘legacy’ link level OAM schemes (802.3ah, ATM)
  CCMs from RG are potential DoS targets
  Would generate a lot of CCMs
CCM

## Slide 4: IEEE 802.1ag – Connectivity Fault Management
CCM: Connectivity Check Message
MEP: Maintenance End Point. A CFM station that can initiate and listen to CFM messages
MIP: Maintenance Intermediate Point. A CFM station that listens to CFM messages (might be allowed to send AIS).

## Slide 5: Ethernet OAM – 802.1ag
Continuity Check Message /CCM ( Auto and On-demand)
  Multicast from MEP. Received by MEPs and MIPs. Catalogued by receiving MEPs.
Traceroute Message and Reply (TM, TR)
  Next-hop Multicast from MEP to next MEP or MIP along route. Receiver both replies with unicast to original MEP, and sends Traceroute to next MEP/MIP.
Loopback Message and Reply (LM, LR)
  Unicast from MEP to MEP or MIP, which replies with unicast to originating MEP
Alarm Indication (AIS)
  Multicast from MEP or MIP when link in a certain inferior domain fails (is send in opposite direction)
CE
CE
Customer Domain
Provider Domain
Operator Domain
Operator Domain
Operator Domain
Eth Access
MPLS Core
MPLS Access
Customer
Customer
Service Provider
Network OAM
Service OAM
PW/MPLS OAM
MPLS Domain
MPLS Domain
Maintenance End Point
Maintenance Intermediate Point
0
3
5
7
Notes: Maintenance End Points (MEPs) are active elements of Ethernet CFM. They periodically transmit Continuity Check Messages and expect to periodically receive similar messages from other MEPs within a Domain. They also transmit Traceroute and Loopback Messages at the request of the Administrator. MEPs are responsible for confining CFM Messages within the bounds of a Maintenance Domain. (More details on CFM Message types in Section 2.3).
Maintenance Intermediate Points (MIPs) are passive elements of Ethernet CFM. They catalogue information received from Maintenance End Points (and other Maintenance Intermediate Points), and only respond to particular CFM messages (Traceroute and Loopback). Maintenance Intermediate Points forward CFM messages within a Maintenance Domain.
Transparent Points are passive Maintenance Points too. The difference between them and Maintenance Intermediate Points is that the former do not catalogue information from CFM messages, but merely forward them within a Domain
Continuity Check
These are “heart-beat” messages exchanged periodically between Maintenance End Points. They allow Maintenance End Points to discover other Maintenance End Points within a Domain, and allow Maintenance Intermediate Points to discover Maintenance End Points.
  Multicast from MP. Received by MPs and LPs. Catalogued by receiving MPs.
Traceroute
: These are transmitted by a Maintenance End Point on the request of the Administrator to track the path (hop-by-hop) to a destination Maintenance End Point. They allow the transmitting node to discover vital connectivity data about the path. It is similar in concept to UDP Traceroute
  Next-hop Multicast from MP to next MP or LP along route. Receiver both replies with unicast to original MP, and sends Traceroute to next MP/LP.
Loopback (Ping)
  These are transmitted by a Maintenance End Point on the request of the Administrator to verify connectivity to a particular Maintenance Point. Loopback indicates whether the destination is reachable or not - it does not allow hop-by-hop discovery of the path. It is similar in concept to ICMP Echo (Ping).
  Unicast from MP to LP or MP, which replies with unicast to originating MP.

## Slide 6: CFM Terminology
“Bridge-Brain” Model: All OAM messages are responded by the ‘brain’ of the bridge. The bridge has no ability to understand where an OAM frame entered the switch. Uses a single MAC-address for all MEP/MIPs, using different MEPids. *
“Bridge-Port” Model: OAM messages can be responded by using dedicated per port hardware/software. Requires a unique MAC-address per MEP/MIP. The bridge knows where an OAM frame entered the switch.
Domain: Boundaries of CFM management
Level: Access control structure for CFM Domain information & state. higher numbers (towards physical level) are bounded by lower numbers (towards service level)

## Slide 7: Changes to 802.1ag
802.1ag LM are towards MAC-addresses
Makes sense to summarize all MEPs on an access node under a single MAC-address
  Most Access Nodes would use brain model
  Interworking would mean brain model almost by defintion.
MEPs can be made unique by MEPid (13 bit integer) and MAID
  It is assumed that multiple MA’s can be created per S-VLAN if needed.
Loopback Messages can not target a MEPid
New Message (Inquiry/Status) must be added to CFM
  Allows a MEP to query a remote bridge about the status of a Port or MEP (by targetting MEPid).
  Remote Bridge will respond after performing local test of the Port/MEP
  Typically send by the BBNG
CCMs would need to be (optionally) turned off for mass rollout of broadband services

## Slide 8: CFM terminology
Inward MEP: MEP on a bridge port which is responding to messages originated at other side of relay function
Outward MEP: MEP on a bridge port which is responding to messages originated at same side of relay function
MEP Interior Facing Function (IFF): main function of the MEP i.e. this the function that sends CCs, maintains a DB, sends and replies to LBs and TRs.
MEP Exterior Facing Function (EFF): function that can send signals in the ‘opposite’ direction of the MEP i.e. for AIS.
MEP Virtual Interior Facing Function (VIFF): MEP that maintains a DB not by relying on CCs, but rather on physical level or ‘link-level OAM’ such as MPLS OAM, ATM OAM, 802.3ah OAM).

## Slide 9: Conceptual Model of an Optimised Solution
DSL Port has 1 outward MEP, MIP and inward MEP stacked
MEP at level 7 on Access Node port sees signals through it’s VIFF
MEP on RG at level 7 (and level 0) are ‘virtual’ MEPs i.e. logically on RG, physically a software construct on access node
EFF on outward MEP at level 7 in AN can send AIS, which will bubble up level 0 to reach BBNG
CC’s can also be sent from inward MEP at level 5 in AN to signal health of DSL line (removing the need for this ‘virtual MEPs’. See next slide)
ATM signals (AIS, CC) could be translated to appropriate CFM signals.
We still need a new opcode to check the DSL line, as all MEPs (inward /outward, any level), are probably operated by the same ‘bridge-brain’.
RG
Access_Node
Aggr_Switch
Aggr_Switch
BBNG
Level 0
Level 3
Level 7
(link)
DSL Domain
Ethernet Domain
Virtual

## Slide 10: Implementation of the model without ‘virtual MEPs’
MEP on access node is inward facing (level 3)
State of the MEP is dependent on underlying ATM/802.3ah/physical health’.
Could use LifeTime=0 TLV or Port State TLV in CC’s, or just stop sending CC’s if something went wrong with DSL Line.
No way to translate any ATM signals to CFM signals.
Can AIS be used if CCs are turned off ?
We still need a new opcode to check the DSL line, ‘bridge-brain’ model is assumed.
RG
Access_Node
Aggr_Switch
Aggr_Switch
BBNG
Level 3
DSL Domain
Ethernet Domain

## Slide 11: Line Identification
MEPid is a 13-bit integer value
Allows 8k MEPs per S-VLAN
  *might* not be enough for broadband, unless we could have different, side by side maintenance associations per S-VLAN
Broadband usually uses ‘circuit-id’ as a way of identifying DSL line, next to S-VLAN/C-VLAN (if a VLAN per dsl line is used).
You could think of the circuit-id as the MEP Name
Not easy way to link MEP Name id to MEP id and MEP MAC-address (for sure when CC’s are turned off)

## Slide 12: MEP Name
Should IFF definition be extended to include MEP Name TLV ?
MEP Name TLV could take format from RFC3046 (DHCP Option82)
  DSL Forum is developing a global circuit-id syntax using RFC3046
MEP Name TLV (19.3.11.3.2) is already defined and compatible with RFC3046 notation
MEP Name can be part of CCMs
If CCMs are turned off, we still need a protocol to translate MEP Name to MEP id + MEP MAC-address
Introducing the Maintenance Point Resolution Protocol

## Slide 13: MP Resolution Query Message (MRQM)
MRQMs purpose is to query within the S-VLAN and MA level all MEPs about who is carrying a given MEP Name
MEP Name, MAID are carried as TLVs in a multicast message with a new opcode targetted at the MA level
MEPs who do not recognise this opcode must behave according to the specified 802.1ag behaviour when not recognising opcodes
MEPs not finding a local match silently drop the message and take no further action
Queries that time out will generate a ‘MEP NAME Unresolved-Message’ to be communicated to the administrator

## Slide 14: MP Resolution Response Message (MRRM)
Upon receiving a MRQM and recognising the MEP Name, a MEP will reply with a MRRM message
New Opcode needed, unicast message back to originating MEP containing MEP Name, MEP ID , MAID, MEP Mac-address TLVs
Upon receiving the MRRM a MEP can update it’s local database
  Both MRRM and CCMs can populate the database
If multiple responses are received, the MEP should print a ‘MEP Name inconsistency error’ and report to the administrator
No unsollicited MRRMs are allowed

## Slide 15: Summary
802.1ag can be used as a cornerstone for broadband access networks
802.1ag needs to be enhanced
  Ability to turn off CCMs
  Extra Opcodes (Inquiry/Status) to accommodate bridge brain models
  Clear interworking scenarios
    E-LMI, 802.3ah, ATM
    Either through ‘virtual’ MEP or through binding dsl line health to MEP Port State
  Need MEP name resolving protocol
    MEP Name to MEP id + MAC-address

## Slide 16
<number>
<number>
<number>
© 2004, Cisco Systems, Inc. All rights reserved.